## Slide 1
COURSE SLIDES · WSQ
CompTIA Certified Network+ Training (N10-009)
WSQ Course Code: TGS-2025054472
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version v2.0 · 19 August 2026
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
?
Your Trainer
General Trainer template — to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr. Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
EXPERTISE
Networking, cybersecurity, cloud infrastructure, data science and AI — 20+ years of training and consulting.
DELIVERS
WSQ courses on CompTIA Network+, Security+, Linux+, cloud computing and applied AI.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name, organisation and role.
• Your experience with networking, Linux or IT support (if any).
• What network you manage or plan to build after this course.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is too small.
3
Mutual respect: agree to disagree.
4
One conversation at a time.
5
Be punctual; return from breaks on time.
6
75% attendance is required.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
LMS / TMS · lms-tms.tertiaryinfotech.com
Download Your Course Material
1
1 · Go to the LMS portal
Open https://lms-tms.tertiaryinfotech.com in your browser.
2
2 · Log in
Sign in with the account e-mail you used to register for this course.
3
3 · Open this course
Select 'CompTIA Certified Network+ Training' in My Courses.
4
4 · Download
Download the Learner Slides, Learner Guide and Lesson Plan (PDF).
5
5 · Get the labs
Open the lab repository on GitHub — the link is on the course page.
6
6 · Keep them open
You may use these materials during the open-book assessment.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 9
SCHEDULE · 9:30 AM – 6:30 PM DAILY
Lesson Plan — 5 Days · 8 Hours a Day
1
Day 1 · Networking Concepts
OSI model, appliances, cloud, ports & protocols, media, topologies, IPv4/IPv6 · Labs 1–7.
2
Day 2 · Network Implementation
Routing, NAT/PAT, VLANs & trunking, STP, link aggregation, wireless, installations · Labs 8–14.
3
Day 3 · Network Operations
Documentation, change & configuration management, monitoring, DR, network services · Labs 15–20.
4
Day 4 · Network Security
Encryption & PKI, IAM/AAA, segmentation, attacks and defence features · Labs 21–27.
5
Day 5 · Network Troubleshooting & Assessment
Seven-step methodology, layer-by-layer diagnosis, performance · Labs 28–36 · Final Assessment (WA + PP).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 · Explain networking concepts
OSI model, appliances, cloud, ports & protocols, traffic types, media, topologies and IP addressing.
2
LO2 · Implement networks
Routing (BGP/EIGRP/OSPF), NAT/PAT, VLANs, STP, link aggregation, wireless and installations.
3
LO3 · Operate networks
Documentation, IPAM, change management, SNMP/flow/log monitoring, DR and network services.
4
LO4 · Secure networks
Encryption, PKI, IAM, AAA, segmentation, attack recognition and defence features.
5
LO5 · Troubleshoot networks
The CompTIA methodology applied with the right tool at every layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
FIVE DOMAINS · 36 HANDS-ON LABS
Course Outline — the Five N10-009 Domains
1
Domain 1.0 · Networking Concepts · 23%
OSI, appliances, cloud, ports & protocols, traffic, media, topologies, IPv4 · Labs 1–7.
2
Domain 2.0 · Network Implementation · 20%
Routing, switching, wireless and physical installations · Labs 8–14.
3
Domain 3.0 · Network Operations · 19%
Documentation, life-cycle, change, monitoring, DR, services, access · Labs 15–20.
4
Domain 4.0 · Network Security · 14%
Logical/physical security, attacks, segmentation and defence · Labs 21–27.
5
Domain 5.0 · Network Troubleshooting · 24%
Methodology, cabling, services, performance, tools · Labs 28–36.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
KNOW THE BLUEPRINT
N10-009 Exam Weighting by Domain
Chart: 
| Networking Concepts | Network Implementation | Network Operations | Network Security | Network Troubleshooting
Exam weighting (%) | 23 | 20 | 19 | 14 | 24
WHAT THE DATA SHOWS
Troubleshooting (24%) and Networking Concepts (23%) carry almost half the exam — the course spends Day 1 and Day 5 on them and every lab ends with a verify step.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
THE CERTIFICATION TARGET
About the CompTIA Network+ Exam (N10-009)
1
Format
Maximum of 90 questions — multiple-choice and performance-based — in 90 minutes.
2
Passing score
720 on a 100–900 scale. Book at Pearson VUE test centres or online proctoring.
3
No prerequisites
CompTIA recommends A+ and 9–12 months of networking experience, but neither is required.
4
Renewal
The certification is valid for 3 years and renews through CompTIA CE credits.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
FREE TOOLS USED THROUGHOUT
Your Lab Environment
1
Killercoda Ubuntu Playground
A free, throwaway Ubuntu VM in your browser — every Linux lab runs here. https://killercoda.com/playgrounds/scenario/ubuntu
2
TIS IP Calculator
Web subnetting tool for CIDR/VLSM planning and verification. https://alfredang.github.io/ipcalculator/
3
TIS PCAP Analyzer
Upload and dissect packet captures layer by layer in the browser. https://alfredang.github.io/pcapanalyzer/
4
TIS Cybersecurity Simulator
Practise recognising network attacks in a safe simulated environment. https://alfredang.github.io/cybersecuritysimulator/
5
TIS Regex Generator
Build the regular expressions used to search and filter log files. https://alfredang.github.io/regexgenerator/
6
No installs needed
Everything is browser-based; packages are pulled with apt inside the playground VM.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
BEFORE YOU START
Briefing for Assessment
1
Do · Clear your desk
Place phones and other materials under the table or on the floor.
2
Don't · No recording
No photos or recording of assessment scripts.
3
Don't · No discussion
Work individually — no discussion during the assessment.
4
Do · Black or blue pen
Use a black or blue pen for hard-copy assessments.
5
Don't · No correction fluid
No liquid paper or correction tape may be used.
6
Do · Stop on time
Scripts are collected when time is up.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
FINAL ASSESSMENT · DAY 5
Assessment
1
Written Assessment (WA)
Short-Answer Questions (SAQ) · 1 hour · open book. Tests the underpinning networking knowledge.
2
Practical Performance (PP)
Hands-on networking tasks · 90 minutes · open book. Tests the ability you built in the 36 labs.
3
Open book
You may use the course slides, the Learner Guide and approved materials only.
4
Eligibility
A minimum of 75% attendance is required to be eligible for assessment and funding.
5
Result
You are assessed as Competent (C) or Not Yet Competent (NYC) on each instrument.
6
Appeals
An appeal process is available if you wish to contest an assessment outcome.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR on the LMS
2
Digital attendance
Scan the SSG QR
3
Sit WA then PP
Open book · 60 + 90 min
4
Submit on the LMS
Upload your answers
5
Sign the record
Assessment Summary
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
WSQ FUNDING
Criteria for Funding
1
Attendance
A minimum attendance rate of 75%, based on the SSG Digital Attendance record.
2
Assessment
Complete both assessment components and be assessed as 'Competent'.
3
Digital attendance
Scan the SSG QR code for AM, PM and Assessment on every training day.
4
TRAQOM survey
Complete the mandatory TRAQOM course feedback survey on the LMS.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
DOMAIN 1.0 · 23% OF THE EXAM
Networking Concepts
OSI model · appliances · cloud · ports & protocols · traffic types · media · transceivers & connectors · topologies · IPv4 addressing
1.0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
WHAT YOU'LL DO
Hands-On Labs — Networking Concepts
Labs 1–3
• OSI Model Packet Inspection
• IPv4 Subnetting and CIDR
• IPv6 Addressing and Link-Local
Labs 4–6
• Common Ports and Protocols
• DNS Record Types
• DHCP Lease Capture (DORA)
Lab 7
• Simulating a Cloud VPC with Namespaces
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
DOMAIN 1 · 23% OF THE EXAM
Domain 1 — Networking Concepts.
Seven layers, addressing, ports, media, topologies and cloud — 23% of the N10-009 exam and the foundation every other domain builds on.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
EXAM BLUEPRINT
N10-009 Exam Domain Weights
Chart: 
| 1 Concepts | 2 Implementation | 3 Operations | 4 Security | 5 Troubleshooting
Weight % | 23 | 20 | 19 | 14 | 24
WHAT THE DATA SHOWS
Concepts and Troubleshooting together are nearly half the exam — and troubleshooting questions lean on the concepts you learn here.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
OBJ 1.1 · OSI MODEL
Why We Model Networks
1
Models simplify
A model is a basic representation that makes a complex system explainable one piece at a time.
2
Frames
Devices exchange data in discrete chunks called frames, built and destroyed inside the NIC.
3
1,500 bytes
The default Ethernet payload limit (MTU); jumbo frames stretch to 9,000 bytes.
4
OSI vs TCP/IP
OSI is the 7-layer teaching and troubleshooting model; TCP/IP is the 4-layer practical stack.
5
PDU
Protocol Data Unit — the name of the data chunk changes at each layer as headers are added.
6
Exam anchor
N10-009 expects you to place any protocol, device or symptom at its correct layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
OBJ 1.1 · OSI MODEL
The Seven Layers
1
L7 — Application
Protocols the software speaks: HTTP, FTP, SMTP, DNS. Where data is produced and consumed.
2
L6 — Presentation
Formats and translates data: encryption (TLS), compression, character encoding.
3
L5 — Session
Opens, manages and tears down dialogs between hosts; think RPC and API sessions.
4
L4 — Transport
End-to-end delivery: TCP (reliable) and UDP (best-effort), addressed by port numbers.
5
L3 — Network
Logical addressing and routing between networks: IP and ICMP. Routers live here.
6
L2 — Data Link
Frames and MAC addresses on the local link; switches forward here, FCS detects errors.
7
L1 — Physical
Bits on the wire or in the air: cables, connectors, transceivers, hubs, radio.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
OBJ 1.1 · OSI MODEL
PDUs and Devices by Layer
Layer(s)
PDU
Typical devices / protocols
L5-L7 upper layers
Data
HTTP, TLS, DNS, proxies
L4 Transport
Segment / datagram
TCP, UDP, load balancer
L3 Network
Packet
IP, ICMP, router, L3 switch
L2 Data Link
Frame
Ethernet, switch, NIC, AP
L1 Physical
Bits
Cables, hubs, transceivers
WHEN IT MATTERS Exam shortcut: name the PDU and you have named the layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
OBJ 1.1 · OSI MODEL
Encapsulation: Data Down the Stack
1
Data
app payload
2
Segment
TCP/UDP header
3
Packet
IP header added
4
Frame
MAC header + FCS
5
Bits
onto the medium
WHY IT MATTERS
Every capture you will read shows these headers nested in exactly this order — and decapsulation reverses the sequence at the receiver.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
OBJ 1.1 · OSI MODEL
OSI vs TCP/IP Model
OSI (7 layers)
TCP/IP (4 layers)
• 7-6-5: Application, Presentation, Session
• 4: Transport — segments, ports
• 3: Network — packets, routing
• 2-1: Data Link and Physical
• Application — HTTP, DNS, SMTP, TLS
• Transport — TCP and UDP
• Internet — IP, ICMP, IGMP
• Network Access — Ethernet, Wi-Fi, media
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
OBJ 1.1 · OSI MODEL
Upper Layers in Practice
1
Session (L5)
Establishes and resumes conversations — RPC calls, NetBIOS sessions, SQL connections.
2
Presentation (L6)
TLS encryption, JPEG/PNG encoding, ASCII vs Unicode — data made readable and safe.
3
Application (L7)
The protocol carrying user intent: a GET request, a mail submission, a DNS query.
4
Why it blurs
Real stacks fold L5-L7 together — TLS spans layers — but the exam still tests the clean split.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
OBJ 1.1 · OSI MODEL
The MAC Address
1
48-bit physical address
Burned into every NIC: first 24 bits are the vendor OUI, last 24 the unique device ID.
2
Hex notation
Example 00:16:3e:4a:99:d1 — view yours with ip link (Linux) or ipconfig /all (Windows).
3
Destination + source
Every frame carries both; a NIC normally processes only frames addressed to it.
4
FF-FF-FF-FF-FF-FF
The broadcast MAC — every NIC in the broadcast domain must process the frame.
5
Duplicate MACs
Rare but real — cloned VMs are a classic source of duplicate-MAC connectivity faults.
6
Physical vs logical
MAC = physical address (L2); IP = logical address (L3). ARP glues them together.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
OBJ 1.1 · OSI MODEL
Anatomy of an Ethernet Frame
1
Preamble
7 bytes of alternating bits plus a start delimiter — lets receivers sync their clocks.
2
Destination + source MAC
6 bytes each — switches forward on the destination, learn from the source.
3
EtherType
Declares the payload protocol: 0x0800 IPv4, 0x86DD IPv6, 0x0806 ARP.
4
Payload
46-1,500 bytes of upper-layer data; padded if too short.
5
FCS
4-byte CRC checksum — corrupt frames are silently dropped, upper layers must recover.
6
Size range
64 to 1,522 bytes standard; jumbo frames up to 9,000 for storage and DC traffic.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
OBJ 1.4 · TRAFFIC TYPES
Traffic Types
1
Unicast
One sender to one receiver — the vast majority of traffic, e.g. your HTTP session.
2
Broadcast
One to all in the broadcast domain (FF-FF... / 255.255.255.255). IPv6 abolishes it.
3
Multicast
One to a subscribed group — IPv4 224.0.0.0/4, IPv6 ff00::/8; membership managed by IGMP.
4
Anycast
One address advertised from many places; routing delivers to the nearest — how 8.8.8.8 scales.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
OBJ 1.1 · OSI MODEL
Reading a Capture Layer by Layer
One tcpdump line contains headers from three layers — the payload adds the fourth.
# tcpdump -i eth0 -nn -v -c 5 'tcp port 80'
IP 10.244.0.5.55512 > 93.184.216.34.80:
Flags [S], seq 1287312, win 64240
# add -e for the link-layer (L2) header:
00:16:3e:4a:99:d1 > 52:54:00:12:35:02
# add -A for the ASCII payload (L7):
GET / HTTP/1.1
Host: example.com
L2 Data Link
MAC-to-MAC delivery on the local link — visible only with the -e flag.
L3 Network
Source and destination IP addresses route the packet between networks.
L4 Transport
Ports 55512 > 80 plus the SYN flag — a TCP connection being opened.
L7 Application
The HTTP GET request itself — the data everything else exists to carry.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
OBJ 1.1 · OSI MODEL
From URL to Wire
1
Browser builds an HTTP GET (L7)
▶
2
TCP adds ports + starts handshake (L4)
▶
3
IP adds source/destination address (L3)
▶
4
NIC frames it with MACs + FCS (L2)
▶
5
Bits transmitted on the medium (L1)
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
OBJ 1.1 · OSI MODEL
Troubleshooting by Layer
1
L1 first
Link lights, cables, transceivers, Wi-Fi signal — most 'network down' calls end here.
2
L2 next
Check MAC learning, VLAN membership, ARP entries; switches misbehave at this layer.
3
L3 routing
ping and traceroute test addressing and routes — wrong gateway or mask lives here.
4
L4 ports
Service unreachable but host pings? Check listening ports and firewall rules.
5
L7 last
DNS answers, certificates, application errors — the top of the bottom-up method.
6
Name the layer
Exam questions describe a symptom and expect the layer — practise the mapping now.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
DOMAIN 1.0 · HANDS-ON
OSI Model Packet Inspection
LAB 1
Capture live traffic and map each protocol header to its OSI layer.
Capture HTTP traffic with tcpdump on a Killercoda Ubuntu host, generate requests with curl, and match the MAC, IP, TCP and HTTP headers you see to OSI layers 2, 3, 4 and 7.
YOU'LL BUILD
A live capture and a saved .pcap where you can point at every header and name its OSI layer.
TOOLCHAIN
tcpdump, curl, Killercoda Ubuntu, TIS PCAP Analyzer (alfredang.github.io/pcapanalyzer)
DONE WHEN
tcpdump shows SYN/ACK/GET packets and you can name the OSI layer of every header; the TIS PCAP Analyzer decodes the same layers from the downloaded osi-lab.pcap.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
LAB 1 · PROCESS MAP
How Lab 1 Runs
1
Install the capture tools
apt · step 1
2
Start a background capture of five
tcpdump · step 3
3
Map each header
Step 5 of 8
4
Re-run with -e -A to expose L2 MACs
tcpdump · step 6
5
Stop any background captures
kill · step 8
THE POINT
Capture live traffic and map each protocol header to its OSI layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
LAB 1 · VERIFY
OSI Model Packet Inspection
✅ Expected result
tcpdump shows SYN/ACK/GET packets and you can name the OSI layer of every header; the TIS PCAP Analyzer decodes the same layers from the downloaded osi-lab.pcap.
IF IT DOESN'T WORK
No packets captured
Check the interface with ip -brief addr — capture on the interface marked UP, not lo.
curl hangs or fails
The playground may block port 80 — try curl -s http://neverssl.com instead.
tcpdump: command not found
Re-run apt update && apt install -y tcpdump curl — the install step may have failed.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
OBJ 1.2 · APPLIANCES
Core Networking Appliances
1
Router
Connects networks and forwards packets by IP; every LAN's default gateway is a router interface.
2
Switch
Forwards frames by MAC using its learned MAC table; each port is its own collision domain.
3
Layer 3 switch
Switches inside VLANs and routes between them in hardware at wire speed.
4
Hub (legacy)
A multiport repeater — one shared collision domain using CSMA/CD; replaced by switches.
5
Access point
Bridges 802.11 wireless clients onto the wired LAN at Layer 2.
6
Wireless controller
Centrally manages fleets of APs: channels, power, roaming and policy.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
OBJ 1.2 · APPLIANCES
Which Layer Does Each Device Read?
Device
Layer
Forwards / filters on
Hub / repeater
L1
Electrical signal only
Switch, bridge, AP
L2
MAC addresses
Router, L3 switch
L3
IP addresses and routes
Load balancer
L4-L7
Ports, sessions, URLs
Firewall / IPS
L3-L7
Rules, state, signatures
WHEN IT MATTERS A device's layer tells you what information it can see — and what it can never see.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
OBJ 1.2 · APPLIANCES
Security and Application Appliances
1
Firewall
Filters traffic between zones by rule: addresses, ports, and connection state.
2
IDS
Passively inspects mirrored traffic and raises alerts on signatures or anomalies.
3
IPS
Sits inline in the traffic path and actively blocks malicious traffic in real time.
4
Load balancer
Distributes client sessions across a server pool and health-checks every member.
5
Forward proxy
Fetches web content on behalf of internal clients — filtering, caching, logging.
6
Reverse proxy
Fronts your servers: TLS offload, caching, and shielding the origin from the Internet.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
OBJ 1.2 · APPLIANCES
IDS or IPS?
Must bad traffic be blocked automatically?
YES — deploy an IPS
Place it inline so it can drop packets in real time — and accept that a false positive can block legitimate traffic.
NO — deploy an IDS
Feed it a mirror/SPAN copy. It only alerts, so it can never break the network — but a human must act on the alert.
Many NGFW platforms bundle both modes — the inline-vs-passive placement decision still applies.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
OBJ 1.2 · APPLIANCES
Forward vs Reverse Proxy
Forward proxy (protects clients)
Reverse proxy (protects servers)
• Sits between your users and the Internet
• Enforces acceptable-use and URL filtering
• Caches popular content to save bandwidth
• Hides internal client identities
• Sits between the Internet and your servers
• Terminates TLS and offloads encryption
• Load-balances and caches for the backend
• Hides and shields the origin servers
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
OBJ 1.2 · APPLIANCES
NAS vs SAN
Attribute
NAS
SAN
Access level
File (SMB, NFS)
Block (raw volumes)
Network
Standard Ethernet LAN
Fibre Channel or iSCSI
Appears as
Shared folders
Local disks to the OS
Hardware
NAS appliance
HBAs, FC switches, arrays
Typical use
Team file shares
Databases, VM datastores
WHEN IT MATTERS FCoE carries Fibre Channel over Ethernet; multipathing keeps SAN storage reachable through failures.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
OBJ 1.2 · APPLIANCES
Physical vs Virtual Appliances
Physical appliance
Virtual appliance (NFV)
• Dedicated hardware, predictable throughput
• ASICs accelerate switching and crypto
• Scaling means buying and racking boxes
• Failure domain is the chassis
• Router, firewall, LB run as VMs/containers
• Deployed in minutes from an image
• Scales out on shared compute
• Portable across data center and cloud
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
OBJ 1.5 · MEDIA
Copper: Coaxial and Twinaxial
1
Coaxial
A single center conductor inside a shield — highly resistant to EMI; used for cable broadband.
2
RG-6
75-ohm coax for cable TV and DOCSIS internet; terminated with threaded F-type connectors.
3
BNC
Bayonet-twist coax connector found on older gear and lab equipment.
4
Twinax / DAC
Twin conductors; direct-attach copper links switches over short 10-100G runs, cheaper than optics.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
OBJ 1.5 · MEDIA
Twisted Pair Essentials
1
Four twisted pairs
The twists cancel EMI and crosstalk between pairs — tighter twists, higher category.
2
UTP vs STP
Unshielded is the default; shielded adds foil/braid for electrically noisy environments.
3
100 m channel limit
The maximum twisted-pair run: 90 m horizontal plus 10 m of patch cords.
4
RJ45 (8P8C)
The standard data connector; RJ11 is the smaller 2-3 pair telephone jack.
5
T568A / T568B
The two pin-out standards — use one consistently; mixing them creates a crossover.
6
Solid vs stranded
Solid core for in-wall horizontal runs; stranded for flexible patch cables.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
OBJ 1.5 · MEDIA
Twisted-Pair Categories
Category
Max speed
Bandwidth
Notes
Cat 5e
1 Gbps
100 MHz
Minimum for gigabit
Cat 6
1 G (10 G to 55 m)
250 MHz
Internal separator
Cat 6a
10 Gbps to 100 m
500 MHz
New-build standard
Cat 7
10 Gbps
600 MHz
Shielded, GG45/TERA
Cat 8
25/40 Gbps to 30 m
2,000 MHz
Data center ToR runs
WHEN IT MATTERS Every link component — cable, jacks, patch panel — must meet the category or the link downgrades.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
OBJ 1.5 · MEDIA
Fiber: Single-Mode vs Multimode
Single-mode (SMF)
Multimode (MMF)
• Laser source, 8-10 micron core
• Runs of tens of kilometers
• Yellow jacket by convention
• WAN, metro and carrier links
• LED/VCSEL source, 50 or 62.5 micron core
• Hundreds of meters (OM3/OM4/OM5)
• Aqua or orange jacket
• Inside buildings and data centers
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
OBJ 1.5 · MEDIA
Ethernet Standards to Recognise
Standard
Speed
Medium
Distance
100BASE-TX
100 Mbps
Cat 5 UTP
100 m
1000BASE-T
1 Gbps
Cat 5e UTP
100 m
10GBASE-T
10 Gbps
Cat 6a UTP
100 m
1000BASE-SX
1 Gbps
Multimode fiber
~550 m
1000BASE-LX
1 Gbps
Single-mode fiber
5-10 km
10GBASE-SR / LR
10 Gbps
MMF / SMF
400 m / 10 km
WHEN IT MATTERS Read the name: speed, BASE (baseband), then media hint — T twisted pair, S short fiber, L long fiber.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
OBJ 1.5 · ETHERNET
Hubs, Switches and Domains
1
CSMA/CD
Hub-era rule: listen before sending, detect collisions, back off and retry.
2
Collision domain
Where frames can collide — an entire hub, but only a single switch port.
3
Broadcast domain
How far a broadcast reaches — the whole LAN/VLAN, bounded only by routers.
4
MAC address table
Switches learn source MACs per port and forward frames only where needed.
5
Full duplex
Switched ports send and receive simultaneously — collisions disappear.
6
STP
Spanning Tree Protocol blocks redundant links so switching loops cannot melt the LAN.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
OBJ 1.5 · MEDIA
Cable Ratings and Fire Safety
1
Plenum (CMP)
Fire-retardant, low-smoke jacket — required in air-handling spaces above ceilings.
2
Riser (CMR)
Rated for vertical runs between floors — flame-resistant but not plenum-grade.
3
PVC / non-plenum
General patching only — burns readily and emits toxic smoke.
4
Check the box
Fire rating is printed on the manufacturer's box and cable jacket — inspectors will.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
OBJ 1.5 · STRUCTURED CABLING
Structured Cabling Spaces
1
MDF
Main distribution frame — the primary equipment room where the backbone terminates.
2
IDF
Intermediate frames per floor/zone, uplinked back to the MDF.
3
Demarc
Where the provider's responsibility ends and yours begins.
4
Horizontal run
Solid-core cable from the IDF patch panel to each work-area wall outlet.
5
Patch panel
110-punchdown terminations for runs; patch cables jump to switch ports.
6
Racks and U
Equipment racks are 19 inches wide; height is measured in 1.75-inch units (U).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
OBJ 1.5 · MEDIA
Testing and Locating Cable
1
Wiremap tester
Verifies each pin lands on the right pin — catches opens, shorts and split pairs.
2
TDR / OTDR
Time-domain reflectometers measure length and locate mid-cable breaks (optical for fiber).
3
Toner and probe
The 'fox and hound' — a tone generator plus probe finds one cable in a bundle.
4
Loopback plug
Tests a NIC's ability to send and receive to itself.
5
Crosstalk metrics
NEXT/FEXT measurements catch poor terminations that whisper between pairs.
6
Attenuation
Signal loss over distance — why category ratings carry a length limit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
OBJ 1.5 · WIRELESS
Wireless Media
1
802.11 Wi-Fi
Unlicensed 2.4/5/6 GHz radio LANs, defined by the IEEE 802.11 family.
2
Cellular
Carrier-licensed 4G/5G — WAN links for mobile users, IoT and branch backup.
3
Satellite
Coverage anywhere with sky view; GEO adds ~600 ms latency, LEO constellations far less.
4
The trade
Wireless wins on mobility and reach — traded against interference and shared airtime.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
OBJ 1.5 · TRANSCEIVERS
Transceiver Form Factors
Form factor
Speed
Notes
SFP
1 Gbps
Hot-swappable; fiber or RJ45
SFP+
10 Gbps
Same cage as SFP
QSFP
4 x 1 G / 40 G
Four lanes in one module
QSFP+ / QSFP28
40 G / 100 G
Spine and uplink ports
WHEN IT MATTERS Multi-source agreements (MSAs) keep modules interoperable across vendors — GBIC was the ancestor.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
OBJ 1.5 · CONNECTORS
Connectors to Recognise on Sight
1
LC
Small square duplex fiber connector — the default on SFP modules.
2
SC
Larger square push-pull fiber connector — 'stick and click'.
3
ST
Round bayonet-twist fiber connector on legacy multimode plants.
4
MPO / MTP
Multi-fiber ribbon connector feeding 40/100G parallel optics.
5
RJ45 and RJ11
8-pin Ethernet jack vs the smaller 4/6-pin telephone jack.
6
F-type and BNC
Threaded and bayonet coax connectors for broadband and lab gear.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
OBJ 1.6 · TOPOLOGIES
Network Topologies
1
Star / hub-and-spoke
All nodes home to a central device — today's standard LAN; the center is the failure point.
2
Full mesh
Every node links to every other: n(n-1)/2 links — maximum resilience, maximum cost.
3
Partial mesh / hybrid
Key sites meshed, others single-homed — the practical WAN compromise.
4
Point-to-point
One dedicated link between two endpoints — leased lines and wireless bridges.
5
Bus and ring (legacy)
Shared coax and token passing — obsolete, but the exam expects recognition.
6
Physical vs logical
The cabling layout and the data flow can differ — describe both when documenting.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
OBJ 1.6 · TOPOLOGIES
Choosing a Topology
Topology
Resilience
Cost
Best fit
Star
Low (center fails)
Low
Access LANs
Full mesh
Highest
Highest
Small WAN cores
Partial mesh
High
Medium
Regional WANs
Hub-and-spoke
Low
Low
Branch-to-HQ, SD-WAN
Point-to-point
Per-link
Low
Site interconnects
WHEN IT MATTERS Count the links before you promise resilience — every extra path is money and management.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
OBJ 1.6 · ARCHITECTURES
Three-Tier Architecture
1
Core
fast, resilient L3
2
Distribution
policy + routing
3
Access
user & server ports
WHY IT MATTERS
Each tier has one job: access connects hosts, distribution applies policy, core moves packets fast. Collapsed core merges the top two for smaller sites.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
OBJ 1.6 · ARCHITECTURES
Spine-and-Leaf vs Three-Tier
Three-tier (classic)
Spine-and-leaf (modern DC)
• Optimised for north-south client traffic
• Hosts can be several hops apart
• STP blocks redundant links
• Scale up: buy bigger core boxes
• Optimised for east-west server traffic
• Any leaf is two hops from any leaf
• All links active with ECMP routing
• Scale out: add spines and leaves
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
OBJ 1.6 · NETWORK TYPES
Traffic Flows and Network Types
1
North-south
Traffic entering or leaving the data center — client to server.
2
East-west
Server-to-server traffic inside the DC — dominant since virtualization and microservices.
3
LAN / WLAN
A single site's wired or wireless network.
4
WAN
Links sites across geography — the Internet is the biggest WAN of all.
5
CAN / MAN
Campus and metropolitan scale sit between LAN and WAN.
6
PAN
Personal-area links: Bluetooth, USB tethering, wearables.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
OBJ 1.6 · NETWORK TYPES
Special-Purpose Networks
1
IoT devices
Sensors, cameras, controllers — isolate on their own SSID/VLAN with ACLs; patch firmware.
2
VoIP / UC
Voice, video and chat over IP: SIP signalling on 5060/5061, RTP media streams.
3
ICS / SCADA
Industrial control: PLCs, HMIs and RTUs supervised over wide areas — segment strictly from IT.
4
Storage networks
NAS/SAN traffic often rides its own network for performance and isolation.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
OBJ 1.7 · IPv4 ADDRESSING
IP addressing is the most-rewarded skill on the exam.
Every router, firewall rule and cloud VPC starts with correct CIDR math — this section builds it from binary upward.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
OBJ 1.7 · IPv4 ADDRESSING
IPv4 Address Anatomy
1
32 bits, four octets
Dotted decimal such as 192.168.4.12 — each octet ranges 0-255.
2
Network + host portions
The subnet mask draws the boundary line between the two.
3
Binary underneath
192 is 11000000 — subnetting is just moving the 1s/0s boundary rightward.
4
Subnet mask
All 1s on the left, all 0s on the right — 255.255.255.0 is written /24 in CIDR.
5
Default gateway
The local router interface a host uses to reach remote networks.
6
Unique per network
Duplicate IPs break connectivity — usually a rogue static assignment.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
OBJ 1.7 · IPv4 ADDRESSING
Decimal to Binary, the Exam Way
Each octet is 8 bits with place values 128 64 32 16 8 4 2 1.
Place: 128 64 32 16 8 4 2 1
171 -> 128? yes (43 left) 64? no
32? yes (11 left) 16? no
8? yes (3 left) 4? no
2? yes 1? yes
171 = 1 0 1 0 1 0 1 1
224 = 11100000 95 = 01011111
255 = 11111111 0 = 00000000
Method
Subtract the largest place value that fits and write 1; write 0 where it does not fit.
Check
The place values you marked with 1 must sum back to the original number.
Why bother
Masks and CIDR boundaries only make sense at the bit level — this is the foundation.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
OBJ 1.7 · IPv4 ADDRESSING
Classful Addressing (Historical)
Class
First octet
Default mask
Purpose
A
1-126
/8 (255.0.0.0)
Huge networks
B
128-191
/16 (255.255.0.0)
Medium networks
C
192-223
/24 (255.255.255.0)
Small networks
D
224-239
n/a
Multicast
E
240-255
n/a
Experimental
WHEN IT MATTERS 127.x.x.x is reserved for loopback. CIDR replaced classes in 1993, but the exam still tests them.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
OBJ 1.7 · IPv4 ADDRESSING
RFC 1918 Private Ranges
CIDR block
Range
Addresses
Typical use
10.0.0.0/8
10.0.0.0 - 10.255.255.255
16.7 M
Enterprises, clouds
172.16.0.0/12
172.16.0.0 - 172.31.255.255
1 M
Mid-size nets, VPCs
192.168.0.0/16
192.168.0.0 - 192.168.255.255
65,536
Home and SOHO
WHEN IT MATTERS Private addresses never route on the Internet — NAT translates them at the edge.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
OBJ 1.7 · IPv4 ADDRESSING
Special IPv4 Addresses
1
127.0.0.1
IPv4 loopback — the host talking to itself; IPv6 uses ::1.
2
169.254.x.x (APIPA)
Self-assigned when DHCP fails — a client stuck here cannot reach its DHCP server.
3
Network address
Host bits all 0 — names the subnet itself; never assignable to a host.
4
Broadcast address
Host bits all 1 — reaches every host on the subnet.
5
0.0.0.0
The 'any' address — unconfigured source, or the default route 0.0.0.0/0.
6
Public addresses
Everything routable outside private/reserved space — allocated through RIRs.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
OBJ 1.7 · IPv4 ADDRESSING
How NAT Hides Private Addresses
1
Host 192.168.1.10 sends toward 8.8.8.8
▶
2
Edge router swaps source to its public IP
▶
3
Translation recorded in the NAT table
▶
4
Reply arrives at the public address
▶
5
Router maps it back to the private host
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
OBJ 1.7 · ARP
ARP: Gluing Layer 3 to Layer 2
1
The problem
A host knows the destination IP, but the frame it builds needs a destination MAC.
2
ARP request
Broadcast: 'Who has 192.168.1.1?' — every host in the broadcast domain hears it.
3
ARP reply
The owner answers unicast with its MAC; the mapping is cached for reuse.
4
arp -a / ip neigh
Inspect the cache — stale or poisoned entries cause 'unreachable' faults.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
OBJ 1.7 · IPv4 ADDRESSING
Local or Remote? The Mask Decides
1
AND your IP with the subnet mask
▶
2
AND the destination with the same mask
▶
3
Results equal? The destination is local
▶
4
Local: ARP for the destination's MAC
▶
5
Remote: ARP for the default gateway
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
OBJ 1.7 · SUBNETTING
CIDR: Splitting a /24 into /26s
Borrow 2 host bits: 2^2 = 4 subnets, 2^6 - 2 = 62 hosts each.
192.168.10.0/24 -> four /26 blocks of 64
Sub Network First Last Bcast
1 192.168.10.0 .1 .62 .63
2 192.168.10.64 .65 .126 .127
3 192.168.10.128 .129 .190 .191
4 192.168.10.192 .193 .254 .255
Mask /26 = 255.255.255.192 (...11000000)
Block size
256 - 192 = 64, so subnets start every 64: .0, .64, .128, .192.
Usable hosts
64 addresses minus network and broadcast leaves 62 per subnet.
Verify
The TIS IP Calculator confirms every range — exactly what you do in Lab 2.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
OBJ 1.7 · SUBNETTING
CIDR Host Counts to Memorise
Prefix
Mask
Subnets from a /24
Usable hosts
/25
255.255.255.128
2
126
/26
255.255.255.192
4
62
/27
255.255.255.224
8
30
/28
255.255.255.240
16
14
/29
255.255.255.248
32
6
/30
255.255.255.252
64
2 (P2P links)
WHEN IT MATTERS Pattern: each bit borrowed doubles the subnets and roughly halves the hosts.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
OBJ 1.7 · SUBNETTING
VLSM: Right-Sizing Subnets
1
The idea
Carve one block into different-sized subnets matched to each segment's host count.
2
Largest first
Allocate the biggest requirement first, then continue at the next free boundary.
3
Worked example
From a /24: a /25 for 100 users, a /26 for 50 servers, /30s for router links.
4
Why it matters
No wasted space — critical in cloud VPCs, where the CIDR is fixed at creation.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
OBJ 1.7 · IPv4 ADDRESSING
IPv4 Addressing: Classic Fault Patterns
• Duplicate IP address — two hosts configured statically with the same address
• Duplicate MAC address — usually cloned virtual machines
• Wrong default gateway — local traffic works, remote traffic fails
• Wrong subnet mask — 'random' unreachable hosts on the same LAN
• APIPA 169.254.x.x — the DHCP server never answered
• Expired or exhausted lease — check scope size and lease times
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
DOMAIN 1.0 · HANDS-ON
IPv4 Subnetting and CIDR
LAB 2
Split a /24 into four /26 subnets and verify the math with the TIS IP Calculator.
Use the TIS IP Calculator to break 192.168.10.0/24 into four /26 subnets, record each network, host range and broadcast, then assign an address from subnet 2 to a Linux interface.
YOU'LL BUILD
A completed four-subnet plan and a Linux interface carrying 192.168.10.65/26 as a labelled secondary address.
TOOLCHAIN
TIS IP Calculator (alfredang.github.io/ipcalculator), iproute2, Killercoda Ubuntu
DONE WHEN
The calculator shows 62 usable hosts and unique network/broadcast per /26, and ip -4 addr show eth0 lists inet 192.168.10.65/26 on label eth0:1.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
LAB 2 · PROCESS MAP
How Lab 2 Runs
1
Open the TIS IP Calculator in a
· step 1
2
Calculate each /26 block
26 · step 3
3
Fill the subnet table
Step 4 of 7
4
Assign an address from subnet 2 to
ip · step 5
5
Clean up the address
ip · step 7
THE POINT
Split a /24 into four /26 subnets and verify the math with the TIS IP Calculator.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
LAB 2 · VERIFY
IPv4 Subnetting and CIDR
✅ Expected result
The calculator shows 62 usable hosts and unique network/broadcast per /26, and ip -4 addr show eth0 lists inet 192.168.10.65/26 on label eth0:1.
IF IT DOESN'T WORK
Calculator ranges look wrong
Confirm you entered prefix /26, not /24 — the prefix length drives every boundary.
RTNETLINK: File exists
The address is already assigned — remove it first with ip addr del 192.168.10.65/26 dev eth0.
Address missing after add
Run as root and check you used dev eth0 — Killercoda's primary NIC is eth0.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
OBJ 1.8 · IPv6
Why IPv6
1
128-bit addresses
2^128 addresses end exhaustion — written as eight hex groups separated by colons.
2
Shortening rules
Drop leading zeros in each group; compress one run of zero groups with :: (once only).
3
No broadcast
IPv6 replaces broadcast with multicast (ff02::1 = all nodes) and anycast.
4
No NAT required
End-to-end addressing returns; firewalls, not address translation, enforce the boundary.
5
Efficient header
Fixed 40-byte header and no router fragmentation — faster forwarding.
6
2001:db8::/32
The documentation prefix — always safe for labs, examples and courseware.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
OBJ 1.8 · IPv6
Shortening an IPv6 Address
Two rules: strip leading zeros per group, and compress one zero run with ::.
Full:
2001:0db8:0000:0000:0001:0000:0000:1234
Rule 1 - drop leading zeros:
2001:db8:0:0:1:0:0:1234
Rule 2 - compress ONE zero run:
2001:db8::1:0:0:1234
Wrong: 2001:db8::1::1234 (two ::)
Only one ::
Two compressions would be ambiguous — the parser could not count the missing groups.
Pick the longest run
When two zero runs tie, compress the leftmost — the convention resolvers use.
Exam trap
Expanding a shortened address back to eight groups is a favourite question.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
OBJ 1.8 · IPv6
Key IPv6 Address Types
Type
Prefix
Role
Global unicast
2000::/3
Public, Internet-routable
Link-local
fe80::/10
Auto on every interface; one link only
Unique local
fc00::/7
Private — the RFC1918 analogue
Multicast
ff00::/8
ff02::1 all nodes, ff02::2 routers
Loopback
::1/128
Same role as 127.0.0.1
WHEN IT MATTERS Every IPv6 interface always holds a link-local address — even with no router or DHCP anywhere.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
OBJ 1.8 · IPv6
SLAAC: An Address Without a Server
1
Link-local
fe80:: self-made
2
RS
host asks routers
3
RA
prefix + gateway
4
Address
prefix + intf ID
5
DAD
duplicate check
WHY IT MATTERS
A v6 host configures itself from router advertisements alone — DHCPv6 is optional, used only when you need central control or extra options like DNS.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
OBJ 1.8 · IPv6
Interface IDs and Coexistence
1
EUI-64
Builds the 64-bit interface ID from the MAC: split it, insert FFFE, flip bit 7.
2
Privacy extensions
Random interface IDs defeat device tracking — the default on modern OSes.
3
Dual stack
Run IPv4 and IPv6 side by side — today's standard migration strategy.
4
Tunnels and NAT64
6to4/Teredo carry v6 inside v4; NAT64/DNS64 lets v6-only clients reach v4 servers.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
OBJ 1.8 · IPv6
IPv6 Subnetting Conventions
1
Every LAN is a /64
SLAAC needs 64 bits of interface ID — never subnet a LAN smaller than /64.
2
A site gets a /48
That is 65,536 /64 subnets — plan generously, address conservation is over.
3
Nibble boundaries
Subnet in 4-bit steps so prefixes stay readable in hex.
4
Zone IDs
Link-local commands need %eth0 to choose the interface — exactly as in Lab 3.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
DOMAIN 1.0 · HANDS-ON
IPv6 Addressing and Link-Local
LAB 3
Plan an IPv6 /64, add a global address, and ping link-local using a zone ID.
Break down 2001:db8::/64 in the TIS IP Calculator's IPv6 mode, add a documentation-range global address to eth0, observe the auto-generated fe80:: link-local address, and ping across both.
YOU'LL BUILD
An interface holding both a link-local fe80:: address and a global 2001:db8::10/64, verified by ping.
TOOLCHAIN
TIS IP Calculator (alfredang.github.io/ipcalculator), iproute2, ping6, Killercoda
DONE WHEN
ip -6 addr show eth0 lists both fe80::... and 2001:db8::10/64, and both pings reply (the ff02::1 ping needs the %eth0 zone suffix).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
LAB 3 · PROCESS MAP
How Lab 3 Runs
1
Open the IP Calculator in IPv6 mode
· step 1
2
Inspect the existing IPv6 config
ip · step 3
3
Verify both addresses are present
ip · step 5
4
Ping the all-nodes multicast with a
ping6 · step 6
5
Clean up
ip · step 8
THE POINT
Plan an IPv6 /64, add a global address, and ping link-local using a zone ID.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LAB 3 · VERIFY
IPv6 Addressing and Link-Local
✅ Expected result
ip -6 addr show eth0 lists both fe80::... and 2001:db8::10/64, and both pings reply (the ff02::1 ping needs the %eth0 zone suffix).
IF IT DOESN'T WORK
ping6: Invalid argument
Link-local targets need a zone — use ff02::1%eth0 so the kernel knows the egress interface.
No fe80:: address on eth0
IPv6 is disabled — sysctl -w net.ipv6.conf.eth0.disable_ipv6=0, then re-check.
Global ping fails
Confirm the add worked: ip -6 addr show eth0 must list 2001:db8::10/64 before you ping.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
OBJ 1.4 · PORTS & PROTOCOLS
Port Numbers: The L4 Address
1
0-1023 well-known
Reserved for standard services — HTTP 80, SSH 22, DNS 53. Memorise these.
2
1024-49151 registered
Vendor-registered applications: RDP 3389, MySQL 3306, SIP 5060.
3
49152-65535 ephemeral
Random client-side source ports, recycled per connection.
4
The socket pair
Source IP:port plus destination IP:port uniquely identifies every conversation.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
OBJ 1.4 · PORTS & PROTOCOLS
TCP vs UDP
TCP — connection-oriented
UDP — connectionless
• Three-way handshake before any data
• Sequencing, ACKs and retransmission
• Flow and congestion control
• HTTP(S), SSH, SMTP, FTP, RDP
• No handshake — just send
• No delivery guarantee, low overhead
• Ideal for real-time and tiny queries
• DNS, DHCP, TFTP, NTP, SNMP, RTP
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
OBJ 1.4 · TCP
The TCP Three-Way Handshake
1
SYN
client, seq = x
2
SYN-ACK
server, ack = x+1
3
ACK
open, data flows
WHY IT MATTERS
The [S] flag you captured in Lab 1 is step one of this exchange — and half-open handshakes are how SYN floods and stealth scans work.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
OBJ 1.4 · PORTS & PROTOCOLS
TCP or UDP for Your Application?
Must every byte arrive, in order, guaranteed?
YES — use TCP
Pay the handshake and header overhead to gain sequencing, acknowledgements and retransmission — right for web, mail, file transfer.
NO — use UDP
Skip the ceremony for speed: lost packets are ignored or handled by the app — right for voice, video, DNS lookups and telemetry.
QUIC (HTTP/3) builds TCP-like reliability on top of UDP — know that it exists.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
OBJ 1.4 · PORTS & PROTOCOLS
ICMP, IGMP, GRE and IPsec
1
ICMP
Layer 3 control messages — echo (ping), destination unreachable, TTL exceeded. No ports.
2
IGMP
Hosts join and leave IPv4 multicast groups in 224.0.0.0/4.
3
GRE
A generic tunnel that wraps any protocol inside IP — no encryption of its own.
4
IPsec AH
Authentication Header: integrity and origin proof, but no confidentiality.
5
IPsec ESP
Encapsulating Security Payload: encryption — the workhorse of site-to-site VPNs.
6
IKE
Negotiates IPsec keys and security associations over UDP 500/4500.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
OBJ 1.4 · PORTS & PROTOCOLS
Ports: File Transfer and Remote Access
Port
Protocol
Transport
Security note
20/21
FTP data / control
TCP
Cleartext — avoid
22
SSH and SFTP
TCP
Encrypted channel
23
Telnet
TCP
Cleartext — use SSH
69
TFTP
UDP
LAN boot/config only
445
SMB
TCP
Windows file sharing
3389
RDP
TCP
TLS-protected desktop
WHEN IT MATTERS Pairs to contrast on the exam: 21 vs 22 (SFTP), 23 vs 22 (SSH), 69 vs 21.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
OBJ 1.4 · PORTS & PROTOCOLS
Ports: Web, Mail and Name Services
Port
Protocol
Transport
Notes
80 / 443
HTTP / HTTPS
TCP
443 adds TLS
25 / 587
SMTP / submission
TCP
587 = STARTTLS sending
110 / 995
POP3 / POP3S
TCP
Download-and-delete mail
143 / 993
IMAP / IMAPS
TCP
Server-side mailboxes
53
DNS
UDP + TCP
TCP for zone transfers
67 / 68
DHCP
UDP
Server 67, client 68
WHEN IT MATTERS Mail flows: SMTP sends between servers, POP3/IMAP retrieve to clients — the S-suffixed ports add TLS.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
OBJ 1.4 · PORTS & PROTOCOLS
Securing E-mail: The Port Story
1
Legacy trio
SMTP 25, POP3 110, IMAP 143 — all cleartext, all still on the exam.
2
Implicit TLS
Wrapped-in-TLS variants: SMTPS 465, POP3S 995, IMAPS 993.
3
STARTTLS on 587
The modern client-submission port: starts plain, upgrades to TLS in-band.
4
Anti-spoofing
SPF, DKIM and DMARC live in DNS TXT records — covered again in the DNS lab.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
OBJ 1.4 · PORTS & PROTOCOLS
Ports: Infrastructure Services
Port
Protocol
Transport
Notes
123
NTP
UDP
Clock sync, stratum tree
161 / 162
SNMP / traps
UDP
Monitoring; v3 adds crypto
389 / 636
LDAP / LDAPS
TCP
Directory queries
514
Syslog
UDP
Central log collection
5060 / 5061
SIP / SIP-TLS
UDP/TCP
VoIP call signalling
500 / 4500
IKE / NAT-T
UDP
IPsec key negotiation
WHEN IT MATTERS These six rows plus the previous two tables cover every port listed in objective 1.4.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
OBJ 1.4 · PORTS & PROTOCOLS
Reading ss and nmap Output
Two commands cover both directions: what you expose, and what a target exposes.
# ss -tulnp (your own listeners)
tcp LISTEN 0.0.0.0:22 sshd
udp UNCONN 127.0.0.53:53 systemd-resolve
# nmap -sT -p 1-1024 scanme.nmap.org
22/tcp open ssh
80/tcp open http
25/tcp filtered smtp
LISTEN vs open
ss shows sockets bound locally; nmap shows what a remote host answers on.
filtered
A firewall silently dropped the probe — no RST ever came back.
Stay numeric
The -n flags keep raw port numbers visible so you learn numbers, not names.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
DOMAIN 1.0 · HANDS-ON
Common Ports and Protocols
LAB 4
Connect protocol names to well-known port numbers using ss and nmap.
Enumerate the listening TCP/UDP sockets on your own host with ss, scan the well-known port range of scanme.nmap.org with nmap, and map every open port you find to the N10-009 protocol list.
YOU'LL BUILD
A completed port-to-protocol map covering your own listeners and the remote scan results.
TOOLCHAIN
nmap, ss, net-tools (netstat), getent, Killercoda Ubuntu
DONE WHEN
ss shows local listeners with numeric ports; nmap reports open ports on scanme.nmap.org (expect 22 and 80); getent services https returns 443/tcp.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
LAB 4 · PROCESS MAP
How Lab 4 Runs
1
Install nmap and net-tools
apt · step 1
2
List TCP/UDP listeners on your own
ss · step 2
3
Scan the well-known range on the Nmap
nmap · step 3
4
Map each open port to the exam list
Step 4 of 5
5
Resolve service names to port numbers
getent · step 5
THE POINT
Connect protocol names to well-known port numbers using ss and nmap.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
LAB 4 · VERIFY
Common Ports and Protocols
✅ Expected result
ss shows local listeners with numeric ports; nmap reports open ports on scanme.nmap.org (expect 22 and 80); getent services https returns 443/tcp.
IF IT DOESN'T WORK
nmap scan returns nothing
Check egress with ping scanme.nmap.org — playground networks can be slow; re-run the scan.
ss: command not found
Use netstat -tulnp from net-tools instead — both list the same listening sockets.
Ports show names, not numbers
Keep the -n flag (ss -tulnp) so output stays numeric and you learn the numbers.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
OBJ 1.4 · DNS
DNS: The Internet's Directory
1
FQDN
host.domain.tld — www.example.com is read right to left, ending at the root.
2
Hierarchy
Root servers -> TLD servers (.com, .sg) -> authoritative servers for each zone.
3
Recursive resolver
Your configured server (e.g. 8.8.8.8) chases referrals and caches the answers.
4
UDP/TCP 53
Queries ride UDP 53; zone transfers and oversized answers switch to TCP 53.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
OBJ 1.4 · DNS
A DNS Lookup, Step by Step
1
Client asks its recursive resolver
▶
2
Cache hit? Answer returns instantly
▶
3
Miss: resolver asks root, then .com TLD
▶
4
TLD refers to the authoritative server
▶
5
A record returned and cached per TTL
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
OBJ 1.4 · DNS
DNS Server Roles and Variants
1
Authoritative
Holds the zone file and gives the definitive answer for its domains.
2
Recursive / caching
Resolves on behalf of clients and remembers answers for the TTL.
3
Internal DNS
Private zones for corp resources — split horizon keeps them invisible outside.
4
Dynamic DNS
Clients or DHCP update records automatically as addresses change.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
OBJ 1.4 · DNS
DNS Record Types on the Exam
Record
Maps
Example / note
A / AAAA
Name -> IPv4 / IPv6
The bread-and-butter records
CNAME
Name -> another name
An alias — never points to an IP
MX
Domain -> mail host
Priority number: lower wins
NS / SOA
Zone -> servers / authority
SOA holds serial and timers
PTR
IP -> name
Reverse zones; mail server checks
TXT / SRV
Text / service + port
SPF and DKIM live in TXT
WHEN IT MATTERS Lab 5 queries every one of these with dig against live domains.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
OBJ 1.4 · DNS
dig in Action
dig +short strips the noise and prints only the answer — perfect for learning records.
$ dig +short A google.com
142.250.4.100
$ dig +short MX google.com
10 smtp.google.com.
$ dig +short -x 8.8.8.8
dns.google.
$ dig +short CNAME www.github.com
github.com.
MX priority
The leading 10 is the preference — lower numbers are tried first.
-x reverses
Turns 8.8.8.8 into its PTR name from the in-addr.arpa reverse zone.
CNAME chains
www.github.com is an alias for github.com — the resolver follows the chain.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
DOMAIN 1.0 · HANDS-ON
DNS Record Types
LAB 5
Query every N10-009 DNS record type with dig and interpret the answers.
Use dig to query A, AAAA, MX, TXT, NS, CNAME, PTR, SOA and SRV records against live domains, reading addresses, mail priorities, aliases and zone-authority data from the answers.
YOU'LL BUILD
A worked set of dig queries — one per record type on the exam — with each answer interpreted.
TOOLCHAIN
dig, nslookup, host (dnsutils), Killercoda Ubuntu
DONE WHEN
Every dig query returns an answer: A gives IPv4, AAAA gives IPv6, MX shows priorities, -x 8.8.8.8 returns dns.google, and the SOA lists the primary NS and serial.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
LAB 5 · PROCESS MAP
How Lab 5 Runs
1
Install dnsutils
apt · step 1
2
Query the AAAA record
dig · step 3
3
Query TXT
dig · step 5
4
Reverse-resolve an IP to a name
dig · step 7
5
Locate a service with an SRV record
dig · step 9
THE POINT
Query every N10-009 DNS record type with dig and interpret the answers.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
LAB 5 · VERIFY
DNS Record Types
✅ Expected result
Every dig query returns an answer: A gives IPv4, AAAA gives IPv6, MX shows priorities, -x 8.8.8.8 returns dns.google, and the SOA lists the primary NS and serial.
IF IT DOESN'T WORK
dig: command not found
Install the tools: apt update && apt install -y dnsutils.
Empty answer for CNAME
Not every name has one — query an alias such as www.github.com, not the bare domain.
SERVFAIL or timeout
Query an explicit resolver: dig @8.8.8.8 +short A google.com to bypass the local stub.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
OBJ 1.4 · DHCP
DORA: How a Lease Happens
1
Discover
bcast from 0.0.0.0
2
Offer
server proposes IP
3
Request
client accepts one
4
Acknowledge
lease confirmed
WHY IT MATTERS
Discover and Request are broadcasts on UDP 67/68 — which is why every broadcast domain needs its own DHCP server or a relay pointing to one.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
OBJ 1.4 · DHCP
DHCP Server Concepts
1
Scope / pool
The range of addresses the server may hand out on a subnet.
2
Lease time
Addresses are borrowed — clients try to renew at 50% of the lease.
3
Reservation
A fixed IP tied to a MAC address — printers and servers stay stable.
4
Exclusion range
Addresses inside the scope the server must never assign.
5
Options
The lease also carries mask, gateway, DNS servers, NTP and more.
6
Relay / IP helper
Forwards client broadcasts to a central DHCP server across subnets.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
OBJ 1.4 · DHCP
Static vs Dynamic vs APIPA
Static assignment
• Manually configured per host
• For routers, servers, printers
• No dependency on DHCP
• Risk: typos, duplicates, drift
Dynamic (DHCP)
• Automatic from a scope
• Self-documenting via leases
• Scales to thousands of hosts
• One server per broadcast domain
APIPA fallback
• 169.254.0.0/16 self-assigned
• Means DHCP was unreachable
• Link-local talk only, no gateway
• A diagnostic clue, not a fix
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
OBJ 1.4 · DHCP
Watching DORA in tcpdump
Filter on 'port 67 or port 68' and renew a lease — all four messages appear.
# tcpdump -i eth0 -nn -v 'port 67 or port 68'
0.0.0.0.68 > 255.255.255.255.67:
DHCP-Message: Discover
10.244.0.1.67 > 255.255.255.255.68:
DHCP-Message: Offer (your-ip 10.244.0.5)
0.0.0.0.68 > 255.255.255.255.67:
DHCP-Message: Request
10.244.0.1.67 > 255.255.255.255.68:
DHCP-Message: ACK (lease-time 3600)
Broadcasts
The client has no address yet, so Discover and Request come from 0.0.0.0.
The Offer
Carries the proposed IP, mask, gateway, DNS and lease time in DHCP options.
ACK seals it
Only after the ACK may the client actually use the address.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
OBJ 1.4 · DHCP
When DHCP Goes Wrong
1
Exhausted scope
More devices than addresses — shrink lease times or widen the scope.
2
Rogue DHCP server
An unauthorised server hands out bad leases — find it, then enable DHCP snooping.
3
Missing relay
Clients across a router never reach the server — configure an IP helper address.
4
IPAM
IP address management tools track scopes, leases and reservations across sites.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
DOMAIN 1.0 · HANDS-ON
DHCP Lease Capture (DORA)
LAB 6
Capture all four DHCP DORA messages during a live lease renewal.
Run tcpdump against UDP ports 67/68 while releasing and re-requesting your DHCP lease with dhclient, then identify the Discover, Offer, Request and Acknowledge messages in the capture.
YOU'LL BUILD
A capture showing the full DORA exchange and a freshly renewed lease on eth0.
TOOLCHAIN
isc-dhcp-client (dhclient), tcpdump, Killercoda Ubuntu
DONE WHEN
The capture shows DHCPDISCOVER broadcast from 0.0.0.0 to 255.255.255.255, followed by Offer, Request and Ack; dhclient reports the address it bound.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
LAB 6 · PROCESS MAP
How Lab 6 Runs
1
Install the DHCP client and capture
apt · step 1
2
Start a background capture on the DHCP
tcpdump · step 2
3
Release the current lease
dhclient · step 3
4
Identify Discover
Step 5 of 6
5
Stop the capture
kill · step 6
THE POINT
Capture all four DHCP DORA messages during a live lease renewal.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
LAB 6 · VERIFY
DHCP Lease Capture (DORA)
✅ Expected result
The capture shows DHCPDISCOVER broadcast from 0.0.0.0 to 255.255.255.255, followed by Offer, Request and Ack; dhclient reports the address it bound.
IF IT DOESN'T WORK
Connectivity lost after release
Expected — dhclient -v eth0 re-acquires a lease; if the session breaks, reload the playground.
No DHCP packets in capture
Check the filter is 'port 67 or port 68' and start the capture before releasing.
dhclient: command not found
Install it: apt update && apt install -y isc-dhcp-client.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
OBJ 1.3 · CLOUD
The network is now software.
Hypervisors, NFV and cloud VPCs rebuild every concept in this domain — switches, routers, firewalls, subnets — as code you can deploy in seconds.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 118
OBJ 1.3 · VIRTUALIZATION
Virtualization Foundations
1
Type 1 hypervisor
Bare-metal: ESXi, Hyper-V, KVM — the production data center standard.
2
Type 2 hypervisor
Hosted on a desktop OS: VirtualBox, VMware Workstation — labs and testing.
3
Why virtualize
Consolidation, power savings, snapshots and fast recovery of whole systems.
4
vSwitch
A software switch connecting VM NICs — configure it like a physical switch.
5
Virtual disks
VHD/VHDX/VMDK files hold entire machines — portable and snapshottable.
6
Not emulation
Virtualization shares real CPU hardware; emulation imitates different hardware.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 119
OBJ 1.8 · MODERN NETWORKS
NFV and SDN
1
NFV
Network functions — router, firewall, load balancer — shipped as software appliances.
2
SDN
Splits the control plane from the data plane; the network is programmed centrally.
3
The planes
Data forwards packets, control decides routes, management configures it all.
4
Distributed switching
One logical switch spans every host — configure once, applied everywhere.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 120
OBJ 1.3 · CLOUD
Cloud Service Models
Model
Provider manages
You manage
Example
IaaS
Hardware, hypervisor
OS, apps, data
AWS EC2
PaaS
Up to the runtime
Code and data
Heroku, App Service
SaaS
The whole stack
Usage and config
Microsoft 365
DaaS
Virtual desktops
Profiles, policy
Windows 365
WHEN IT MATTERS The more the provider manages, the less you control — pick per workload, not per company.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 121
OBJ 1.3 · CLOUD
Cloud Deployment Models
Model
Who uses it
Trade-off
Public
Anyone, shared infrastructure
Lowest cost, least control
Private
One organisation
Full control, full cost
Hybrid
A mix of both
Flexibility + complexity
Community
A shared-interest group
Split compliance costs
WHEN IT MATTERS Hybrid is the enterprise norm: sensitive systems stay private, elastic workloads burst to public.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 122
OBJ 1.3 · CLOUD
Cloud Characteristics
1
Scalability
Grow capacity on demand without buying or racking hardware.
2
Elasticity
Grow and shrink automatically with load — pay only for what runs.
3
Multitenancy
Many customers share the provider's infrastructure, isolated logically.
4
Least privilege
Cloud IAM grants every identity only the access it needs — nothing more.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 123
OBJ 1.3 · CLOUD
Inside a VPC
1
VPC
Your private software-defined network in a cloud region, with a CIDR block you choose.
2
Subnets
Carve the VPC CIDR per availability zone; public subnets route to an internet gateway.
3
Route tables
Decide where each subnet's traffic goes — the VPC's built-in routers.
4
Security groups
Stateful per-instance firewalls — allow rules only, replies pass automatically.
5
Network ACLs
Stateless subnet-level filters supporting both allow and deny rules.
6
Gateways
Internet, NAT and VPN gateways connect the VPC to everything outside it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 124
OBJ 1.3 · CLOUD
Security Groups vs Network ACLs
Security group (instance level)
Network ACL (subnet level)
• Stateful — return traffic auto-allowed
• Allow rules only
• Attached to instances / NICs
• First line for app-tier isolation
• Stateless — reply needs its own rule
• Allow and deny rules, numbered
• Applies to everything in the subnet
• Broad guardrails and IP blacklists
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 125
OBJ 1.3 · CLOUD
A Packet Leaves Your VPC
1
Instance
SG egress check
2
Subnet
NACL evaluated
3
Route table
0.0.0.0/0 -> GW
4
Gateway
IGW or NAT GW
5
Internet
public source IP
WHY IT MATTERS
Cloud troubleshooting is this pipeline in order: instance firewall, subnet ACL, route, gateway — the same layered thinking as the OSI model.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 126
OBJ 1.3 · CLOUD
Connecting to the Cloud
1
VPN over Internet
IPsec tunnels to a cloud VPN gateway — quick, cheap, encrypted.
2
Direct Connect
Private circuits (ExpressRoute, Direct Connect) — predictable latency and bandwidth.
3
Transit gateways
Hub-and-spoke interconnect for many VPCs and on-prem sites.
4
NAT gateway
Lets private subnets reach out to the Internet without being reachable inbound.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 127
OBJ 1.8 · MODERN NETWORKS
Infrastructure as Code
1
IaC
Networks described in files (Terraform, CloudFormation) — versioned like source code.
2
Automation
Provisioning without manual steps: consistent, repeatable, reviewable.
3
Orchestration
Chains automated tasks into whole-environment deployments.
4
Why it wins
A VPC built from code can be rebuilt identically in minutes — Lab 7 does it by hand once.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
127

## Slide 128
OBJ 1.3 · CLOUD
Public, Private or Hybrid?
Does compliance or data residency force workloads on-premises?
YES — private or hybrid
Keep regulated data on private infrastructure and burst stateless workloads to public cloud through a hybrid design.
NO — public first
Start public for elasticity and low capital cost; revisit only if scale, latency or new rules demand it.
Cost surprises come from egress traffic — model data flows before you commit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
128

## Slide 129
DOMAIN 1.0 · HANDS-ON
Simulating a Cloud VPC with Namespaces
LAB 7
Build a VPC-style virtual network from namespaces, a bridge and veth pairs.
Recreate cloud VPC building blocks on one Linux host: two network namespaces act as VMs, a Linux bridge acts as the virtual switch, and veth pairs cable them together on subnet 10.0.1.0/24.
YOU'LL BUILD
Two isolated 'VMs' (web and db) pinging each other through a Linux bridge — a working VPC subnet.
TOOLCHAIN
iproute2 (ip netns, ip link, veth, bridge), Killercoda Ubuntu
DONE WHEN
ip netns exec web ping -c2 10.0.1.20 returns two replies — two isolated hosts sharing one subnet through a bridge, with no router involved.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
129

## Slide 130
LAB 7 · PROCESS MAP
How Lab 7 Runs
1
Create two namespaces to act as the
ip · step 1
2
Create a veth 'virtual cable' for each
ip · step 3
3
Move the VM-side ends into their
ip · step 5
4
Assign IPs in the same /24 and bring
ip · step 6
5
Clean up
ip · step 8
THE POINT
Build a VPC-style virtual network from namespaces, a bridge and veth pairs.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
130

## Slide 131
LAB 7 · VERIFY
Simulating a Cloud VPC with Namespaces
✅ Expected result
ip netns exec web ping -c2 10.0.1.20 returns two replies — two isolated hosts sharing one subnet through a bridge, with no router involved.
IF IT DOESN'T WORK
Network is unreachable
Bring interfaces up in both namespaces, including lo, and re-check the 10.0.1.x addresses.
Destination Host Unreachable
Verify both bridge-side ends are enslaved and up: ip link set br-web master br0 (and br-db).
Cannot find device veth-web
That end now lives inside the namespace — manage it via ip netns exec web ip link ...
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
131

## Slide 132
DOMAIN 1 · RECAP
Domain 1 Exam-Day Anchors
1
OSI in order
Please Do Not Throw Sausage Pizza Away — and PDUs: bits, frame, packet, segment, data.
2
Port table cold
FTP 21, SSH 22, DNS 53, DHCP 67/68, HTTP 80, HTTPS 443, NTP 123, RDP 3389.
3
RFC1918 ranges
10/8, 172.16/12, 192.168/16 — private, NATed, never routed publicly.
4
Subnet math
Block size = 256 minus the mask's last octet; hosts = 2^host-bits minus 2.
5
DORA + SLAAC
DHCP is Discover-Offer-Request-Ack; IPv6 can self-configure from an RA.
6
Cloud layers
SG then NACL then route then gateway — the packet pipeline of every VPC.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
132

## Slide 133
NEXT · DOMAIN 2
Concepts are the map. Everything else is the road.
Domain 2 puts these concepts to work: routing, switching, VLANs and wireless — built on the addressing and models you now own.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
133

## Slide 134
DOMAIN 1.0 RECAP
Recap — Networking Concepts
• You can now: Capture live traffic and map each protocol header to its OSI layer.
• You can now: Split a /24 into four /26 subnets and verify the math with the TIS IP Calculator.
• You can now: Plan an IPv6 /64, add a global address, and ping link-local using a zone ID.
• You can now: Connect protocol names to well-known port numbers using ss and nmap.
• You can now: Query every N10-009 DNS record type with dig and interpret the answers.
• You can now: Capture all four DHCP DORA messages during a live lease renewal.
• You can now: Build a VPC-style virtual network from namespaces, a bridge and veth pairs.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
134

## Slide 135
DOMAIN 2.0 · 20% OF THE EXAM
Network Implementation
Routing technologies · switching technologies · wireless devices · physical installations
2.0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
135

## Slide 136
WHAT YOU'LL DO
Hands-On Labs — Network Implementation
Labs 8–10
• Static Routing Between Two Subnets
• 802.1Q VLAN Tagging
• Link Aggregation (LACP Bond)
Labs 11–13
• Wireless Concepts and Channel Survey
• NAT and PAT with iptables
• DHCP Server with isc-dhcp-server
Lab 14
• Authoritative DNS with BIND9
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
136

## Slide 137
20% OF THE EXAM
Domain 2 — Network Implementation.
Routing, switching, wireless and physical installations — 20% of the N10-009 exam and the heart of the build-it job role.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
137

## Slide 138
OBJ 2.1 · ROUTING TECHNOLOGIES
Routers Connect Network IDs
1
Routers care about destinations
A router reads the destination network ID, looks it up in its routing table and forwards out the matching interface.
2
Any medium
Routing is Layer 3 — a router joins Ethernet, fiber and wireless segments because IP is independent of the link below.
3
Every router has a routing table
The table maps destination networks to a next hop or exit interface; no match and no default route means the packet is dropped.
4
Default route
0.0.0.0/0 is the gateway of last resort — everything without a more specific match goes there, usually upstream.
5
Gateway router
The router end hosts point at (their default gateway); it moves traffic between the LAN and everything beyond.
6
Upstream router
The next router towards the ISP and Internet core — SOHO gateways simply default-route everything upstream.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
138

## Slide 139
OBJ 2.1 · ROUTING TECHNOLOGIES
Reading a Routing Table
1
Destination + prefix
The network this row matches, e.g. 10.2.2.0/24 — the prefix length says how many leading bits must match.
2
Next hop (via)
The neighbouring router's IP the packet is handed to; it must sit on a directly connected subnet.
3
Interface (dev)
Which NIC the frame leaves on; connected routes appear automatically when an IP is configured.
4
Metric
Tie-breaker between equal routes from the same protocol — lower wins.
5
See it yourself
Linux: ip route. Windows: route print or netstat -r. Cisco: show ip route.
6
Loopback & multicast
127.0.0.0/8 stays on-box; 224.0.0.0/4 (class D) is multicast — both appear as special rows.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
139

## Slide 140
OBJ 2.1 · ROUTING TECHNOLOGIES
Metrics and Convergence — Key Terms
1
Hop count
Routers crossed to reach the destination — RIP's only measure, blind to link speed.
2
Bandwidth / cost
OSPF derives cost from interface bandwidth, so a 3-hop 10G path beats a 1-hop 100M link.
3
Latency / delay
EIGRP factors delay into its composite metric; satellite links get penalised.
4
MTU
Maximum transmission unit per link — mismatches cause fragmentation or silent drops (Lab 33).
5
Convergence
The state where every router's table reflects the current topology; faster is better.
6
Convergence window
Between failure and re-convergence, packets can loop or blackhole — protocols race to shrink it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
140

## Slide 141
OBJ 2.1 · ROUTING TECHNOLOGIES
Static vs Dynamic Routing
Static routing
Dynamic routing
• Admin types each route by hand — persistent until removed
• Zero protocol overhead: no hellos, no updates, no CPU
• Predictable and secure — nothing advertises a bad route
• Does not adapt: a failed link means manual repair
• Best for stubs, labs and default routes
• Routers exchange reachability via a routing protocol
• Learns new subnets and routes around failures itself
• Costs CPU, bandwidth and a convergence window
• Needs securing (authentication) against rogue peers
• Best for anything beyond a handful of routers
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
141

## Slide 142
OBJ 2.1 · ROUTING TECHNOLOGIES
Choosing a Routing Approach
Does the topology change often or span many routers?
YES — DYNAMIC ROUTING
Run OSPF (open) or EIGRP (Cisco); routers learn and re-converge around failures automatically. Use BGP between autonomous systems.
NO — STATIC ROUTES
A handful of fixed routes is simpler, uses zero CPU or bandwidth and cannot be poisoned by a rogue peer — ideal for stub networks.
Most real networks mix both: dynamic in the core, static at stubs and for the default route.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
142

## Slide 143
OBJ 2.1 · ROUTING TECHNOLOGIES
IGP vs EGP — Where Protocols Live
1
Autonomous System (AS)
One organisation's network under a single routing policy, identified by an AS number — your ISP is one, Google is another.
2
IGP — interior
Runs INSIDE one AS: OSPF, EIGRP, RIP, IS-IS. Optimises for fast paths and quick convergence.
3
EGP — exterior
Runs BETWEEN ASes. BGP is the only EGP in use — it optimises for policy and reachability, not speed.
4
Distance vector
Routers tell neighbours their whole table periodically ('routing by rumour') — RIP.
5
Link state
Routers flood link advertisements so everyone builds the same map, then run Dijkstra — OSPF, IS-IS.
6
Path vector
BGP advertises the full AS path per prefix; a router seeing its own AS number detects the loop.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
143

## Slide 144
OBJ 2.1 · ROUTING TECHNOLOGIES
Administrative Distance — Who Do You Trust?
Route source
AD
Trust level
Connected
0
Directly attached — always wins
Static
1
Manually configured
eBGP
20
External BGP peers
EIGRP
90
Cisco IGP
OSPF
110
Standards-based IGP
RIP
120
Legacy — least trusted
WHEN IT MATTERS When two protocols offer the SAME prefix, the lower AD wins before any metric is compared.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
144

## Slide 145
OBJ 2.1 · ROUTING TECHNOLOGIES
Route Selection — The Order That Matters
1
Longest prefix match
most specific wins
2
Lowest AD
most trusted source
3
Lowest metric
best path in protocol
4
Forward / balance
send the packet
WHY IT MATTERS
A /32 static route beats an OSPF /16 every time — prefix length is compared before AD or metric, a classic exam trap.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
145

## Slide 146
OBJ 2.1 · ROUTING TECHNOLOGIES
Routing Protocols Compared
Protocol
Type
Metric
AD
Role
RIP
Distance vector
Hop count (max 15)
120
Legacy small LANs
OSPF
Link state
Cost (bandwidth)
110
Enterprise IGP
EIGRP
Adv. distance vector
Bandwidth + delay
90
Cisco networks
BGP
Path vector
AS-path + attributes
20 eBGP
The Internet's EGP
WHEN IT MATTERS Know the AD column cold — it is the most-tested fact on this slide.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
146

## Slide 147
OBJ 2.1 · ROUTING TECHNOLOGIES
RIP — Routing Information Protocol
1
Distance vector
Advertises its full table to neighbours every 30 seconds; routes by hop count alone.
2
Max 15 hops
Hop 16 means unreachable — a hard diameter limit that rules RIP out of large networks.
3
RIPv1 vs RIPv2
v1 was classful (no masks in updates); v2 added masks, multicast updates and authentication.
4
Slow convergence
Minutes to stabilise after a failure, with loop-prevention hacks (split horizon, poison reverse).
5
Where you'll see it
Legacy gear and tiny stub networks; on the exam it is the 'AD 120, hop-count, max 15' answer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
147

## Slide 148
OBJ 2.1 · ROUTING TECHNOLOGIES
OSPF — Open Shortest Path First
1
Link state
Floods LSAs so every router shares an identical topology map, then computes shortest paths (SPF/Dijkstra).
2
Cost metric
Cost = reference bandwidth / link bandwidth — the protocol prefers fast links, not few hops.
3
Areas
Area 0 is the backbone; other areas attach to it, shrinking each router's database and SPF workload.
4
Neighbors & adjacency
Routers hello on 224.0.0.5, become neighbours, then synchronise databases to reach FULL.
5
Fast convergence
Seconds after a change — triggered updates, no periodic full-table floods.
6
Open standard
RFC-standard, multi-vendor, AD 110 — the default enterprise IGP choice.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
148

## Slide 149
OBJ 2.1 · ROUTING TECHNOLOGIES
EIGRP — Enhanced Interior Gateway
1
Advanced distance vector
Cisco's hybrid: neighbour-based updates like distance vector, but fast and loop-free via DUAL.
2
Composite metric
Bandwidth + delay by default (load and reliability optional) — far smarter than hop count.
3
Feasible successor
A pre-computed backup route lets EIGRP fail over almost instantly without recomputing.
4
Partial updates
Sends only changes, only to affected neighbours — very low steady-state overhead.
5
AD 90
More trusted than OSPF (110) on Cisco boxes; now an open RFC but still mostly Cisco shops.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
149

## Slide 150
OBJ 2.1 · ROUTING TECHNOLOGIES
BGP — The Internet's Routing Protocol
1
Path vector EGP
The routing protocol of the Internet — every ISP exchanges reachability with BGP.
2
Autonomous systems
Prefixes are advertised with the full AS path; policy decides which path wins, not speed.
3
eBGP vs iBGP
eBGP peers between different ASes (AD 20); iBGP carries those routes inside your AS (AD 200).
4
Attributes over metrics
Selection walks attributes in order: weight, local preference, AS-path length, MED...
5
Slow and steady
Over a million Internet routes; convergence takes time — stability and policy beat speed here.
6
TCP 179
BGP peers over a TCP session — a filter or reachability problem shows up as a dropped peering.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
150

## Slide 151
OBJ 2.1 · ROUTING TECHNOLOGIES
Worked: Checking an OSPF Neighbor
Two commands tell you whether OSPF is healthy and what it learned.
R1# show ip ospf neighbor
Neighbor ID Pri State Address Interface
2.2.2.2 1 FULL/DR 10.0.12.2 Gi0/0
3.3.3.3 1 FULL/BDR 10.0.13.2 Gi0/1
R1# show ip route ospf
O 10.2.2.0/24 [110/2] via 10.0.12.2, Gi0/0
FULL state
Adjacency complete — databases synchronised; anything stuck in EXSTART or 2-WAY needs checking
DR / BDR
On multi-access LANs routers elect a Designated Router to cut LSA flooding
[110/2]
AD 110 (OSPF) / metric 2 — cost summed from interface bandwidths along the path
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
151

## Slide 152
OBJ 2.1 · ROUTING TECHNOLOGIES
First Hop Redundancy — VRRP & HSRP
1
The problem
Hosts have ONE default gateway; if that router dies the whole subnet is offline while a second router sits idle.
2
FHRP
First Hop Redundancy Protocols let two or more routers share one virtual IP that hosts use as their gateway.
3
VRRP
Open standard: one master answers the VIP, backups take over on failure — election by priority.
4
HSRP
Cisco's equivalent: active and standby routers exchange hellos; preempt lets the preferred router reclaim.
5
Virtual IP + MAC
The VIP and a virtual MAC float to whichever router is active — hosts never notice the failover.
6
GLBP
Cisco's load-balancing FHRP — multiple gateways forward simultaneously.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
152

## Slide 153
OBJ 2.1 · ROUTING TECHNOLOGIES
SOHO vs Enterprise Routers
SOHO router
Enterprise router
• Router + switch + WAP + firewall in one box
• Web GUI; default IP, username, password — change them
• NAT and a DHCP server enabled by default
• WAN port is usually a DHCP client
• Sized for a handful of devices
• Dedicated routing hardware, modular interfaces
• CLI-driven OS (e.g. Cisco IOS); config as files
• Runs OSPF/BGP, FHRP and QoS at line rate
• 100x the throughput and connection capacity
• Managed via SSH/console with AAA
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
153

## Slide 154
OBJ 2.1 · ROUTING TECHNOLOGIES
Worked: Static Routes on Linux
The exact commands Lab 8 uses to route between 10.1.1.0/24 and 10.2.2.0/24.
# on the router r1
sysctl -w net.ipv4.ip_forward=1
# on host A (10.1.1.2)
ip route add 10.2.2.0/24 via 10.1.1.1
# on host B (10.2.2.2)
ip route add 10.1.1.0/24 via 10.2.2.1
ip route # verify the table
ip_forward
A Linux box only forwards packets between interfaces when this kernel switch is on
via 10.1.1.1
The next hop — must be on a directly connected subnet the host can already reach
Symmetry
Both sides need a route; a one-way route gives replies no path back
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
154

## Slide 155
DOMAIN 2.0 · HANDS-ON
Static Routing Between Two Subnets
LAB 8
Build a two-subnet topology and route between them with static routes.
Create three network namespaces (host A, router R1, host B), wire them with veth pairs, enable IP forwarding on R1 and add the static routes that let 10.1.1.0/24 reach 10.2.2.0/24.
YOU'LL BUILD
A working routed path A -> R1 -> B with hand-written static routes on both end hosts.
TOOLCHAIN
iproute2, ip netns, sysctl
DONE WHEN
ip netns exec a ping -c2 10.2.2.2 succeeds, and ip route inside namespace a shows 10.2.2.0/24 via 10.1.1.1.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
155

## Slide 156
LAB 8 · PROCESS MAP
How Lab 8 Runs
1
Create three namespaces; r1 is the
ip · step 1
2
Move each veth end into its namespace
ip · step 3
3
Bring up loopbacks and all veth
for · step 5
4
Enable IP forwarding on the router
ip · step 6
5
Verify with ping
ip · step 8
THE POINT
Build a two-subnet topology and route between them with static routes.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
156

## Slide 157
LAB 8 · VERIFY
Static Routing Between Two Subnets
✅ Expected result
ip netns exec a ping -c2 10.2.2.2 succeeds, and ip route inside namespace a shows 10.2.2.0/24 via 10.1.1.1.
IF IT DOESN'T WORK
Ping A to B fails
Check forwarding: ip netns exec r1 sysctl net.ipv4.ip_forward must return 1
Network is unreachable
A static route is missing — re-add: ip route add 10.2.2.0/24 via 10.1.1.1
Interface shows DOWN
Bring up BOTH ends of each veth pair with ip link set <if> up
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
157

## Slide 158
OBJ 2.2 · SWITCHING TECHNOLOGIES
Managed Switches and Switch Management
1
Unmanaged switch
Plug and play, zero configuration, no VLANs — fine for a desk, invisible to the network team.
2
Managed switch
Configurable: VLANs, trunks, STP, LACP, mirroring, SNMP. Everything in this domain assumes one.
3
Management IP / SVI
Give a management VLAN interface an address; your PC must be able to reach that subnet to manage it.
4
Change the defaults
Default admin passwords on switches are public knowledge — change them before the switch carries traffic.
5
Console access
A console/rollover cable gives CLI access with no network at all — your lifeline when config breaks.
6
Out-of-band mgmt
A separate management network keeps control access alive when the production LAN is down.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
158

## Slide 159
OBJ 2.2 · SWITCHING TECHNOLOGIES
VLAN Fundamentals
1
What a VLAN is
One physical switch split into multiple logical switches — each VLAN is its own broadcast domain.
2
Why segment
Smaller broadcast domains, failure containment, and policy boundaries between departments and device types.
3
VLAN ID
12-bit field: 1-4094 usable. VLAN 1 is the default everywhere — move production traffic off it.
4
Data VLAN
Ordinary user traffic — PCs, laptops and servers grouped by function or department.
5
Voice VLAN
IP phones get their own tagged VLAN for QoS and clean troubleshooting; the PC daisy-chains through the phone.
6
Crossing VLANs
Traffic between VLANs must be ROUTED — a Layer 3 hop, covered two slides on.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
159

## Slide 160
OBJ 2.2 · SWITCHING TECHNOLOGIES
Inside the 802.1Q Tag
1
4-byte tag
802.1Q inserts 4 bytes into the Ethernet header after the source MAC — Lab 9 captures one live.
2
TPID 0x8100
The first 2 bytes announce 'this frame is tagged' so receivers parse the rest of the tag.
3
VLAN ID (12 bits)
Which VLAN the frame belongs to — switches use it to keep traffic separated on trunks.
4
PCP (3 bits)
Priority Code Point — the Class of Service marking QoS uses to prioritise voice and video.
5
Tag lifecycle
Added when a frame enters a trunk, stripped when it exits an access port — hosts normally never see tags.
6
Linux view
A sub-interface eth0.10 tags everything VID 10 on the way out — exactly how Lab 9 models a trunk.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
160

## Slide 161
OBJ 2.2 · SWITCHING TECHNOLOGIES
Access Ports vs Trunk Ports
Access port
Trunk port
• Carries a single VLAN, untagged
• Connects end devices: PCs, printers, cameras
• switchport mode access + access vlan 10
• Voice VLAN rides alongside, tagged with CoS
• Protect with port security and BPDU guard
• Carries many VLANs between switches/routers
• Every frame tagged 802.1Q except the native VLAN
• switchport mode trunk + allowed vlan list
• Native VLAN must match both ends (not VLAN 1)
• Linux models it as eth0.<id> sub-interfaces
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
161

## Slide 162
OBJ 2.2 · SWITCHING TECHNOLOGIES
Native VLAN, Voice VLAN and VTP
1
Native VLAN
The one VLAN a trunk carries UNTAGGED. Frames arriving untagged on the trunk land here.
2
Mismatch danger
If the two ends disagree on the native VLAN, frames silently leak between VLANs — CDP/LLDP will warn.
3
Best practice
Set the native VLAN to an unused ID (not 1) with no user traffic — blunts VLAN-hopping attacks.
4
Voice VLAN config
switchport voice vlan 20: phone traffic tagged with CoS; the PC behind the phone stays untagged.
5
VTP
Cisco's VLAN Trunking Protocol syncs the VLAN database between switches — convenient, and dangerous if a stale switch joins.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
162

## Slide 163
OBJ 2.2 · SWITCHING TECHNOLOGIES
InterVLAN Routing — Three Designs
1
Why needed
VLANs are separate broadcast domains — without a router, SALES can never reach the printer in OPS.
2
Router-on-a-stick
One router interface split into 802.1Q subinterfaces (g0/0.10, g0/0.20) — one per VLAN, each that VLAN's gateway.
3
Subinterface config
encapsulation dot1q 10 plus an IP in VLAN 10's subnet — logical interfaces on one trunk cable.
4
SVI
On a Layer 3 switch, 'interface vlan 10' is a virtual routed interface — no external router needed.
5
Layer 3 switch
Routes between SVIs in hardware at wire speed — the standard enterprise design.
6
Which to pick
Router-on-a-stick for labs and small sites (the one cable is the bottleneck); SVIs everywhere else.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
163

## Slide 164
OBJ 2.2 · SWITCHING TECHNOLOGIES
Worked: VLAN + Trunk on Cisco IOS
Reading the config that puts a PC in VLAN 10 and uplinks over a trunk.
Switch(config)# vlan 10
Switch(config-vlan)# name SALES
Switch(config)# interface gi0/1
Switch(config-if)# switchport mode access
Switch(config-if)# switchport access vlan 10
Switch(config)# interface gi0/24
Switch(config-if)# switchport mode trunk
Switch(config-if)# switchport trunk native vlan 99
access vlan 10
End-device ports carry one untagged VLAN; the PC never sees a tag
mode trunk
The uplink carries every VLAN, each frame tagged 802.1Q with its VLAN ID
native vlan 99
Untagged trunk frames fall into the native VLAN — move it off VLAN 1 for security
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
164

## Slide 165
OBJ 2.2 · SWITCHING TECHNOLOGIES
Interface Configuration: Speed & Duplex
1
Speed & duplex
Modern ports autonegotiate 10/100/1000/10G full duplex; hard-coding only one side breaks it.
2
Duplex mismatch
One side full, one half: late collisions, CRC errors, terrible throughput — a classic exam symptom.
3
Autonegotiation rule
Both sides auto, or both sides forced identically — never mixed.
4
Runts & giants
Frames under 64 bytes (runts) or oversize (giants) usually signal duplex, cable or MTU faults.
5
show interface
Errors, drops, and the speed/duplex actually negotiated — first stop for a slow-port complaint.
6
Err-disabled
Violations (port security, BPDU guard) shut the port to err-disabled; it stays down until recovered.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
165

## Slide 166
OBJ 2.2 · SWITCHING TECHNOLOGIES
MTU and Jumbo Frames
1
MTU 1500
The Ethernet default payload size — every hop must handle a packet's size or fragment it.
2
Jumbo frames
MTU up to ~9000 bytes: fewer frames per gigabyte and less CPU — used on storage and backup networks.
3
End-to-end rule
EVERY device in the path (switches and both hosts) must agree on jumbo MTU or traffic mysteriously fails.
4
Fragmentation
Routers fragment oversized IPv4 packets unless DF is set; IPv6 never fragments in transit.
5
Black holes
If DF is set and ICMP 'frag needed' is filtered, big packets vanish silently — Lab 33 reproduces this.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
166

## Slide 167
DOMAIN 2.0 · HANDS-ON
802.1Q VLAN Tagging
LAB 9
Create 802.1Q VLAN sub-interfaces and capture a tagged frame.
Load the 8021q kernel module, create eth0.10 and eth0.20 sub-interfaces each with its own subnet, verify the VLAN IDs with ip -d link, then capture a live tagged frame with tcpdump -e.
YOU'LL BUILD
Two VLAN sub-interfaces on one NIC — a Linux model of a trunk port — plus a captured 802.1Q tag.
TOOLCHAIN
iproute2, 8021q module, tcpdump
DONE WHEN
ip -d link show eth0.10 reports 'vlan id 10', and the tcpdump output shows the 802.1Q tag (vlan 10) in the Ethernet header.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
167

## Slide 168
LAB 9 · PROCESS MAP
How Lab 9 Runs
1
Load the 802.1Q kernel module
modprobe · step 1
2
Create the VLAN 20 sub-interface
ip · step 3
3
Verify the VLAN ID with detailed link
ip · step 5
4
Start a capture that prints Ethernet
tcpdump · step 6
5
Clean up
ip · step 8
THE POINT
Create 802.1Q VLAN sub-interfaces and capture a tagged frame.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
168

## Slide 169
LAB 9 · VERIFY
802.1Q VLAN Tagging
✅ Expected result
ip -d link show eth0.10 reports 'vlan id 10', and the tcpdump output shows the 802.1Q tag (vlan 10) in the Ethernet header.
IF IT DOESN'T WORK
modprobe: module not found
apt update first; the 8021q module ships with standard Ubuntu kernels
No vlan tag in tcpdump output
Capture on the parent eth0 with -e; tags are already stripped on the sub-interface
RTNETLINK: File exists
The sub-interface already exists — ip link del eth0.10, then recreate it
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
169

## Slide 170
OBJ 2.2 · SWITCHING TECHNOLOGIES
Loops, Storms and Spanning Tree
1
The loop problem
Ethernet frames have no TTL — two links between switches and one broadcast circulates forever.
2
Broadcast storm
The loop amplifies every broadcast; CPU and links saturate and the LAN 'melts' until a cable is pulled.
3
MAC flapping
The same source MAC arrives on two ports alternately; the MAC table thrashes and delivery breaks.
4
STP (802.1D)
Switches elect a root bridge and block redundant ports, pruning the mesh into a loop-free logical tree.
5
BPDU
Bridge Protocol Data Units — hello frames exchanged every 2 s to build and maintain the tree.
6
Bridge ID
Priority + MAC; lowest wins root. Set priority so YOUR core is root, not a random access switch.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
170

## Slide 171
OBJ 2.2 · SWITCHING TECHNOLOGIES
How Spanning Tree Converges
1
Elect root bridge
lowest bridge ID wins
2
Pick root ports
cheapest path to root
3
Pick designated ports
one per segment
4
Block the rest
loops broken
WHY IT MATTERS
One logical tree, no loops: a cabling mistake no longer melts the LAN in a broadcast storm — and RSTP re-converges in about a second.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
171

## Slide 172
OBJ 2.2 · SWITCHING TECHNOLOGIES
STP Port States — 802.1D vs RSTP
802.1D state
Learns MACs
Forwards
RSTP (802.1w)
Blocking
No
No
Discarding (alt/backup)
Listening
No
No
Discarding
Learning
Yes
No
Learning
Forwarding
Yes
Yes
Forwarding
WHEN IT MATTERS Legacy STP takes 30-50 s to converge; RSTP cuts it to about a second — always prefer RSTP/MSTP.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
172

## Slide 173
OBJ 2.2 · SWITCHING TECHNOLOGIES
Protecting Switch Ports
1
Port security
Limit which and how many MACs may use an access port; violations err-disable it.
2
BPDU guard
Access ports should never receive BPDUs — if one arrives (rogue switch!), kill the port.
3
Root guard
Stops a downstream switch from hijacking the root role — protects your tree design.
4
Loop guard
Blocks a port that stops hearing BPDUs instead of trusting it — belt and braces against loops.
5
DHCP snooping
The switch tracks legit DHCP servers per port; rogue OFFERs from untrusted ports are dropped.
6
Dynamic ARP inspection
Uses the snooping table to drop spoofed ARP replies — kills on-LAN man-in-the-middle.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
173

## Slide 174
OBJ 2.2 · SWITCHING TECHNOLOGIES
Link Aggregation and LACP
1
Port bonding / aggregation
Bundle 2-8 physical links into one logical port-channel — more bandwidth AND redundancy.
2
LACP (802.3ad / 802.1AX)
The standard negotiation protocol: both ends agree the bundle — mismatches stay down safely.
3
Modes
active/active and active/passive form a channel; passive/passive never negotiates — exam favourite.
4
Hashing, not magic
Each flow hashes onto ONE member link — a single big transfer never exceeds one link's speed.
5
NIC teaming
The server-side twin: bond NICs for redundancy (active-backup) or throughput (802.3ad to the switch).
6
Linux bonding
modprobe bonding mode=802.3ad — /proc/net/bonding/bond0 shows partner and slave state (Lab 10).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
174

## Slide 175
OBJ 2.2 · SWITCHING TECHNOLOGIES
Port Mirroring (SPAN)
1
SPAN / port mirror
The switch copies frames from source ports or a VLAN to a destination port for analysis.
2
Why
Switches deliver frames only to their destination — without a mirror your sniffer sees almost nothing.
3
Setup
Choose the source (port or VLAN; rx, tx or both) and the destination port where Wireshark or an IDS listens.
4
Remote SPAN
RSPAN carries the mirror across a dedicated VLAN to a sniffer on another switch.
5
TAP alternative
A hardware test access point copies traffic passively — no switch CPU load, no drops under load.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
175

## Slide 176
DOMAIN 2.0 · HANDS-ON
Link Aggregation (LACP Bond)
LAB 10
Bundle interfaces into an LACP (802.3ad) bond and inspect its state.
Install ifenslave, load the bonding driver in 802.3ad mode, create bond0, enslave a NIC and read the LACP aggregator, partner MAC and per-slave link state from /proc/net/bonding/bond0.
YOU'LL BUILD
A bond0 interface running LACP with aggregator and slave state visible in /proc/net/bonding/bond0.
TOOLCHAIN
ifenslave, bonding module, iproute2
DONE WHEN
cat /proc/net/bonding/bond0 shows 'Bonding Mode: IEEE 802.3ad Dynamic link aggregation' plus the slave's MII status and aggregator ID.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
176

## Slide 177
LAB 10 · PROCESS MAP
How Lab 10 Runs
1
Install ifenslave
apt · step 1
2
Create the bond interface
ip · step 3
3
Enslave the NIC
ip · step 4
4
Bring up the slave and the bond
ip · step 5
5
Clean up
ip · step 7
THE POINT
Bundle interfaces into an LACP (802.3ad) bond and inspect its state.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
177

## Slide 178
LAB 10 · VERIFY
Link Aggregation (LACP Bond)
✅ Expected result
cat /proc/net/bonding/bond0 shows 'Bonding Mode: IEEE 802.3ad Dynamic link aggregation' plus the slave's MII status and aggregator ID.
IF IT DOESN'T WORK
Playground disconnects
Enslaving the only NIC drops Killercoda — rebuild the playground or use a multi-NIC VM
bond0 shows no partner MAC
The peer must speak LACP too; without an 802.3ad partner the aggregator stays down
Cannot enslave eth0
Set the interface down first (ip link set eth0 down), then set master bond0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
178

## Slide 179
OBJ 1.2 · NETWORK APPLIANCES
Quality of Service and Traffic Shaping
1
Why QoS
When a link congests something must be dropped — QoS decides what suffers so voice and video do not.
2
Classify & mark
Traffic is identified and marked (802.1p CoS at L2, DSCP at L3) so every hop honours the same policy.
3
Queuing
Priority queues drain first — a VoIP packet jumps the line ahead of a backup transfer.
4
Traffic shaping
Buffers and smooths traffic to a target rate; policing simply drops the excess.
5
SOHO QoS
Home routers offer simple per-protocol or per-device priorities — the same idea, one checkbox.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
179

## Slide 180
OBJ 1.2 · NETWORK APPLIANCES
IDS vs IPS
IDS — detect and alert
IPS — detect and act
• Out-of-band: watches a COPY (port mirror or TAP)
• Detects and alerts; humans respond
• Cannot block, so it cannot break traffic
• False positives cost analyst time only
• Example: Suricata in IDS mode (Lab 26)
• In-band (inline): real traffic flows through it
• Drops or resets malicious flows automatically
• A false positive can block good traffic
• Needs throughput matching the link
• A firewall filters, an IDS notifies, an IPS acts
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
180

## Slide 181
OBJ 1.2 · NETWORK APPLIANCES
Proxy Servers — Three Flavours
Forward proxy
• Sits in front of clients
• Caching and content filtering
• Hides clients from servers
• Common in schools and offices
Transparent proxy
• No client configuration
• Must sit inline in the path
• Intercepts traffic silently
• Often at the network edge
Reverse proxy
• Sits in front of servers
• Load balancing plus caching
• TLS offload / crypto acceleration
• Absorbs DoS attacks
• Hides the server fleet
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
181

## Slide 182
OBJ 1.2 · NETWORK APPLIANCES
Load Balancing
1
What it does
Spreads client requests across a pool of servers — capacity AND availability behind one VIP.
2
Round robin
Each request goes to the next server in the list; DNS round robin is the zero-hardware version.
3
Least connections
Smarter schedulers send work to the server that is actually least busy right now.
4
Health checks
Dead servers are pulled from rotation automatically — users never see the failure.
5
Persistence
Sticky sessions pin a client to one backend when the application keeps state locally.
6
Where it lives
Dedicated appliances, reverse proxies (nginx, HAProxy) or cloud load-balancer services.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
182

## Slide 183
OBJ 1.2 · NETWORK APPLIANCES
Device Placement — Edge to Core
1
Screened subnet (DMZ)
Public-facing servers live in an isolated zone between two firewall layers — a breach there stays there.
2
Edge firewall
Faces the Internet: allows unsolicited traffic only to published screened-subnet services.
3
Interior firewall
Second layer between the DMZ and LAN — nothing from the DMZ initiates into the private network.
4
Inline IPS
Sits in-band just inside the edge so it can act on attacks before they spread.
5
Internal segmentation
Extra firewalls and ACLs around HR, finance and OT — blast-radius control inside the domain.
6
SOHO 'DMZ host'
A home router's DMZ setting forwards ALL ports to one host — outside protection, not a real DMZ.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
183

## Slide 184
OBJ 2.3 · WIRELESS DEVICES
No cables. Same rules.
Wireless swaps copper for radio — but VLANs, DHCP, security and troubleshooting all still apply on the far side of the access point.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
184

## Slide 185
OBJ 2.3 · WIRELESS DEVICES
802.11 Building Blocks
1
Access point (WAP)
A Layer 2 bridge between 802.11 radio and 802.3 Ethernet — wireless clients join the wired LAN through it.
2
SSID
The network name a human selects — a word or phrase up to 32 bytes.
3
BSSID
The MAC address of one AP's radio — the identifier your NIC actually associates with.
4
ESSID
Several APs sharing one SSID form an Extended Service Set — clients roam between BSSIDs seamlessly.
5
CSMA/CA
Radios cannot detect collisions, so they AVOID them: listen first, back off randomly, then transmit.
6
Half duplex on air
Only one station talks per channel at a time — airtime is the shared resource to protect.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
185

## Slide 186
OBJ 2.3 · WIRELESS DEVICES
Wireless Network Types
1
Infrastructure
Clients talk through an AP wired into the LAN — the normal enterprise mode.
2
Ad hoc (IBSS)
Client-to-client with no AP — a quick file share between two laptops, nothing more.
3
Mesh
APs relay traffic wirelessly to each other — coverage without pulling cable to every node.
4
Point-to-point
Two directional antennas bridge buildings — a wireless leased line.
5
Wireless bridge
Joins two wired segments over radio — often the role at each end of a point-to-point link.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
186

## Slide 187
OBJ 2.3 · WIRELESS DEVICES
802.11 Standards at a Glance
Standard
Wi-Fi name
Band
Max PHY rate
802.11b
-
2.4 GHz
11 Mbps
802.11a
-
5 GHz
54 Mbps
802.11g
-
2.4 GHz
54 Mbps
802.11n
Wi-Fi 4
2.4 / 5 GHz
600 Mbps (MIMO)
802.11ac
Wi-Fi 5
5 GHz
6.9 Gbps (MU-MIMO)
802.11ax
Wi-Fi 6 / 6E
2.4 / 5 / 6 GHz
9.6 Gbps (OFDMA)
WHEN IT MATTERS n introduced MIMO; ac added MU-MIMO; ax adds OFDMA and, as 6E, the 6 GHz band.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
187

## Slide 188
OBJ 2.3 · WIRELESS DEVICES
Wireless Ceilings by Generation
Chart: 
| 802.11b | 802.11a/g | 802.11n | 802.11ac | 802.11ax
Max PHY rate (Mbps) | 11 | 54 | 600 | 6933 | 9608
WHAT THE DATA SHOWS
Each generation multiplies the ceiling — nearly 900x from b to ax. Real throughput is roughly half the PHY rate; airtime and interference decide the rest.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
188

## Slide 189
OBJ 2.3 · WIRELESS DEVICES
Frequency Bands: 2.4 vs 5 vs 6 GHz
Band
Clean channels
Widths
Notes
2.4 GHz
1, 6, 11 only
20 MHz
Long range; congested
5 GHz
36-165 (DFS mid)
20/40/80/160
More channels; radar DFS
6 GHz (6E)
PSC channels
20-160+
WPA3 mandatory; short range
WHEN IT MATTERS Lower frequency travels further and penetrates better; higher frequency carries more data over less distance.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
189

## Slide 190
OBJ 2.3 · WIRELESS DEVICES
Channels and Channel Width
1
Channel
The slice of the band an AP transmits on — neighbouring APs must use different, non-overlapping channels.
2
2.4 GHz reality
Channels overlap heavily; only 1, 6 and 11 are clean of each other — the classic honeycomb plan.
3
Channel width
20 MHz standard; 40/80/160 MHz bond channels for speed but eat spectrum and invite interference.
4
DFS
Dynamic Frequency Selection: mid-band 5 GHz shares with radar — the AP must vacate on detection.
5
6 GHz PSC
Preferred Scanning Channels help clients discover 6E networks in the huge new band.
6
Wider is not better
In dense offices many 20/40 MHz cells beat a few 160 MHz cells — airtime reuse wins.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
190

## Slide 191
OBJ 2.3 · WIRELESS DEVICES
Antenna Types and Patterns
Antenna
Pattern
Gain
Typical use
Omni / dipole
360-degree doughnut
Low
Ceiling APs, open offices
Patch
Half-sphere from a wall
Medium
Exterior walls, corridors
Yagi
Narrow directional beam
High
Long halls, building links
Parabolic
Very narrow beam
Very high
Point-to-point bridges
WHEN IT MATTERS Gain (dBi) trades coverage width for reach — match the radiation pattern to the room, not the other way round.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
191

## Slide 192
OBJ 2.3 · WIRELESS DEVICES
Power over Ethernet Standards
Standard
Name
Power (PSE)
Typically powers
802.3af
PoE
15.4 W
VoIP phones, basic WAPs
802.3at
PoE+
30 W
Wi-Fi 6 WAPs, PTZ cameras
802.3bt
PoE++
60-90 W
Displays, laptops, kiosks
WHEN IT MATTERS Power comes from a PoE switch or a midspan injector — no mains socket needed at the AP's ceiling mount.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
192

## Slide 193
OBJ 2.3 · WIRELESS DEVICES
Wireless Security: WEP to WPA3
Mode
Encryption
Key exchange
Notes
WEP
RC4, static keys
None
Broken — never use
WPA
TKIP (RC4)
PSK 4-way
Stopgap; deprecated
WPA2-PSK
AES-CCMP
4-way handshake
PMKID/offline attacks
WPA2-Enterprise
AES-CCMP
802.1X / RADIUS
Per-user credentials
WPA3-SAE
AES-CCMP/GCMP
SAE (Dragonfly)
Forward secrecy
WPA3-Ent 192-bit
GCMP-256
802.1X
Government grade
WHEN IT MATTERS Deploy WPA3 where clients allow; WPA2/WPA3 transition mode bridges the gap. Wi-Fi 6E mandates WPA3.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
193

## Slide 194
OBJ 2.3 · WIRELESS DEVICES
PSK or Enterprise Authentication?
Do users need individual credentials and revocation?
YES — WPA3-ENTERPRISE
802.1X with RADIUS (EAP-TLS or PEAP): per-user authentication, per-session keys, revoke one account without touching the rest.
NO — WPA3-SAE (PSK)
One shared passphrase, zero infrastructure. SAE resists offline guessing — but anyone with the phrase gets in; rotate on staff exit.
Guest traffic belongs on its own SSID with client isolation and a captive portal.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
194

## Slide 195
OBJ 2.3 · WIRELESS DEVICES
802.1X — Who Does What
1
Supplicant
The client software asking to join — built into every modern OS.
2
Authenticator
The AP (or switch) that relays credentials; it never sees the password itself.
3
RADIUS server
Checks credentials against AD/LDAP and returns accept or reject plus keying material (UDP 1812).
4
EAP methods
EAP-TLS (certificates, strongest) and PEAP/MS-CHAPv2 (username + password) are the common choices.
5
Per-session keys
Every user gets unique encryption keys — one compromised laptop never exposes others' traffic.
6
Same on wires
802.1X also gates Ethernet ports — network access control for the whole access layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
195

## Slide 196
OBJ 2.3 · WIRELESS DEVICES
Guest Networks and Captive Portals
1
Separate SSID
Guests get their own SSID mapped to its own VLAN — never the corporate network.
2
Captive portal
A web page intercepts the first request: accept terms, enter a voucher or log in before Internet access.
3
Client isolation
Guests cannot see each other's devices — blocks lateral snooping inside the hotspot.
4
Internet-only ACL
The guest VLAN routes to the Internet and NOTHING internal — enforced at the firewall.
5
Bandwidth limits
Rate-limit the guest SSID so visitors cannot starve production airtime.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
196

## Slide 197
OBJ 2.3 · WIRELESS DEVICES
Hardening the WLAN
1
Change defaults
Default admin credentials and IPs are in every manual online — the first thing an attacker tries.
2
Disable WPS
The 8-digit PIN brute-forces in hours; turn WPS off everywhere.
3
Management access
Disable remote/WAN management; administer APs from a wired admin VLAN over HTTPS or SSH.
4
SSID hiding & MAC filters
Both are trivially sniffed — they stop only casual users; treat as tidiness, not security.
5
Firmware updates
AP vulnerabilities (KRACK and friends) are fixed in firmware — patch APs like servers.
6
Strong passphrase
For PSK networks a long random passphrase resists offline cracking; rotate on staff exit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
197

## Slide 198
OBJ 2.3 · WIRELESS DEVICES
Threats to Your Wireless Network
1
Rogue AP
An unauthorised AP on your LAN — often an employee's convenience — punches a hole in the perimeter.
2
Evil twin
An attacker clones your SSID with a stronger signal; victims associate and hand over their traffic.
3
Deauth attack
Spoofed deauthentication frames kick clients off — DoS, or bait for the evil twin. 802.11w (PMF) blocks it.
4
Jamming
Illegal RF noise floods the band — nothing associates until the source is found with a spectrum analyser.
5
Wardriving
Attackers map weak networks in bulk — WPA3 and monitoring make you a poor target.
6
WIPS
Wireless IPS sensors detect rogues, twins and deauth floods — and can contain them automatically.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
198

## Slide 199
OBJ 2.3 · WIRELESS DEVICES
Enterprise Wireless Architecture
1
Autonomous AP
Each AP configured on its own — fine for a handful, unmanageable at fifty.
2
Lightweight AP
A thin AP pulls config and firmware from a controller and tunnels traffic to it (CAPWAP).
3
WLC
The Wireless LAN Controller pushes SSIDs, channels, power and security to every AP centrally.
4
Cloud-managed
Controller-in-the-cloud (Meraki-style) — the same model with a dashboard instead of an on-prem box.
5
Roaming
Controllers coordinate fast handoff (802.11r) so a VoIP call survives a walk between APs.
6
RF management
The controller auto-tunes channels and power across APs to minimise co-channel interference.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
199

## Slide 200
OBJ 2.3 · WIRELESS DEVICES
Site Surveys and AP Placement
1
Site survey
Walk the space with a Wi-Fi analyser: map coverage, noise and neighbours BEFORE and after installing.
2
Interference
Microwaves, wireless peripherals, neighbouring APs — 2.4 GHz suffers most; prefer 5 or 6 GHz.
3
Absorption & reflection
Concrete, metal and water absorb or bounce signal; glass reflects — placement is physics.
4
SNR
Signal-to-noise ratio matters more than raw signal: aim for 25 dB or better, more for voice.
5
AP placement
Central, ceiling-mounted, away from metal; match the antenna pattern to the room's shape.
6
Test and iterate
Antenna placement is part art — measure, adjust, re-measure. Lab 11 is your first survey.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
200

## Slide 201
DOMAIN 2.0 · HANDS-ON
Wireless Concepts and Channel Survey
LAB 11
Survey nearby wireless networks and map channels, bands and security modes.
Use iw on a wireless laptop (or WiFi Analyzer / Wireless Diagnostics) to scan nearby APs, recording each SSID's channel, signal and security mode, then map channels to bands and compare WEP through WPA3.
YOU'LL BUILD
A site-survey table of nearby APs: SSID, band, channel, signal (dBm) and security mode.
TOOLCHAIN
iw, wavemon, WiFi Analyzer (Windows), Wireless Diagnostics (macOS)
DONE WHEN
The scan output lists SSIDs with freq, signal and RSN/WPA details, and you can explain why 1, 6 and 11 are the only non-overlapping 2.4 GHz channels.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
201

## Slide 202
LAB 11 · PROCESS MAP
How Lab 11 Runs
1
On a wireless laptop
iw · step 1
2
Scan nearby APs for SSID
iw · step 2
3
Record each AP
Step 3 of 6
4
Compare security modes from WEP to
Step 5 of 6
5
Quiz
Step 6 of 6
THE POINT
Survey nearby wireless networks and map channels, bands and security modes.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
202

## Slide 203
LAB 11 · VERIFY
Wireless Concepts and Channel Survey
✅ Expected result
The scan output lists SSIDs with freq, signal and RSN/WPA details, and you can explain why 1, 6 and 11 are the only non-overlapping 2.4 GHz channels.
IF IT DOESN'T WORK
iw: command not found
apt install iw wavemon on Linux; on Windows/macOS use the free analyzer apps instead
Scan returns nothing
Run as root, check the interface name with iw dev, and rfkill unblock wifi
No 6 GHz networks visible
The adapter must support Wi-Fi 6E; older NICs only report 2.4/5 GHz BSSs
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
203

## Slide 204
OBJ 2.1 · NAT & PAT
NAT Comes in Three Flavours
Static NAT (SNAT)
• One private IP to one public IP
• The mapping never changes
• Publishes inside servers
• Wastes public addresses
Dynamic NAT
• Pool of public addresses
• First come, first mapped
• Pool exhausts under load
• Still 1-to-1 while held
PAT / NAT overload
• Many private to ONE public IP
• Tracks flows by source port
• What every SOHO router does
• Linux: iptables MASQUERADE
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
204

## Slide 205
OBJ 2.1 · NAT & PAT
How PAT Translates a Flow
1
Host sends packet
src 10.1.1.2:41712
2
Router rewrites
src = public IP:port
3
Track in table
conntrack entry
4
Reply returns
dst = public:port
5
Reverse lookup
back to 10.1.1.2
WHY IT MATTERS
Thousands of private hosts share one public IPv4 address — PAT is why IPv4 survives, and why unsolicited inbound needs port forwarding.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
205

## Slide 206
OBJ 2.1 · NAT & PAT
Port Forwarding, Triggering and DMZ
1
Port forwarding
The router maps inbound public:port to a chosen inside host:port — how a NATed server goes public.
2
Port range forwarding
Forward a whole span of ports at once for applications that need many.
3
Port triggering
An outbound connection on the trigger port opens a temporary inbound port — classic for active FTP.
4
SOHO DMZ host
Forwards EVERYTHING to one host — that machine now lives outside the router's protection. Avoid.
5
NAT and servers
Without a forward rule PAT has no mapping for unsolicited inbound — connections die at the router.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
206

## Slide 207
OBJ 2.1 · NAT & PAT
Worked: Reading a MASQUERADE Rule
The one iptables line behind Lab 12, and the conntrack evidence it leaves.
iptables -t nat -A POSTROUTING \
-s 10.1.1.0/24 -o eth0 -j MASQUERADE
# live translation table
conntrack -L | head -2
tcp ... src=10.1.1.2 dst=8.8.8.8 sport=41712
src=8.8.8.8 dst=<public-ip> dport=41712
POSTROUTING
Source NAT happens after the routing decision, just before the packet leaves eth0
MASQUERADE
Dynamic SNAT that always uses the outgoing interface's current address — ideal for DHCP WANs
sport tracking
PAT maps each inside flow to a unique public port so replies find their way back
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
207

## Slide 208
DOMAIN 2.0 · HANDS-ON
NAT and PAT with iptables
LAB 12
Configure PAT with iptables MASQUERADE and verify live translations in conntrack.
Rebuild a namespace client behind the host, enable forwarding, add a MASQUERADE rule on eth0, prove the source address is rewritten with curl ifconfig.me, and inspect the live translation table with conntrack -L.
YOU'LL BUILD
A namespace reaching the Internet through the host's IP — many-to-one PAT exactly as a SOHO router does it.
TOOLCHAIN
iptables, conntrack, iproute2, curl
DONE WHEN
curl -s ifconfig.me from inside the namespace prints the host's public IP, not 10.1.1.2, and conntrack -L shows the translated flow with its ports.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
208

## Slide 209
LAB 12 · PROCESS MAP
How Lab 12 Runs
1
Create namespace a wired to the host
ip · step 1
2
Enable IP forwarding on the host
sysctl · step 3
3
Add the MASQUERADE
iptables · step 4
4
Test
ip · step 5
5
Clean up
iptables · step 7
THE POINT
Configure PAT with iptables MASQUERADE and verify live translations in conntrack.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
209

## Slide 210
LAB 12 · VERIFY
NAT and PAT with iptables
✅ Expected result
curl -s ifconfig.me from inside the namespace prints the host's public IP, not 10.1.1.2, and conntrack -L shows the translated flow with its ports.
IF IT DOESN'T WORK
Ping 8.8.8.8 fails from namespace
Check ip_forward=1 and that the default route inside a points at 10.1.1.1
curl still shows 10.1.1.2
MASQUERADE rule missing or wrong -o interface; list with iptables -t nat -L -v
conntrack: command not found
apt install -y conntrack, then rerun conntrack -L
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
210

## Slide 211
OBJ 3.5 · REMOTE ACCESS
IP Tunneling and VPNs
1
Tunneling
Encapsulate one protocol inside another — usually to carry unencrypted traffic through an encrypted channel.
2
VPN
A tunnel that makes a remote machine or site behave as part of the local network.
3
Client-to-site
A laptop VPNs into HQ — remote-access VPN terminated on a concentrator or headend at the edge.
4
Site-to-site
Two offices' routers keep a permanent tunnel — one logical network across the Internet.
5
Protocols
IPsec/IKEv2 and WireGuard dominate today; OpenVPN where TLS-friendliness matters; GRE tunnels without encryption.
6
Split vs full tunnel
Full sends ALL traffic via HQ; split sends only corporate subnets — bandwidth vs inspection trade-off.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
211

## Slide 212
WAN CONNECTIVITY
WAN Technologies Compared
Technology
Medium
Speed class
Notes
DSL / VDSL
Phone line (RJ-11)
To ~100 Mbps
Asymmetric; needs filters
Cable (DOCSIS)
Coax, F-type
To ~1 Gbps
Shared neighbourhood node
Fiber / Metro
Single-mode fiber
1-100 Gbps
DWDM multiplies capacity
Satellite
RG-6 to dish
25-220 Mbps
High latency (GEO)
Cellular 5G
Licensed radio
0.1-10 Gbps
Low/mid/high bands
WHEN IT MATTERS Match the technology to latency and symmetry needs, not just headline speed — satellite latency kills VoIP.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
212

## Slide 213
WAN CONNECTIVITY
MPLS, SD-WAN and Metro Ethernet
1
MPLS
Provider routers switch on short labels instead of IP lookups — predictable performance, traffic engineering.
2
Label edge
The provider edge pushes and pops labels; your traffic rides a private label-switched path, not the raw Internet.
3
SD-WAN
Software steers many transports (MPLS + broadband + LTE) as one WAN — app-aware paths, central policy.
4
Why SD-WAN won
Commodity Internet links at a fraction of MPLS cost, with encryption and failover built in.
5
Metro Ethernet
Carrier Ethernet across a city — a simple Layer 2 handoff at each site.
6
mGRE / DMVPN
Dynamic multipoint tunnels build a site mesh from one hub configuration.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
213

## Slide 214
OBJ 3.5 · REMOTE ACCESS
Remote Access Tools
1
RDP
Microsoft Remote Desktop Protocol, TCP 3389 — a full graphical session; never expose it raw to the Internet.
2
VNC
Cross-platform desktop sharing on TCP 5900 — weakly protected alone, so tunnel it.
3
SSH
Secure Shell, TCP 22 — encrypted CLI, file transfer (SFTP) and port tunnels; keys beat passwords (Lab 23).
4
Jump box / bastion
One hardened, audited entry host placed in front of all management interfaces.
5
In-band vs out-of-band
Manage over the production network, or over a dedicated path or console that survives outages.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
214

## Slide 215
OBJ 1.6 · NETWORK SERVICES
DORA — How a Lease Happens
1
Discover
client broadcast
2
Offer
server proposes IP
3
Request
client accepts one
4
Acknowledge
lease confirmed
WHY IT MATTERS
The first messages are broadcast because the client has no address yet — which is why remote subnets need a DHCP relay (IP helper).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
215

## Slide 216
OBJ 1.6 · NETWORK SERVICES
Designing a DHCP Scope
1
Scope / pool
The subnet plus the range of leasable addresses — keep infrastructure IPs outside the range.
2
Options
Alongside the lease the server hands out router (gateway), DNS servers and domain — one wrong option breaks every client.
3
Lease times
Short leases (minutes) suit guest churn; long leases (days) suit stable LANs — Lab 13 uses 600/7200 s.
4
Reservations
Pin a MAC to a fixed IP centrally — printers get stable addresses without static config.
5
Relay / IP helper
DHCP broadcasts do not cross routers; a relay on each subnet unicasts to the central server.
6
Rogue DHCP
A second server handing out bad gateways breaks a subnet — DHCP snooping is the defence.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
216

## Slide 217
OBJ 1.6 · NETWORK SERVICES
Worked: Reading dhcpd.conf
The exact scope Lab 13 serves on dum0 — every line has a job.
default-lease-time 600;
max-lease-time 7200;
authoritative;
subnet 10.50.0.0 netmask 255.255.255.0 {
range 10.50.0.100 10.50.0.150;
option routers 10.50.0.1;
option domain-name-servers 1.1.1.1, 8.8.8.8;
option broadcast-address 10.50.0.255;
}
range
The pool the server may lease from — keep static servers outside it
option routers
Becomes each client's default gateway; a wrong value strands every client
authoritative
The server NAKs bogus lease requests instead of staying silent — one authority per subnet
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
217

## Slide 218
DOMAIN 2.0 · HANDS-ON
DHCP Server with isc-dhcp-server
LAB 13
Configure isc-dhcp-server to lease addresses on a private subnet.
Install isc-dhcp-server, create a dummy interface at 10.50.0.1/24, write a scope with range, router, DNS and lease-time options, bind the daemon to dum0 only, start it and inspect the leases file.
YOU'LL BUILD
A running authoritative DHCP server scoped to 10.50.0.100-150 on dum0, leaving eth0 untouched.
TOOLCHAIN
isc-dhcp-server, iproute2, systemd
DONE WHEN
systemctl status isc-dhcp-server shows active (running) bound to dum0, and /var/lib/dhcp/dhcpd.leases exists, ready to record client leases.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
218

## Slide 219
LAB 13 · PROCESS MAP
How Lab 13 Runs
1
Install the ISC DHCP server
apt · step 1
2
Bring the dummy interface up
ip · step 3
3
Bind the daemon to dum0 only
sed · step 5
4
Restart and check the service
systemctl · step 6
5
Clean up
systemctl · step 8
THE POINT
Configure isc-dhcp-server to lease addresses on a private subnet.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
219

## Slide 220
LAB 13 · VERIFY
DHCP Server with isc-dhcp-server
✅ Expected result
systemctl status isc-dhcp-server shows active (running) bound to dum0, and /var/lib/dhcp/dhcpd.leases exists, ready to record client leases.
IF IT DOESN'T WORK
Service fails to start
Syntax-check with dhcpd -t; every option line in dhcpd.conf must end with a semicolon
Daemon not listening on dum0
Confirm INTERFACESv4="dum0" in /etc/default/isc-dhcp-server, then restart
Leases file is empty
Normal until a client DISCOVERs on 10.50.0.0/24; leases are appended as granted
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
220

## Slide 221
OBJ 1.6 · NETWORK SERVICES
Running Authoritative DNS
1
Authoritative server
Holds the zone's actual records and answers with authority — what Lab 14 builds with BIND9.
2
Recursive resolver
Chases referrals from root to TLD to authoritative on behalf of clients — the other half of DNS.
3
Zone
A delegated slice of the namespace (lab.local) stored as resource records in a zone file.
4
Primary / secondary
The primary holds the writable zone; secondaries pull copies (AXFR) whenever the serial rises.
5
named.conf
BIND's configuration: each zone block names the zone, its type (master/slave) and its file.
6
named-checkzone
Validate syntax BEFORE reloading — a broken zone otherwise takes your whole domain offline.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
221

## Slide 222
OBJ 1.6 · NETWORK SERVICES
Anatomy of the SOA Record
SOA field
Lab 14 value
Meaning
Serial
2026051001
Zone version — bump on every edit
Refresh
3600
Secondary re-check interval (s)
Retry
1800
Re-poll after a failed refresh
Expire
604800
Secondary gives up after this
Minimum
86400
Negative-caching TTL
WHEN IT MATTERS Forget to bump the serial and your secondaries keep serving the OLD zone — a classic silent DNS failure.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
222

## Slide 223
OBJ 1.6 · NETWORK SERVICES
Worked: Reading a BIND Zone File
The db.lab.local file from Lab 14, line by line.
$TTL 86400
@ IN SOA ns.lab.local. admin.lab.local. (
2026051001 ; serial
3600 1800 604800 86400 )
@ IN NS ns.lab.local.
ns IN A 127.0.0.1
www IN A 10.0.0.10
@ IN MX 10 mail.lab.local.
Trailing dot
ns.lab.local. is absolute; omit the dot and BIND appends the zone name again
Serial
Secondaries only transfer the zone when the serial increases — bump it on every edit
MX 10
The preference number — lower wins when several mail exchangers exist
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
223

## Slide 224
DOMAIN 2.0 · HANDS-ON
Authoritative DNS with BIND9
LAB 14
Host an authoritative DNS zone in BIND9 and query it with dig.
Install bind9, write a zone file for lab.local with SOA, NS, A and MX records, register the zone in named.conf.local, validate the syntax with named-checkzone and query your own server with dig @127.0.0.1.
YOU'LL BUILD
A local BIND9 server answering authoritatively for lab.local, with validated zone syntax.
TOOLCHAIN
bind9, dnsutils (dig), named-checkzone
DONE WHEN
dig @127.0.0.1 www.lab.local returns A 10.0.0.10 with the aa (authoritative answer) flag, and dig @127.0.0.1 MX lab.local returns 'MX 10 mail.lab.local.'
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
224

## Slide 225
LAB 14 · PROCESS MAP
How Lab 14 Runs
1
Install BIND9 and dig
apt · step 1
2
Register zone lab.local as type master
cat · step 3
3
Validate the zone syntax before
named-checkzone · step 4
4
Restart BIND
systemctl · step 5
5
Clean up
systemctl · step 7
THE POINT
Host an authoritative DNS zone in BIND9 and query it with dig.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
225

## Slide 226
LAB 14 · VERIFY
Authoritative DNS with BIND9
✅ Expected result
dig @127.0.0.1 www.lab.local returns A 10.0.0.10 with the aa (authoritative answer) flag, and dig @127.0.0.1 MX lab.local returns 'MX 10 mail.lab.local.'
IF IT DOESN'T WORK
named-checkzone reports errors
Check the SOA parentheses and the trailing dots on FQDNs like ns.lab.local.
dig times out
BIND is not running — systemctl status bind9; verify config with named-checkconf
SERVFAIL for lab.local
The zone failed to load; journalctl -u named shows the parse error — fix, restart
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
226

## Slide 227
OBJ 2.4 · PHYSICAL INSTALLATIONS
MDF, IDF and the Rack
1
MDF
Main Distribution Frame — the building's core room: WAN handoff, core switches, routers, servers.
2
IDF
Intermediate Distribution Frames per floor or area — access switches within 90 m of their users.
3
Demarc
Where the carrier's responsibility ends and yours begins — the demarcation point, usually in the MDF.
4
Rack units
Equipment is measured in U (1U = 1.75 in); plan space, airflow and growth before install day.
5
Patch panels
Horizontal runs terminate on panels; short patch leads jump to switch ports — never re-terminate walls.
6
Locked & dedicated
Distribution rooms are locked and badge-controlled, free of storage and water pipes — security at layer 0.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
227

## Slide 228
OBJ 2.4 · PHYSICAL INSTALLATIONS
Cable Management Done Right
1
Structured pathways
Ladder racks, trays and vertical managers — no cable stress, no spaghetti, airflow preserved.
2
Label everything
Both ends of every cable, every panel port, every drop — future-you troubleshoots at 2 a.m.
3
Bend radius & slack
Respect the minimum bend radius (especially fiber); service loops allow moves without re-pulls.
4
Separation
Keep UTP away from fluorescent lights, motors and power runs — EMI is a Layer 1 gremlin.
5
Velcro, not zip ties
Over-tightened ties crush pairs and change cable geometry — velcro wraps are the standard.
6
Documentation
Port maps and as-built diagrams live with the rack — updated with every change.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
228

## Slide 229
OBJ 2.4 · PHYSICAL INSTALLATIONS
Power: UPS, PDU, Load and Voltage
1
UPS
The battery bridge over outages and brownouts — line-interactive, or online double-conversion for clean power.
2
Runtime vs capacity
Size the UPS in VA/watts for the load, then check minutes of runtime at that load — both matter.
3
PDU
Rack power distribution — metered and switched PDUs report draw and can remote-cycle an outlet.
4
Dual feeds
Dual power supplies on separate circuits and PDUs (A + B feeds) survive a tripped breaker.
5
Voltage & circuits
Match equipment to the circuit (230 V in Singapore); dedicated circuits per rack, no daisy-chained strips.
6
Generator
For real continuity a generator backs the UPS: battery rides the seconds, diesel rides the hours.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
229

## Slide 230
OBJ 2.4 · PHYSICAL INSTALLATIONS
Environment: HVAC, Humidity, Fire
1
HVAC
Racks emit constant heat; dedicated cooling with hot/cold-aisle layouts keeps intake air cold.
2
Temperature
Target roughly 18-27 C at the equipment intake; monitor per rack, not per room.
3
Humidity
40-60% relative humidity — too dry invites static discharge, too damp invites condensation and corrosion.
4
Fire suppression
Clean-agent gas (FM-200, Novec) or pre-action sprinklers — water and live electronics do not mix.
5
Sensors
Temperature, humidity, leak and door sensors feed monitoring — alerts before hardware cooks.
6
Grounding
Bond racks to earth ground and use ESD straps on boards — invisible damage kills gear later.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
230

## Slide 231
OBJ 2.4 · PHYSICAL INSTALLATIONS
A Physical Installation, Start to Finish
1
Site survey and requirements
▶
2
Design: MDF/IDF, pathways, power
▶
3
Rack, label and cable
▶
4
Test and validate every link
▶
5
Document and baseline
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
231

## Slide 232
NEXT: NETWORK OPERATIONS
You built the network. Now run it.
Domain 3 turns to operations: monitoring, documentation and the disaster-recovery numbers that keep what you just built alive.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
232

## Slide 233
DOMAIN 2.0 RECAP
Recap — Network Implementation
• You can now: Build a two-subnet topology and route between them with static routes.
• You can now: Create 802.1Q VLAN sub-interfaces and capture a tagged frame.
• You can now: Bundle interfaces into an LACP (802.3ad) bond and inspect its state.
• You can now: Survey nearby wireless networks and map channels, bands and security modes.
• You can now: Configure PAT with iptables MASQUERADE and verify live translations in conntrack.
• You can now: Configure isc-dhcp-server to lease addresses on a private subnet.
• You can now: Host an authoritative DNS zone in BIND9 and query it with dig.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
233

## Slide 234
DOMAIN 3.0 · 19% OF THE EXAM
Network Operations
Documentation · life-cycle · change & configuration management · monitoring · DR · network services · access & management
3.0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
234

## Slide 235
WHAT YOU'LL DO
Hands-On Labs — Network Operations
Labs 15–16
• SNMP Monitoring
• NetFlow Analysis with nfdump
Labs 17–18
• Centralised Logging with Rsyslog
• Time Synchronisation with Chrony
Labs 19–20
• Configuration Backup with Git
• Performance Baseline with iperf3
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
235

## Slide 236
19% OF THE EXAM
Domain 3 — Network Operations.
19% of the N10-009 exam: documentation, monitoring, disaster recovery, the network services everyone depends on, and secure access to your own infrastructure.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
236

## Slide 237
N10-009 · DOMAIN 3
Domain 3 Roadmap
1
OBJ 3.1 — Documentation & processes
Physical and logical diagrams, rack diagrams, IPAM, asset inventory, life-cycle, change and configuration management.
2
OBJ 3.2 — Network monitoring
SNMP, flow data, packet capture, baselines, log aggregation and SIEM — knowing what the network is doing.
3
OBJ 3.3 — Disaster recovery
RPO/RTO, MTTR/MTBF, cold/warm/hot sites, active-active vs active-passive, and testing the plan.
4
OBJ 3.4 — Network services
DHCP, SLAAC, DNS and time services (NTP, PTP, NTS) — the quiet plumbing every network leans on.
5
OBJ 3.5 — Access & management
Site-to-site and client VPNs, SSH, APIs, console, out-of-band and jump boxes.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
237

## Slide 238
OBJ 3.1 · DOCUMENTATION
Documentation is the network's memory.
The network that exists is the one in production; the network you can repair at 3 a.m. is the one in the documentation. Keeping them identical is an operations discipline.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
238

## Slide 239
OBJ 3.1 · DOCUMENTATION
Documenting the Network
1
Physical diagram
Where things ARE — rooms, racks, cable runs, patch panels. Follows the actual hardware and wiring.
2
Logical diagram
How data FLOWS — subnets, VLANs, routing paths, firewall zones. Independent of physical location.
3
Rack diagram
Elevation view of one rack: every rack unit numbered, each device drawn at its mounted position.
4
Cable map
Maps each patch-panel port to its wall jack and switch port so a tech can trace any link in seconds.
5
Asset inventory
Hardware, software, licensing and warranty per device — what you own, what it runs, when support ends.
6
IPAM
IP address management — tracks every subnet, assignment and DHCP scope so no address is allocated twice.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
239

## Slide 240
OBJ 3.1 · DOCUMENTATION
Physical vs Logical Diagrams
Physical (Layer 1)
Logical (Layer 2/3)
• Rooms, racks, cable runs, patch panels
• MDF and IDF locations and wiring
• Follows the copper and the fibre
• Used for moves, adds, changes, repairs
• Subnets, VLANs and IP addressing
• Routing paths and firewall zones
• Follows the traffic flow
• Used for design and troubleshooting
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
240

## Slide 241
OBJ 3.1 · DOCUMENTATION
Network Diagrams by Layer
Layer 1 — physical
• Cables, ports and patch panels
• Rack elevations and RU positions
• Media types and cable labels
• TAP and mirror points marked
Layer 2 — switching
• Switches, VLANs and trunks
• STP topology and port channels
• MAC-level adjacencies
• Link speeds and duplex
Layer 3 — routing
• Subnets and IP addressing
• Routers, SVIs and firewalls
• Routing protocols and next hops
• NAT boundaries and VPN tunnels
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
241

## Slide 242
OBJ 3.1 · DOCUMENTATION
MDF, IDF and the Rack Diagram
1
MDF
Main distribution frame — the primary wiring hub where WAN circuits land and core equipment lives.
2
IDF
Intermediate distribution frame — the per-floor closet linking local drops back to the MDF.
3
Rack diagram
One column per rack, numbered in rack units (1U = 1.75 in); shows exactly what is mounted where.
4
Port maps
Patch panel and switch port labelling ties every user drop to its IDF termination — no more toning cables.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
242

## Slide 243
OBJ 3.1 · DOCUMENTATION
The Documentation Set
Document
Shows
Used when
Floor plan
Rooms, racks, aisles, outlets
Planning space and power
Rack diagram
Devices by rack unit
Installing or replacing gear
Wiring diagram
Terminations, runs, standards
Tracing a faulty link
Logical diagram
Subnets, VLANs, routing
Design and troubleshooting
Heat map
Wi-Fi coverage by colour
Fixing dead zones
WHEN IT MATTERS Exam questions give a task — pick the document that answers it: physical for 'where', logical for 'how it flows'.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
243

## Slide 244
OBJ 3.1 · DOCUMENTATION
Asset Inventory
1
Hardware
Make, model, serial, location and owner for every device — the base record for audits and refresh planning.
2
Software
Installed OS and application versions per host — the record patch management works from.
3
Licensing
Which licences you hold, what they cover, when they renew — non-compliance is a legal and audit risk.
4
Warranty & support
Contract and warranty end dates drive refresh budgets and flag devices approaching end of support.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
244

## Slide 245
OBJ 3.1 · DOCUMENTATION
IPAM — IP Address Management
1
Subnet tracking
Every prefix with its VLAN, gateway and purpose in one authoritative database — not a spreadsheet.
2
Assignment records
Static assignments and DHCP scopes recorded together so no address is ever allocated twice.
3
Discovery & reconciliation
IPAM tools scan the network and reconcile what is actually on the wire against the plan.
4
DDI integration
DNS + DHCP + IPAM suites keep records, scopes and leases in sync automatically.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
245

## Slide 246
OBJ 3.1 · DOCUMENTATION
Wireless Surveys & Heat Maps
1
Predictive survey
Software models coverage from floor plans and wall materials before a single AP is mounted.
2
On-site survey
Walk the site measuring real signal, interference and attenuation with the actual AP placement.
3
Heat map
Colour-coded floor plan of signal strength — dead zones and channel overlap visible at a glance.
4
Validation survey
Repeat after deployment to prove the design targets (RSSI, SNR, throughput) are actually met.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
246

## Slide 247
OBJ 3.1 · DOCUMENTATION
Business Documents — SLA, MOU, SOW
Document
Parties
What it defines
SLA
Provider + customer
Service scope, uptime targets, penalties
MOU
Two partners
Agreed duties where a contract is premature
SOW
Vendor + customer
Deliverables, timeline, milestones
NDA
Org + staff / vendor
Keeps sensitive information confidential
AUP
Org + users
What users may do on org systems
WHEN IT MATTERS The SLA's uptime figure drives your redundancy design — 99.99% cannot be met with single points of failure.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
247

## Slide 248
OBJ 3.1 · LIFE-CYCLE MANAGEMENT
Life-cycle Milestones
Milestone
Vendor stops
Your action
End of sale
Selling the product
Stop new purchases
End of life (EOL)
Feature development
Plan and budget replacement
End of support (EOS)
Patches, fixes, RMA
Decommission by this date
WHEN IT MATTERS EOS is the hard deadline: gear past EOS gets no security patches, so every CVE against it stays open forever.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
248

## Slide 249
OBJ 3.1 · LIFE-CYCLE MANAGEMENT
EOL vs EOS — Why the Difference Matters
End of Life (EOL)
End of Support (EOS)
• Vendor stops selling / developing
• Existing units keep receiving fixes
• Trigger to plan the replacement
• Often years before EOS
• No more patches — even for CVEs
• Failing units cannot be RMA'd
• Unpatched gear = standing audit finding
• Hard deadline to decommission
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
249

## Slide 250
OBJ 3.1 · LIFE-CYCLE MANAGEMENT
Software Management
1
OS updates
The most frequent patch type — schedule through change management, never ad hoc on network gear.
2
Firmware
Low-level device code; fixes hardware bugs and vulnerabilities — verify the image checksum before flashing.
3
Patch discipline
Research the release notes, test in a lab, back up the config, then deploy in a maintenance window.
4
Rollback plan
Every update ships with a tested path back — keep the previous image and config within reach.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
250

## Slide 251
OBJ 3.1 · LIFE-CYCLE MANAGEMENT
Decommissioning a Device
1
Remove from production
drain traffic first
2
Wipe configuration
secrets, keys, configs
3
Update the records
inventory, IPAM, diagrams
4
Dispose or redeploy
per asset policy
WHY IT MATTERS
A decommissioned switch with its config intact is a free map of your network — and its credentials — for whoever buys it second-hand.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
251

## Slide 252
OBJ 3.1 · CHANGE MANAGEMENT
Change Management
1
Service request
Every change starts as a tracked ticket — who wants what, why, and by when.
2
Impact assessment
What breaks if this goes wrong? Which users, which services, which SLAs are exposed?
3
Approval
A change advisory board weighs risk against benefit before any window is booked.
4
Maintenance window
Changes land in agreed low-impact hours, announced to stakeholders in advance.
5
Rollback plan
Written before the change: the exact steps that restore the last known-good state.
6
Documentation
The final step — diagrams, configs and the ticket updated to match the new reality.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
252

## Slide 253
OBJ 3.1 · CHANGE MANAGEMENT
The Change Workflow
1
Request
ticket + justification
2
Assess & approve
CAB weighs the risk
3
Schedule
maintenance window
4
Implement
rollback plan ready
5
Verify & document
update every record
WHY IT MATTERS
Most outages are self-inflicted — change management turns risky edits into reviewed, reversible, documented events.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
253

## Slide 254
OBJ 3.1 · CHANGE MANAGEMENT
Standard vs Emergency Changes
Standard change
Emergency change
• Pre-approved, low-risk, repeatable
• Follows the full request workflow
• Lands in a planned window
• Example: adding a VLAN to a trunk
• Fixes an active outage or exploit
• Approval fast-tracked, never skipped
• Implemented immediately
• Documented retrospectively — always
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
254

## Slide 255
OBJ 3.1 · CHANGE MANAGEMENT
Post-Change Verification
Does the change verify clean within the maintenance window?
YES — close the ticket
Record the result, update diagrams, configs and baselines, and communicate completion to stakeholders.
NO — roll back
Execute the pre-written rollback to the last known-good configuration; never troubleshoot past the window's end.
The rollback trigger is agreed before the change starts — not negotiated at 2 a.m.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
255

## Slide 256
OBJ 3.2 · NETWORK MONITORING
If you cannot see it, you cannot manage it.
Network monitoring layers device polling (SNMP), traffic summaries (flow data), full packet capture and centralised logs into one operational picture.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
256

## Slide 257
OBJ 3.2 · NETWORK MONITORING
Network Monitoring Methods
1
SNMP polling
The NMS asks each device for counters on a schedule — CPU, memory, interface octets, errors.
2
SNMP traps
The device pushes an alert the moment something happens — no waiting for the next poll.
3
Flow data
Routers export per-conversation summaries (NetFlow/IPFIX) — who talked to whom, and how much.
4
Packet capture
The full contents of every frame — the deepest view, used surgically via port mirroring.
5
Log aggregation
Syslog from every device lands on one collector for searching and correlation.
6
API integration
Modern gear exposes REST APIs — monitoring pulls structured JSON instead of screen-scraping CLIs.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
257

## Slide 258
OBJ 3.2 · SNMP
SNMP Building Blocks
1
Agent
Runs on the managed device, listens on UDP/161 and answers reads from the manager.
2
NMS / manager
The monitoring station — Zabbix, LibreNMS, PRTG — that polls agents and graphs the results.
3
MIB
Management Information Base — the tree-structured schema of everything a device can report.
4
OID
Object identifier — a dotted path into the MIB; 1.3.6.1.2.1.1.3.0 is sysUpTime.
5
GET vs WALK
snmpget reads one OID; snmpwalk traverses an entire subtree of related objects.
6
Trap (UDP/162)
Unsolicited notification from agent to manager when a threshold or event fires.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
258

## Slide 259
OBJ 3.2 · SNMP
SNMP Versions
Version
Security
Verdict
v1
Community string, cleartext
Legacy — do not use
v2c
Community string, cleartext
Adds bulk gets; still unauthenticated
v3
User auth + encryption
The only choice for production
WHEN IT MATTERS Exam favourite: a community string is a password sent in cleartext — v3 (authPriv) adds real authentication and privacy.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
259

## Slide 260
OBJ 3.2 · SNMP
SNMPv3 Security Levels
Level
Authentication
Encryption
noAuthNoPriv
Username only
None
authNoPriv
SHA/MD5 digest
None
authPriv
SHA/MD5 digest
AES/DES — full privacy
WHEN IT MATTERS authPriv is the deployment target: the manager is authenticated and the polled data is encrypted in transit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
260

## Slide 261
OBJ 3.2 · SNMP
Traps vs Polls
Polling (GET, UDP/161)
Traps (UDP/162)
• Manager pulls on a fixed schedule
• Regular series — ideal for graphs
• Misses events between polls
• Predictable load on devices
• Device pushes the moment events fire
• Instant notification of failures
• Fire-and-forget — can be lost
• Informs add acknowledgement
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
261

## Slide 262
OBJ 3.2 · SNMP
Reading snmpwalk Output
A v2c walk of the system subtree against the lab agent.
$ snmpwalk -v2c -c public 127.0.0.1 system
SNMPv2-MIB::sysDescr.0 = STRING: Linux ubuntu
5.15.0-91-generic x86_64
SNMPv2-MIB::sysObjectID.0 = OID:
NET-SNMP-MIB::netSnmpAgentOIDs.10
DISMAN-EVENT-MIB::sysUpTimeInstance =
Timeticks: (8642100) 1 day, 0:00:21.00
SNMPv2-MIB::sysContact.0 = STRING: root@lab
SNMPv2-MIB::sysName.0 = STRING: ubuntu
-v2c -c public
Version 2c with community 'public' — the credential, and it crosses the wire in cleartext.
MIB::name.0
With MIBs installed, numeric OIDs render as names — sysDescr.0 instead of 1.3.6.1.2.1.1.1.0.
Timeticks
sysUpTime counts hundredths of a second — a sudden reset here means the device rebooted.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
262

## Slide 263
DOMAIN 3.0 · HANDS-ON
SNMP Monitoring
LAB 15
Configure an SNMP agent and poll MIB objects with snmpwalk and snmpget (OBJ 3.2).
Install snmpd on Ubuntu, configure a read-only v2c community string, then walk the system and IF-MIB subtrees to read uptime, interface names and live traffic counters — the raw data every NMS graphs.
YOU'LL BUILD
A polling-ready SNMP agent on UDP/161 answering v2c queries, plus walked system and interface OIDs.
TOOLCHAIN
snmpd, snmpwalk, snmpget, snmp-mibs-downloader
DONE WHEN
snmpwalk returns sysDescr/sysUpTime values and IF-MIB::ifInOctets shows a rising octet counter per interface — rerun it and watch the numbers grow.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
263

## Slide 264
LAB 15 · PROCESS MAP
How Lab 15 Runs
1
Install the SNMP agent and client
apt · step 1
2
Add a read-only community for loopback
echo · step 2
3
Restart the agent to load the new
systemctl · step 3
4
Fetch a single OID with snmpget
snmpget · step 5
5
Walk the per-interface traffic
snmpwalk · step 6
THE POINT
Configure an SNMP agent and poll MIB objects with snmpwalk and snmpget (OBJ 3.2).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
264

## Slide 265
LAB 15 · VERIFY
SNMP Monitoring
✅ Expected result
snmpwalk returns sysDescr/sysUpTime values and IF-MIB::ifInOctets shows a rising octet counter per interface — rerun it and watch the numbers grow.
IF IT DOESN'T WORK
Timeout: No Response from 127.0.0.1
Restart snmpd and confirm agentaddress in snmpd.conf includes udp:127.0.0.1:161.
Output shows numeric OIDs only
Install snmp-mibs-downloader and comment out the 'mibs :' line in /etc/snmp/snmp.conf.
Authentication/community failure
Community mismatch — use -c public and confirm the rocommunity line was appended to snmpd.conf.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
265

## Slide 266
OBJ 3.2 · FLOW DATA
Flow Data — NetFlow & IPFIX
1
What a flow is
One record per conversation: the 5-tuple plus byte, packet and duration counters — metadata, no payload.
2
Exporter
The router, switch or probe (fprobe in the lab) that watches traffic and emits flow records.
3
Collector
Receives and stores the records — nfcapd listening on UDP/9995 in the lab.
4
Analyser
nfdump, ntopng or a SIEM turns stored flows into top-talker and capacity reports.
5
Versions
NetFlow v5 (fixed fields), v9 (templates), IPFIX (the IETF standard), sFlow (packet sampling).
6
vs packet capture
Flows are tiny to store and keep weeks of history; capture keeps payloads but only for minutes.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
266

## Slide 267
OBJ 3.2 · FLOW DATA
Reading an nfdump Report
Top source IPs summarised from the lab collector's stored flows.
$ nfdump -R /tmp/flows -s srcip -n 3
Top 3 Src IP Addr ordered by flows:
Date first seen Src IP Addr Flows Bytes
09:12:04 2026 10.0.0.15 142 8.1 M
09:12:31 2026 10.0.0.22 57 1.2 M
09:13:02 2026 8.8.8.8 12 4560
Summary: total flows: 211, bytes: 9.4 M
-s srcip
Aggregate by source IP — an instant top-talkers list for capacity or incident work.
Flows vs Bytes
Many flows with few bytes suggests scanning; few flows with huge bytes means bulk transfer.
-R /tmp/flows
Reads every rolled capture file in the directory — flow history is just files on disk.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
267

## Slide 268
OBJ 3.2 · PACKET CAPTURE
Packet Capture & Port Mirroring
1
Port mirroring (SPAN)
The switch copies frames from chosen ports or VLANs to an analyser port — capture without touching the path.
2
Network TAP
Inline hardware splits the signal to a monitor port — sees every bit, including errors SPAN may drop.
3
Full capture
tcpdump and Wireshark record whole packets, payloads included — storage-hungry, deepest evidence.
4
Choosing the tool
Flows for trends and history, capture for deep dives — mirror only what you must, only as long as you must.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
268

## Slide 269
DOMAIN 3.0 · HANDS-ON
NetFlow Analysis with nfdump
LAB 16
Export, collect and analyse flow data to find top talkers and busiest ports (OBJ 3.2).
Run a flow exporter (fprobe) and collector (nfcapd) on one VM, generate web and ICMP traffic, then use nfdump to build top-talker and destination-port reports from the captured flow records.
YOU'LL BUILD
A working exporter-to-collector NetFlow v5 pipeline with nfdump top-N reports of your own traffic.
TOOLCHAIN
fprobe, nfcapd, nfdump, curl, ping
DONE WHEN
nfdump -R /tmp/flows -s srcip lists your VM as a top talker and -s dstport shows ports 443 and ICMP traffic from the curl and ping you generated.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
269

## Slide 270
LAB 16 · PROCESS MAP
How Lab 16 Runs
1
Install the flow collector and
apt · step 1
2
Start fprobe exporting NetFlow v5
fprobe · step 3
3
Generate web and ICMP traffic to
curl · step 4
4
Wait for the collector to roll a file
sleep · step 5
5
Stop the exporter and collector
pkill · step 7
THE POINT
Export, collect and analyse flow data to find top talkers and busiest ports (OBJ 3.2).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
270

## Slide 271
LAB 16 · VERIFY
NetFlow Analysis with nfdump
✅ Expected result
nfdump -R /tmp/flows -s srcip lists your VM as a top talker and -s dstport shows ports 443 and ICMP traffic from the curl and ping you generated.
IF IT DOESN'T WORK
nfdump: no matched flows
Wait the full 60 s — nfcapd only rolls a readable file every rotation interval.
Collector directory is empty
Confirm fprobe points at 127.0.0.1:9995 and nfcapd is running with -p 9995 (check with ps).
fprobe: no such device eth0
List interfaces with ip link and start fprobe against the VM's actual NIC name.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
271

## Slide 272
OBJ 3.2 · LOG AGGREGATION
Log Aggregation with Syslog
1
Why centralise
Logs on a failed or compromised device are gone; on a collector they survive and can be correlated.
2
Syslog transport
UDP/514 classic, TCP/514 for reliable delivery, TLS on TCP/6514 for confidentiality.
3
Facility.severity
Every message carries both tags — auth.warning, local0.info — and selectors route on them.
4
Collector
rsyslog or syslog-ng receives, filters and stores; the SIEM ingests from there.
5
Retention & WORM
Keep logs long enough for compliance and incident timelines; write-once storage resists tampering.
6
Test the pipeline
logger injects an event end-to-end — prove forwarding works before an incident depends on it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
272

## Slide 273
OBJ 3.2 · LOG AGGREGATION
Syslog Severity Levels 0-7
Level
Keyword
Meaning
0
emergency
System unusable — all hands
1 / 2
alert / critical
Act immediately / critical fault
3 / 4
error / warning
Failures and conditions to review
5 / 6
notice / info
Significant-but-normal / routine events
7
debug
Verbose troubleshooting output
WHEN IT MATTERS Lower number = more severe. Logging 'at level 4' collects 0-4; debug is switched on only while you troubleshoot.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
273

## Slide 274
OBJ 3.2 · SIEM
SIEM — Aggregate, Correlate, Alert
1
Aggregation
One searchable store for logs, flows and alerts from every source in the estate.
2
Correlation
Links related events across systems — one failed login is noise; 500 across 20 hosts is an attack.
3
Alerting
Configurable triggers and thresholds notify the on-call the moment a pattern fires.
4
WORM storage
Write once, read many — evidence-grade log storage that cannot be quietly edited.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
274

## Slide 275
OBJ 3.2 · LOG AGGREGATION
Working the Aggregated Log
1
grep / grep -E
First-line analysis — filter the collector's log by host, tag, severity or pattern.
2
Regular expressions
Match classes of events, not single strings — build and test them in the TIS Regex Generator, then run with grep -E.
3
logger
Injects labelled test events (-p local0.info) so you can verify routing rules safely.
4
Structured logging
JSON output and APIs feed parsers directly, replacing fragile text scraping.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
275

## Slide 276
DOMAIN 3.0 · HANDS-ON
Centralised Logging with Rsyslog
LAB 17
Build a syslog forwarding pipeline and filter aggregated events by severity and pattern (OBJ 3.2).
Configure rsyslog to receive on TCP/514 and forward to itself over loopback, inject test events with logger, then verify and filter the aggregated log — including a regex built in the TIS Regex Generator.
YOU'LL BUILD
A send-and-receive rsyslog collector on TCP/514 with verified test events and regex-filtered output.
TOOLCHAIN
rsyslog, logger, ss, grep -E, TIS Regex Generator
DONE WHEN
ss shows rsyslog listening on :514, grep finds the injected 'Network+ Lab 17 test event' in /var/log/syslog, and your grep -E regex from the TIS Regex Generator matches it too.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
276

## Slide 277
LAB 17 · PROCESS MAP
How Lab 17 Runs
1
Enable the imtcp receiver module in
sed · step 1
2
Forward every event to the collector
echo · step 3
3
Restart rsyslog and confirm the 514
systemctl · step 4
4
Inject a test event with an explicit
logger · step 5
5
Build a regex in the TIS Regex
grep · step 7
THE POINT
Build a syslog forwarding pipeline and filter aggregated events by severity and pattern (OBJ 3.2).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
277

## Slide 278
LAB 17 · VERIFY
Centralised Logging with Rsyslog
✅ Expected result
ss shows rsyslog listening on :514, grep finds the injected 'Network+ Lab 17 test event' in /var/log/syslog, and your grep -E regex from the TIS Regex Generator matches it too.
IF IT DOESN'T WORK
Nothing listening on port 514
Both sed edits must apply — recheck rsyslog.conf uncommented imtcp lines, then restart rsyslog.
Test event missing from syslog
Run logger without -p first; then check /etc/rsyslog.d/50-forward.conf uses @@127.0.0.1:514.
grep -E returns no matches
Test the regex in the TIS Regex Generator against a pasted log line before using it with grep.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
278

## Slide 279
OBJ 3.4 · NETWORK SERVICES
The quiet services every network leans on.
DHCP hands out addresses, DNS resolves names, NTP keeps every clock honest — and when any of them wobbles, everything else looks broken.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
279

## Slide 280
OBJ 3.4 · DHCP
DHCP Essentials
1
Scope
The pool of addresses the server may lease on one subnet, minus any exclusions.
2
Lease
An address is borrowed, not owned — the client renews at 50% of the lease time.
3
Reservation
A fixed IP bound to a MAC address — printers and servers get the same address every time.
4
Options
Extras pushed with the lease: router (3), DNS (6), domain name (15), TFTP for phones (66).
5
Relay / IP helper
A router forwards the local DHCP broadcast as unicast to a central server on another subnet.
6
Exclusions
Addresses inside the range the server must never hand out — statics live here.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
280

## Slide 281
OBJ 3.4 · DHCP
DORA — the DHCP Handshake
1
Discover
client broadcasts
2
Offer
server proposes an IP
3
Request
client accepts one
4
Acknowledge
lease confirmed
WHY IT MATTERS
DORA runs as broadcast — without a relay agent (IP helper) it can never cross a router to reach a centralised DHCP server.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
281

## Slide 282
OBJ 3.4 · DHCP
Reading dhcpd.conf
A minimal ISC DHCP scope with one reservation.
subnet 192.168.10.0 netmask 255.255.255.0 {
range 192.168.10.100 192.168.10.199;
option routers 192.168.10.1;
option domain-name-servers 9.9.9.9;
default-lease-time 86400;
}
host printer1 {
hardware ethernet 00:11:22:33:44:55;
fixed-address 192.168.10.50;
}
range
The scope: only .100-.199 are leased; .2-.99 stay free for statics and reservations.
option lines
DHCP options 3 and 6 — the default gateway and DNS server pushed with every lease.
host block
A reservation: the client with this MAC always receives 192.168.10.50.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
282

## Slide 283
OBJ 3.4 · DHCP
Reservation vs Static Assignment
DHCP reservation
Static configuration
• Configured centrally on the server
• Device still runs plain DHCP
• Options update from one place
• Survives device re-imaging
• Typed into the device itself
• Works with no DHCP server at all
• Every change is a device visit
• Right for routers, core switches
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
283

## Slide 284
OBJ 3.4 · SLAAC
SLAAC — Addressing Without a Server
1
Router Advertisement
IPv6 routers advertise the /64 prefix; hosts solicit and listen for RAs at startup.
2
Self-generated address
The host builds its own address from the prefix plus EUI-64 or a random identifier.
3
DAD
Duplicate Address Detection confirms no other node already holds the address.
4
DHCPv6 still exists
Stateful DHCPv6 or the RA 'other config' flag supplies DNS and options when SLAAC alone is not enough.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
284

## Slide 285
OBJ 3.4 · DNS
DNS Architecture
1
Authoritative server
Holds the zone data and answers for it definitively — the source of truth for a domain.
2
Recursive resolver
Chases the answer through root, TLD and authoritative servers on the client's behalf, then caches it.
3
Primary zone
The writable copy of the zone, edited on the primary server.
4
Secondary zone
Read-only replicas kept in sync by zone transfer (AXFR/IXFR) for redundancy.
5
Zone file & SOA
The records for one domain; the SOA serial number versions every change.
6
TTL
How long resolvers may cache an answer — long TTLs cut load but slow down migrations.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
285

## Slide 286
OBJ 3.4 · DNS
Authoritative vs Recursive
Authoritative
Recursive
• Owns the zone's records
• Answers only for its own domains
• Run where your zones live
• Compromise = forged records
• Owns no records — resolves and caches
• Answers anything for its clients
• Run near users (ISP, 1.1.1.1, 8.8.8.8)
• Compromise = poisoned cache
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
286

## Slide 287
OBJ 3.4 · DNS
DNS Record Types — Recap
Record
Maps
Note
A / AAAA
Name to IPv4 / IPv6
The workhorse records
CNAME
Alias to canonical name
Never at the zone apex
MX
Domain to mail server
Priority number picks order
PTR
IP back to name
Reverse DNS; mail filters check it
TXT
Name to free text
SPF, DKIM, site verification
NS / SOA
Zone to its servers
Delegation and zone authority
WHEN IT MATTERS Domain 1 covered the records; Domain 3 asks who answers — authoritative vs recursive, primary vs secondary.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
287

## Slide 288
OBJ 3.4 · TIME SYNCHRONISATION
Time Services — NTP, PTP, NTS
1
Why time matters
Logs, certificates, Kerberos and SIEM correlation all break when clocks drift apart.
2
NTP (UDP/123)
Polls reference servers and gradually disciplines the local clock toward true time.
3
Stratum hierarchy
Distance from the reference clock — each hop from stratum 0 hardware adds one.
4
Multiple sources
Clients compare several upstream servers and vote out 'falsetickers' before trusting any.
5
PTP (IEEE 1588)
Precision Time Protocol — hardware timestamping for sub-microsecond accuracy in finance and telecom.
6
NTS
Network Time Security wraps NTP key exchange in TLS — stops attackers spoofing your time source.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
288

## Slide 289
OBJ 3.4 · TIME SYNCHRONISATION
NTP Strata
Stratum
What it is
Example
0
The reference clock itself
GPS, caesium / atomic clock
1
Server wired to a stratum 0
Time appliance in the DC
2-15
Each network hop adds one
Enterprise and pool servers
16
Unsynchronised
Clock not valid — do not trust
WHEN IT MATTERS Lower stratum = closer to the reference. Ported from the legacy deck: NTP operates as a hierarchy of clock strata over UDP/123.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
289

## Slide 290
OBJ 3.4 · TIME SYNCHRONISATION
Reading chronyc sources
Which server is my clock actually following?
$ chronyc sources -v
MS Name/IP address Stratum Poll Reach Offset
^* time.cloudflare.com 3 6 377 +142us
^- ntp.ubuntu.com 2 6 377 -1250us
^? 10.0.0.99 0 6 0 +0ns
^* / ^- / ^?
* is the selected source, - a viable backup candidate, ? unreachable or untested.
Stratum
Cloudflare here is stratum 3 — three hops from a hardware reference clock.
Reach 377
Octal bitmask of the last eight polls — 377 means all eight answered.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
290

## Slide 291
DOMAIN 3.0 · HANDS-ON
Time Synchronisation with Chrony
LAB 18
Configure NTP time sync with chrony and interpret stratum, offset and drift (OBJ 3.4).
Install chrony (the modern ntpd replacement), inspect the selected time sources and stratum hierarchy, add an extra NTP server with iburst, and force an immediate clock step.
YOU'LL BUILD
A VM synchronised over UDP/123 with multiple NTP sources and a readable chronyc tracking report.
TOOLCHAIN
chrony, chronyc
DONE WHEN
chronyc sources -v shows time.cloudflare.com in the list with a ^* or ^- marker, and chronyc tracking reports a stratum below 16 with a sub-second system time offset.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
291

## Slide 292
LAB 18 · PROCESS MAP
How Lab 18 Runs
1
Install chrony and start the service
apt · step 1
2
List time sources
chronyc · step 2
3
Show stratum
chronyc · step 3
4
Restart chrony and re-check the source
systemctl · step 5
5
Force an immediate clock step
chronyc · step 6
THE POINT
Configure NTP time sync with chrony and interpret stratum, offset and drift (OBJ 3.4).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
292

## Slide 293
LAB 18 · VERIFY
Time Synchronisation with Chrony
✅ Expected result
chronyc sources -v shows time.cloudflare.com in the list with a ^* or ^- marker, and chronyc tracking reports a stratum below 16 with a sub-second system time offset.
IF IT DOESN'T WORK
All sources show ^? unreachable
UDP/123 egress may be blocked — wait for retries, or verify with chronyc activity and tracking.
New server never appears
The server line must be in /etc/chrony/chrony.conf and chrony restarted — check for typos.
Stratum shows 16
16 means unsynchronised — run chronyc -a makestep and give the sources a minute to be selected.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
293

## Slide 294
OBJ 3.1 · CONFIGURATION MANAGEMENT
Configuration Management
1
Production config
The running configuration on the live device — what the network actually does right now.
2
Backup config
A stored copy taken on schedule and before every change — your rollback path.
3
Baseline config
The approved golden template a device of that role should match — any drift is a defect.
4
Golden images
Known-good firmware and OS images kept with checksums for clean rebuilds.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
294

## Slide 295
OBJ 3.1 · CONFIGURATION MANAGEMENT
Config Backup Discipline
1
Back up before every change
▶
2
Store versioned, off the device
▶
3
Diff running vs baseline regularly
▶
4
Alert on unauthorised drift
▶
5
Test restores — a backup is a claim
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
295

## Slide 296
OBJ 3.1 · CONFIGURATION MANAGEMENT
Version Control for Configurations
1
History
Every change recorded with author, timestamp and message — an audit trail for free.
2
Diff
See exactly what changed between any two versions — the fastest root-cause tool there is.
3
Blame
Line-by-line attribution answers 'who set this, and when?' in one command.
4
Revert
Undo one bad change without losing everything committed after it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
296

## Slide 297
DOMAIN 3.0 · HANDS-ON
Configuration Backup with Git
LAB 19
Put network configuration under version control for history, diff, blame and rollback (OBJ 3.1).
Initialise a git repository in /etc, commit a baseline of the critical network configs, make and commit a change, inspect the audit trail with log and show, then roll the change back with revert.
YOU'LL BUILD
A version-controlled /etc with a baseline commit, a tracked change, and a demonstrated one-command rollback.
TOOLCHAIN
git
DONE WHEN
git log --oneline shows the baseline, the change and the revert as three commits, and cat /etc/hosts confirms the lab-vm line was removed by the rollback.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
297

## Slide 298
LAB 19 · PROCESS MAP
How Lab 19 Runs
1
Install git
apt · step 1
2
Commit a baseline of the critical
git · step 3
3
Make a change and view the pending
echo · step 4
4
Commit the change with a meaningful
git · step 5
5
Roll the change back with revert
git · step 7
THE POINT
Put network configuration under version control for history, diff, blame and rollback (OBJ 3.1).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
298

## Slide 299
LAB 19 · VERIFY
Configuration Backup with Git
✅ Expected result
git log --oneline shows the baseline, the change and the revert as three commits, and cat /etc/hosts confirms the lab-vm line was removed by the rollback.
IF IT DOESN'T WORK
Please tell me who you are
Set both identity values: git config user.email and git config user.name before committing.
Nothing added to commit
Run the git add with explicit filenames from inside /etc — pathspec errors mean a wrong cwd.
Revert did not change hosts
Revert undoes the LAST commit — check git log to confirm HEAD was the hosts change, not another edit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
299

## Slide 300
OBJ 3.2 · NETWORK MONITORING
Baselines & Anomaly Alerting
1
Baseline
Measurements taken while the network is healthy — the operational definition of 'normal'.
2
Performance metrics
Bandwidth, throughput, latency, jitter and loss — trended per link and per service.
3
Availability monitoring
Up/down state and uptime percentage, tracked against the SLA target.
4
Anomaly alerting
Alert on deviation from the baseline, not just fixed thresholds — it catches the subtle failures.
5
Interface counters
Errors, discards, CRCs, giants and runts — rising counters flag layer 1-2 trouble.
6
Utilisation
Sustained load near capacity means congestion is coming — plan upgrades from the trend line.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
300

## Slide 301
OBJ 3.2 · NETWORK MONITORING
Interface Statistics to Watch
1
Link state
Up/down and flapping history — a link that bounces hourly is a failing SFP or cable.
2
Speed / duplex
A 100/half port on a gigabit switch is usually a failed autonegotiation, not a slow NIC.
3
CRC errors
Frames failing the checksum — cabling, connectors or EMI corrupting bits in flight.
4
Giants & runts
Frames beyond or below legal Ethernet sizes — MTU mismatches, bad NICs, collisions.
5
Discards / drops
Good frames thrown away for lack of buffer — the signature of congestion.
6
Byte counts
Send/receive octets feed the utilisation graphs every capacity decision rests on.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
301

## Slide 302
OBJ 3.2 · AVAILABILITY
The Cost of a Nine
Chart: 
| 99% | 99.9% | 99.99% | 99.999%
Downtime allowed, minutes/year | 5256 | 526 | 53 | 5
WHAT THE DATA SHOWS
Each extra nine cuts permitted downtime tenfold — 99.9% allows almost nine hours a year, 99.99% under an hour. The SLA figure dictates the redundancy budget.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
302

## Slide 303
OBJ 3.2 · PERFORMANCE METRICS
Measuring Throughput with iperf3
1
Client / server model
One end listens (-s), the other transmits (-c) — measure the path between them, not a guess.
2
TCP vs UDP tests
TCP reports achievable goodput; UDP at a set rate (-b) exposes jitter and datagram loss.
3
Parallel streams
-P opens several flows at once — separates TCP window limits from true bandwidth limits.
4
Reverse mode
-R sends from server to client — the test for asymmetric paths like DOCSIS upstream.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
303

## Slide 304
DOMAIN 3.0 · HANDS-ON
Performance Baseline with iperf3
LAB 20
Baseline throughput, jitter and loss with iperf3 TCP, UDP, parallel and reverse tests (OBJ 3.2).
Run an iperf3 server as a daemon and test against it: a 10-second TCP throughput test, four parallel streams, a 100 Mbps UDP test that reports jitter and loss, and a reverse test for asymmetric paths.
YOU'LL BUILD
A recorded performance baseline: TCP bitrate, parallel-stream totals, UDP jitter/loss and reverse-direction results.
TOOLCHAIN
iperf3
DONE WHEN
The TCP test reports a multi-Gbps loopback Bitrate, the UDP test shows jitter in ms with near-zero lost datagrams, and the -P 4 run sums four streams in the [SUM] row.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
304

## Slide 305
LAB 20 · PROCESS MAP
How Lab 20 Runs
1
Install iperf3
apt · step 1
2
Run a 10-second TCP throughput test
iperf3 · step 3
3
Open four parallel streams to saturate
iperf3 · step 4
4
Run a UDP test at 100 Mbps
iperf3 · step 5
5
Stop the server
pkill · step 7
THE POINT
Baseline throughput, jitter and loss with iperf3 TCP, UDP, parallel and reverse tests (OBJ 3.2).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
305

## Slide 306
LAB 20 · VERIFY
Performance Baseline with iperf3
✅ Expected result
The TCP test reports a multi-Gbps loopback Bitrate, the UDP test shows jitter in ms with near-zero lost datagrams, and the -P 4 run sums four streams in the [SUM] row.
IF IT DOESN'T WORK
Connection refused to 127.0.0.1
The server is not running — start it again with iperf3 -s -D and confirm with pgrep iperf3.
Server busy — another test running
Only one client at a time per server; wait for the previous run or pkill iperf3 and restart.
UDP shows heavy datagram loss
Lower the offered rate (-b 10M) — loss at a set bandwidth is the finding, not an error.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
306

## Slide 307
OBJ 3.3 · DISASTER RECOVERY
Plan for the bad day before it arrives.
Disaster recovery quantifies what you can afford to lose (RPO), how long you can be down (RTO), and rehearses the switchover before it is ever real.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
307

## Slide 308
OBJ 3.3 · DISASTER RECOVERY
DR Metrics — RPO, RTO, MTTR, MTBF
Metric
Question it answers
Example
RPO
How much data can we lose?
Backups every 4 h = RPO 4 h
RTO
How long until service is back?
Restore must finish in 2 h
MTTR
Average time to repair a failure
Ticket open to fixed: 45 min
MTBF
Average time between failures
PSU rated at 100,000 h
WHEN IT MATTERS RPO sizes your backup frequency; RTO sizes your recovery infrastructure. Both are business decisions before they are technical ones.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
308

## Slide 309
OBJ 3.3 · DISASTER RECOVERY
Recovery Sites — Cold, Warm, Hot
Site
Readiness
Cost
Failover time
Cold
Space and power only — no gear
$
Days
Warm
Hardware in place, data loaded on demand
$$
Hours
Hot
Live replica with data in sync
$$$
Minutes
Cloud
Elastic DR-as-a-service, pay on use
$-$$
Design-dependent
WHEN IT MATTERS Pick the cheapest site that still meets the RTO — a hot site protecting a tolerant workload is money burned.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
309

## Slide 310
OBJ 3.3 · DISASTER RECOVERY
Active-Active vs Active-Passive
Active-active
Active-passive
• All nodes serve traffic at once
• Full capacity used in normal running
• A failure just shrinks capacity
• Needs state sync between nodes
• Standby waits idle for failover
• Simpler state management
• Brief pause while standby takes over
• Hardware that mostly sits idle
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
310

## Slide 311
OBJ 3.3 · HIGH AVAILABILITY
High Availability Building Blocks
1
Single point of failure
One component whose failure stops the whole workflow — HA design exists to remove these.
2
Redundancy
Duplicate power, links, supervisors and paths so one failure never becomes an outage.
3
Clustering
Multiple servers act as one logical service and survive the loss of members.
4
Load balancing
Spreads requests across the cluster and steers around failed members automatically.
5
Virtual IP / FHRP
VRRP or HSRP float one gateway address across routers — the default gateway survives a router death.
6
Critical assets & nodes
Know which systems keep production alive — they get the redundancy budget first.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
311

## Slide 312
OBJ 3.3 · DISASTER RECOVERY
DR Failover — and Failback
1
Declare
invoke the DR plan
2
Fail over
DR site takes the load
3
Operate at DR
monitor degraded mode
4
Fail back
planned, off-peak
5
Review
after-action report
WHY IT MATTERS
Failback is the forgotten half — returning to the primary site is itself a risky, planned change with its own window and rollback.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
312

## Slide 313
OBJ 3.3 · DR TESTING
Testing the DR Plan
1
Tabletop exercise
Walk the scenario around a table — cheap, and it finds the gaps in roles, contacts and assumptions.
2
Validation test
Actually restore the backups and fail services over — proves the runbooks, not the intentions.
3
Full failover drill
Run production from the DR site for a period — the only complete proof the plan works.
4
After-action report
Every exercise ends with documented findings and concrete plan updates.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
313

## Slide 314
OBJ 3.3 · INCIDENT RESPONSE
Incident Response
1
Detect & report
first responder
2
Escalate
to the right team
3
Contain & collect
preserve evidence
4
Recover
restore service
5
Review
lessons learned
WHY IT MATTERS
Forensic discipline — secure the area, document the scene, keep chain of custody — is what keeps evidence admissible and the timeline reconstructable.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
314

## Slide 315
OBJ 3.3 · BACKUPS
Backups That Actually Restore
1
3-2-1 rule
Three copies, two media types, one offsite — survives device loss, site loss and ransomware.
2
Snapshots
Point-in-time images for fast local rollback — useful, but never a substitute for offsite copies.
3
Config + state data
Back up device configurations AND application data; the RPO applies to both.
4
Restore testing
An untested backup is a hope, not a plan — schedule restore drills like any other maintenance.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
315

## Slide 316
OBJ 3.5 · VPN
VPN Types
Type
Connects
Typical use
Site-to-site
Two networks via gateways
Branch to HQ, always on
Client-to-site
One device to the network
Remote workers, on demand
Full tunnel
ALL client traffic via VPN
Maximum inspection and control
Split tunnel
Only corporate subnets via VPN
Saves bandwidth, less visibility
WHEN IT MATTERS Site-to-site tunnels are transparent to users; client-to-site needs software (or a clientless HTML5 portal) on each device.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
316

## Slide 317
OBJ 3.5 · VPN
Split or Full Tunnel?
Does policy require inspecting all remote-user traffic?
YES — full tunnel
Route everything through HQ: complete visibility and filtering, at the cost of bandwidth, latency and user experience.
NO — split tunnel
Send only corporate destinations through the VPN; internet traffic goes direct — faster, but invisible to your controls.
Document the choice either way — auditors ask, and users notice.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
317

## Slide 318
OBJ 3.5 · ACCESS & MANAGEMENT
Management Access Methods
1
SSH (TCP/22)
Encrypted CLI — the default for device administration; prefer key-based auth over passwords.
2
GUI
Web management over HTTPS — convenient, but restrict it to the management VLAN.
3
API
REST and NETCONF programmatic control — the foundation of automation and infrastructure as code.
4
Console
Direct serial access — works when the network is down; the recovery path of last resort.
5
Out-of-band
A separate management network or LTE modem, reachable when production is not.
6
Jump box
One hardened, logged host is the only door into the management network.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
318

## Slide 319
OBJ 3.5 · ACCESS & MANAGEMENT
In-band vs Out-of-band Management
In-band
Out-of-band
• Management rides the production net
• Cheap — no extra infrastructure
• Lost exactly when you need it most
• Fine for day-to-day monitoring
• Dedicated network, serial or LTE path
• Reachable during outages
• Extra cost, another network to secure
• Essential for core and remote sites
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
319

## Slide 320
OBJ 3.5 · ACCESS & MANAGEMENT
The Jump Box Access Path
1
Admin authenticates with MFA
▶
2
Lands on the hardened jump box
▶
3
Session is logged and recorded
▶
4
SSH to device on management VLAN
▶
5
Change tracked against a ticket
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
320

## Slide 321
DOMAIN 3 COMPLETE
Operations is where designs meet reality.
Document it, monitor it, back it up, rehearse the disaster, and control every management door — that is Domain 3, and 19% of your exam.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
321

## Slide 322
DOMAIN 3.0 RECAP
Recap — Network Operations
• You can now: Configure an SNMP agent and poll MIB objects with snmpwalk and snmpget (OBJ 3.2).
• You can now: Export, collect and analyse flow data to find top talkers and busiest ports (OBJ 3.2).
• You can now: Build a syslog forwarding pipeline and filter aggregated events by severity and pattern (OBJ 3.2).
• You can now: Configure NTP time sync with chrony and interpret stratum, offset and drift (OBJ 3.4).
• You can now: Put network configuration under version control for history, diff, blame and rollback (OBJ 3.1).
• You can now: Baseline throughput, jitter and loss with iperf3 TCP, UDP, parallel and reverse tests (OBJ 3.2).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
322

## Slide 323
DOMAIN 4.0 · 14% OF THE EXAM
Network Security
Logical & physical security · deception · terminology · audits & compliance · segmentation · attacks · defence features
4.0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
323

## Slide 324
WHAT YOU'LL DO
Hands-On Labs — Network Security
Labs 21–23
• Host Firewall with UFW
• TLS Certificate with OpenSSL and Nginx
• SSH Hardening with Key Authentication
Labs 24–26
• Site-to-Site VPN with WireGuard
• Port Scanning and Service Hardening
• Intrusion Detection with Suricata
Lab 27
• Building an ACL with iptables
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
324

## Slide 325
DOMAIN 4 · 14% OF THE EXAM
Domain 4 - Network Security.
14% of the exam: encryption, identity, attacks, hardening, segmentation and physical defence - how we keep the network confidential, intact and available.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
325

## Slide 326
OBJ 4.1 · SECURITY CONCEPTS
The CIA Triad
Confidentiality
• Only authorised eyes see the data
• Encryption in transit and at rest
• Access controls and least privilege
Integrity
• Data arrives exactly as it was sent
• Hashes detect tampering (SHA-256)
• Digital signatures prove the origin
Availability
• Systems stay reachable when needed
• Redundancy, backups, DDoS defence
• Balance security against usability
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
326

## Slide 327
OBJ 4.1 · SECURITY TERMINOLOGY
Security Terminology
1
Threat
Any actor or event with the potential to harm the network - from a ransomware crew to a burst pipe above the server room.
2
Vulnerability
A weakness that could be abused - an unpatched service, a default password, an open port nobody remembers.
3
Exploit
The technique or code that weaponises a vulnerability to gain access or disrupt service.
4
Risk
Likelihood times impact of a threat exploiting a vulnerability - what budgets and priorities are set against.
5
CVE
Common Vulnerabilities and Exposures - the public catalogue of disclosed flaws, each with an ID like CVE-2021-44228 (Log4Shell).
6
Zero-day
A flaw attackers find before the vendor does - no patch exists yet, so layered defence is the only cover.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
327

## Slide 328
OBJ 4.1 · SECURITY TERMINOLOGY
From Threat to Impact
1
Threat
actor with intent
2
Vulnerability
a weakness exposed
3
Exploit
the flaw weaponised
4
Breach
access gained
5
Impact
CIA compromised
WHY IT MATTERS
Break any link and the attack fails - patching removes vulnerabilities, hardening blocks exploits, monitoring and response limit impact.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
328

## Slide 329
OBJ 4.1 · AUDITS & COMPLIANCE
Audits and Regulatory Compliance
1
Security audit
An independent check that controls exist and work - configs, logs, access reviews, penetration tests.
2
Data locality
Laws that dictate WHERE data may be stored and processed - pins your cloud regions and backup sites.
3
PCI DSS
Card-industry standard: anyone storing or transmitting card data must segment, encrypt and log that environment.
4
GDPR
EU personal-data regulation: privacy by design, breach notification within 72 hours, heavy fines for leaks.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
329

## Slide 330
OBJ 4.1 · AUDITS & COMPLIANCE
Compliance Regimes at a Glance
Regime
Scope
Network requirement
PCI DSS
Cardholder data environments
Segment the CDE, encrypt, log all access
GDPR
Personal data of EU residents
Protect by design; report breaches fast
Data locality
Where data may physically live
Keep regulated data in approved regions
PDPA (SG)
Singapore personal data
Reasonable security arrangements required
WHEN IT MATTERS Audits verify these on paper AND on the wire - segmentation and logs are the evidence.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
330

## Slide 331
OBJ 4.3 · DEFENSE TECHNIQUES
Defense in Depth
1
Perimeter
Edge firewalls, screened subnet, DDoS scrubbing - the first line, never the only line.
2
Network
Segmentation, VLANs, ACLs, IDS/IPS - contain whatever gets past the edge.
3
Host / endpoint
Host firewalls, EDR, patching, hardening - every machine defends itself.
4
Application
Input validation, secure APIs, WAF - the layer attackers actually talk to.
5
Data
Encryption at rest, backups, DLP - the final prize gets its own armour.
6
Separation of duties
No single person holds enough rights to abuse the system alone.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
331

## Slide 332
OBJ 4.3 · ZONES
Trusted vs Untrusted Zones
Trusted zone
Untrusted / screened
• Internal LANs and data-centre subnets
• Users and devices are authenticated
• Servers holding business data
• Still segmented - trust is never absolute
• The Internet - assume hostile
• Guest and BYOD networks
• Screened subnet (DMZ) for public services
• Traffic crossing zones must pass a firewall
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
332

## Slide 333
OBJ 4.3 · SCREENED SUBNET
The Screened Subnet (DMZ)
1
Screened subnet
A buffer network between Internet and LAN hosting the public-facing servers - web, mail, DNS.
2
Bastion host
Any machine directly exposed to the Internet - hardened to the maximum, expected to be attacked.
3
Two-firewall design
Internet -> outer firewall -> DMZ -> inner firewall -> LAN; a DMZ breach still faces a wall.
4
Why it works
If a public server is compromised, the attacker is contained in the DMZ - not inside your LAN.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
333

## Slide 334
OBJ 4.3 · FIREWALLS
Firewall Families
1
Network firewall
A dedicated device at zone boundaries filtering traffic for the whole network.
2
Host-based firewall
Software on each machine (ufw, Windows Defender FW) - the last line, per host.
3
Hardware vs software
Physical appliances at the edge; virtual/software firewalls in cloud and hosts.
4
UTM / NGFW
Unified threat management bundles firewall, IPS, AV and URL filtering in one box.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
334

## Slide 335
OBJ 4.3 · FIREWALLS
Stateless, Stateful, Application-Aware
Type
Decides on
Strength
Limit
Stateless
Ports + IPs, per packet (ACL)
Fast, simple, cheap
No conversation context
Stateful
Tracks connection state
Return traffic auto-allowed
More CPU and memory
App-aware (NGFW)
Packet content via DPI
Sees apps inside port 443
Costly; TLS inspection
WHEN IT MATTERS Most modern firewalls combine all three - ACL speed plus stateful context plus DPI.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
335

## Slide 336
OBJ 4.3 · THE GOLDEN RULE
Default deny. Allow by exception.
A firewall policy starts by blocking everything inbound, then permits only the specific ports, sources and services the business needs - the stance you build in Lab 21.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
336

## Slide 337
DOMAIN 4.0 · HANDS-ON
Host Firewall with UFW
LAB 21
Configure a default-deny host firewall with UFW: global allows, source-restricted rules, rule management.
Set a deny-by-default inbound policy with UFW, permit SSH globally and MySQL only from 10.0.0.0/8, then list, delete and disable rules to manage the firewall lifecycle.
YOU'LL BUILD
A host firewall that denies all inbound traffic except SSH and source-restricted MySQL.
TOOLCHAIN
ufw, iptables
DONE WHEN
ufw status verbose shows Default: deny (incoming), allow (outgoing) plus your 22/tcp and 3306 rules; iptables -L shows the same rules generated underneath.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
337

## Slide 338
LAB 21 · PROCESS MAP
How Lab 21 Runs
1
Install UFW
apt · step 1
2
Allow SSH first - skipping this in a
ufw · step 3
3
Enable the firewall and check the
ufw · step 4
4
Add a source-restricted rule
ufw · step 5
5
Disable the firewall when done
ufw · step 7
THE POINT
Configure a default-deny host firewall with UFW: global allows, source-restricted rules, rule management.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
338

## Slide 339
LAB 21 · VERIFY
Host Firewall with UFW
✅ Expected result
ufw status verbose shows Default: deny (incoming), allow (outgoing) plus your 22/tcp and 3306 rules; iptables -L shows the same rules generated underneath.
IF IT DOESN'T WORK
Locked out of SSH
Always allow 22/tcp before ufw enable; from the console run ufw disable, re-add the rule, re-enable
Rule never matches
Check order with ufw status numbered - more specific source rules must sit above broad ones
ufw: command not found
Install it first: apt update && apt install -y ufw
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
339

## Slide 340
OBJ 4.1 · LOGICAL SECURITY
Making TCP/IP secure.
TCP/IP was designed for openness, not secrecy - confidentiality, integrity and availability are bolted on with encryption, hashes and authentication at every layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
340

## Slide 341
OBJ 4.1 · ENCRYPTION
Encryption: In Transit vs At Rest
Data in transit
Data at rest
• Moving across the network
• TLS 1.3 for web and APIs
• IPSec or WireGuard for site links
• SSH for management sessions
• Stored on disk or in the cloud
• Full-disk encryption (LUKS, BitLocker)
• Database and object-store encryption
• Key management decides real safety
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
341

## Slide 342
OBJ 4.1 · ENCRYPTION
Symmetric Encryption
1
Cleartext
Any unencrypted data - readable by whoever captures the packet.
2
Algorithm + key
The algorithm (AES) is public and well studied; all the secrecy lives in the key.
3
Ciphertext
The scrambled output - useless to an eavesdropper without the key.
4
Same key both ways
Symmetric = one shared key encrypts AND decrypts - fast, but that key must travel safely.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
342

## Slide 343
OBJ 4.1 · ENCRYPTION
Symmetric vs Asymmetric Encryption
Symmetric
Asymmetric
Keys
One shared secret key
Public + private key pair
Speed
Fast - bulk data encryption
Slow - small payloads only
Examples
AES-256, ChaCha20
RSA-2048, ECC / Curve25519
Key exchange
Hard - secret must travel
Easy - publish the public key
Used for
Session data after handshake
Handshake, signatures, certs
WHEN IT MATTERS TLS uses both: asymmetric crypto agrees a session key, symmetric crypto carries the data.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
343

## Slide 344
OBJ 4.1 · INTEGRITY
Cryptographic Hashes
1
Fixed-size fingerprint
Any input, one fixed-length output - SHA-256 always yields 256 bits.
2
Integrity, not secrecy
A hash proves data is unchanged; it does not hide the data.
3
Avalanche effect
Change one bit of input and the entire hash changes - tampering is obvious.
4
MD5 / SHA-1 retired
Collisions have been engineered - use SHA-256 or SHA-3 today.
5
Password storage
Servers store salted hashes, never the password itself.
6
HMAC
A keyed hash proving both integrity and authenticity of a message.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
344

## Slide 345
OBJ 4.1 · TLS
The TLS 1.3 Handshake
1
ClientHello
ciphers + key share
2
ServerHello
key share + cert
3
Verify certificate
chain to trusted CA
4
Derive session keys
both sides compute
5
Encrypted data
symmetric AES/ChaCha
WHY IT MATTERS
TLS 1.3 completes in one round-trip: asymmetric crypto authenticates the server and agrees keys, then fast symmetric crypto protects the whole session.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
345

## Slide 346
OBJ 4.1 · PKI
Certificates and PKI
1
X.509 certificate
Binds a public key to an identity (CN/SAN), signed by an issuer with validity dates.
2
Certificate authority
A trusted third party that signs certificates after verifying the requester's identity.
3
Chain of trust
Leaf cert -> intermediate CA -> root CA pre-installed in every OS and browser.
4
Self-signed
Signed by its own key - fine for labs and internal tools, but every browser warns.
5
CSR
Certificate signing request - your public key plus identity, sent to the CA for signing.
6
Let's Encrypt / ACME
Free automated CA - the ACME protocol issues and renews certs every 90 days.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
346

## Slide 347
OBJ 4.1 · CERTIFICATES
Reading a Certificate with openssl x509
The certificate you generate in Lab 22, decoded field by field.
$ openssl x509 -in lab.crt -noout -text
Certificate:
Data:
Serial Number: 5d:9c:41:...:2e
Issuer: CN = lab.local
Validity
Not Before: Aug 19 02:00:00 2026 GMT
Not After : Aug 19 02:00:00 2027 GMT
Subject: CN = lab.local
Subject Public Key Info:
Public-Key: (2048 bit)
Issuer = Subject
Both read CN=lab.local - the certificate signed itself, so no browser will trust it.
Validity window
Outside Not Before / Not After the cert throws expired or not-yet-valid errors.
Public key
The RSA-2048 key clients use in the TLS handshake to agree session secrets.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
347

## Slide 348
OBJ 4.1 · CERTIFICATES
Certificate Error Scenarios
1
Self-signed warning
No CA in the chain - the browser shows ERR_CERT_AUTHORITY_INVALID.
2
Expired certificate
Past its Not After date - renew with the issuer; automate renewal with ACME.
3
Name mismatch
The CN/SAN does not match the URL's hostname - common after renames and moves.
4
Revoked certificate
The CA withdrew it - clients check live via OCSP or download CRL lists.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
348

## Slide 349
DOMAIN 4.0 · HANDS-ON
TLS Certificate with OpenSSL and Nginx
LAB 22
Generate a self-signed X.509 certificate, serve HTTPS from nginx and inspect the TLS handshake.
Create an RSA-2048 self-signed certificate with openssl req -x509, configure nginx for HTTPS on 443, then verify the handshake and certificate fields from the client with curl, openssl x509 and s_client.
YOU'LL BUILD
An HTTPS server on 443 presenting your own certificate, plus a client-side view of the TLS 1.3 handshake.
TOOLCHAIN
openssl, nginx, curl
DONE WHEN
curl -kv https://localhost prints the TLS version, cipher suite and the CN=lab.local certificate; openssl x509 -text shows identical Issuer and Subject - the mark of a self-signed cert.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
349

## Slide 350
LAB 22 · PROCESS MAP
How Lab 22 Runs
1
Install the packages
apt · step 1
2
Generate a self-signed RSA-2048 cert
openssl · step 2
3
Point nginx at the cert and key
systemctl · step 3
4
Inspect the certificate
openssl · step 5
5
Probe the live handshake with s_client
echo · step 6
THE POINT
Generate a self-signed X.509 certificate, serve HTTPS from nginx and inspect the TLS handshake.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
350

## Slide 351
LAB 22 · VERIFY
TLS Certificate with OpenSSL and Nginx
✅ Expected result
curl -kv https://localhost prints the TLS version, cipher suite and the CN=lab.local certificate; openssl x509 -text shows identical Issuer and Subject - the mark of a self-signed cert.
IF IT DOESN'T WORK
curl: SSL certificate problem
Expected for self-signed - pass -k to curl, or install a CA-signed certificate instead
nginx fails to restart
Run nginx -t to locate the config error; verify the ssl_certificate and key paths exist
Nothing listening on 443
Confirm listen 443 ssl in the server block, then check with ss -tlnp | grep 443
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
351

## Slide 352
OBJ 4.1 · IAM
Who are you, and what may you do?
Identity and access management is security's control plane: identification, authentication, authorization and accounting govern every login, port and API call.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
352

## Slide 353
OBJ 4.1 · IAM
Identification to Accounting (IAM / AAA)
1
Identification - claim an identity (username)
▶
2
Authentication - prove it (password + MFA)
▶
3
Authorization - what you may do (RBAC)
▶
4
Accounting - log what you did (audit trail)
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
353

## Slide 354
OBJ 4.1 · MFA
Multifactor Authentication (MFA)
1
Something you know
Password, PIN, passphrase - the weakest factor on its own.
2
Something you have
Phone TOTP app, smart card, hardware token (YubiKey).
3
Something you are
Biometrics - fingerprint, face, iris.
4
Somewhere you are
Location attribute - geofencing blocks logins from outside approved areas.
5
Something you do
Behavioural attributes - typing rhythm, signature dynamics.
6
MFA = 2+ DIFFERENT factors
Two passwords is not MFA; a password plus a TOTP code is.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
354

## Slide 355
OBJ 4.1 · MFA
Time-Based and Location-Based Authentication
1
Time-based OTP (TOTP)
A shared secret plus the current time yields a 6-digit code valid for 30 seconds.
2
Geofencing
Access permitted only from defined geographic areas or IP ranges.
3
Push / passkeys
FIDO2 passkeys bind the login to the genuine site - phishing-resistant MFA.
4
Least privilege
Grant the minimum rights a role needs, and remove them when the role ends.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
355

## Slide 356
OBJ 4.1 · AUTHORIZATION
Access Control Models
1
Role-based (RBAC)
Rights attach to roles/groups; users inherit by membership - the enterprise default.
2
Mandatory (MAC)
Labels and clearances fixed by policy; users cannot re-share - military and government.
3
Discretionary (DAC)
The resource owner decides who gets access - flexible, but permissions sprawl.
4
Least privilege lens
Whatever the model, grant minimum rights and review them regularly.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
356

## Slide 357
OBJ 4.1 · SSO
Single Sign-On and Federation
1
Single sign-on (SSO)
Authenticate once, access many apps - one strong login to protect with MFA.
2
SAML
XML federation: an identity provider (IdP) asserts who you are to service providers.
3
LDAP / LDAPS
Directory lookups on TCP 389; LDAPS wraps them in TLS on 636 - how apps query AD.
4
Kerberos
Ticket-based SSO in Windows domains - time-stamped tickets issued by the KDC.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
357

## Slide 358
OBJ 4.1 · AAA PROTOCOLS
RADIUS vs TACACS+
RADIUS
TACACS+
Transport
UDP 1812/1813 (or 1645/1646)
TCP 49
Encryption
Password field only
Entire payload
AAA split
AuthN + AuthZ combined
All three separated
Typical use
Wi-Fi, VPN, 802.1X access
Admin access to network gear
Origin
Open standard
Cisco (now published)
WHEN IT MATTERS Exam favourite: RADIUS = network access over UDP; TACACS+ = device administration over TCP 49.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
358

## Slide 359
OBJ 4.1 · EAP
EAP - the Authentication Framework
1
EAP
A framework, not one protocol - it carries many authentication methods inside 802.1X.
2
EAP-TLS
Certificates on both server and client - strongest, passwordless.
3
PEAP
The server's cert builds a TLS tunnel, credentials go inside - the campus Wi-Fi standard.
4
EAP-PSK / EAP-MD5
Legacy lightweight methods - avoid wherever certificates are possible.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
359

## Slide 360
OBJ 4.3 · DEVICE HARDENING
Device Hardening
1
Change default passwords
Factory admin credentials sit in every attacker's wordlist - change them on day one.
2
Disable unused services
Every listening daemon is attack surface - if nobody needs it, stop and disable it.
3
Disable unused ports
Shut idle switch ports; an unused wall jack must not be a live network drop.
4
Patch firmware
Known CVEs in network gear are scanned for within hours of disclosure.
5
Key management
Rotate SSH and API keys; revoke a leaver's keys the day they leave.
6
Secure the management plane
SSH not Telnet, HTTPS not HTTP, on a dedicated management VLAN.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
360

## Slide 361
OBJ 4.3 · HARDENING IN PRACTICE
A Hardened sshd_config
The Lab 23 end-state: keys only, limited users, tested before reload.
# /etc/ssh/sshd_config - hardened
Port 2222
PermitRootLogin prohibit-password
PasswordAuthentication no
PubkeyAuthentication yes
MaxAuthTries 3
AllowUsers admin
# validate BEFORE reloading:
$ sshd -t && systemctl reload ssh
Keys only
PasswordAuthentication no removes brute force as an attack class - keys cannot be guessed.
Blast-radius limits
AllowUsers and MaxAuthTries shrink who may try to log in, and how often.
sshd -t
Test the config before reload - a syntax error must never lock you out of a remote box.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
361

## Slide 362
DOMAIN 4.0 · HANDS-ON
SSH Hardening with Key Authentication
LAB 23
Harden SSH: Ed25519 key authentication, password login disabled, config validated before reload.
Generate an Ed25519 key pair, install the public key in authorized_keys, prove key login works, then disable PasswordAuthentication in sshd_config, validate with sshd -t and confirm password login is refused.
YOU'LL BUILD
An SSH daemon that accepts only public-key authentication, with root password login prohibited.
TOOLCHAIN
openssh-server, openssh-client, ssh-keygen
DONE WHEN
Key login returns root with no password prompt; forcing password authentication returns Permission denied (publickey).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
362

## Slide 363
LAB 23 · PROCESS MAP
How Lab 23 Runs
1
Generate an Ed25519 key pair
ssh-keygen · step 1
2
Test key-based login - no password
ssh · step 3
3
Disable password authentication in
sed · step 4
4
Validate the config
sshd · step 5
5
Discuss bonus hardening
Step 7 of 7
THE POINT
Harden SSH: Ed25519 key authentication, password login disabled, config validated before reload.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
363

## Slide 364
LAB 23 · VERIFY
SSH Hardening with Key Authentication
✅ Expected result
Key login returns root with no password prompt; forcing password authentication returns Permission denied (publickey).
IF IT DOESN'T WORK
Permission denied with the key
Fix permissions: chmod 700 ~/.ssh and chmod 600 ~/.ssh/authorized_keys - sshd refuses lax modes
sshd -t reports errors
Fix the reported line in /etc/ssh/sshd_config before reloading - a bad config can lock you out
Password login still works
Check override files in /etc/ssh/sshd_config.d/ for PasswordAuthentication yes, then reload ssh
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
364

## Slide 365
OBJ 4.1 · ENCRYPTION IN TRANSIT
VPN - Extending the Trusted Zone
1
Site-to-site VPN
Routers or firewalls tunnel whole networks together across the Internet.
2
Client-to-site
Remote access - a laptop joins the corporate network from anywhere.
3
IPSec
AH/ESP with IKE key exchange - the classic standard: rich, interoperable, complex.
4
WireGuard
Modern and tiny: Curve25519 key pairs, no PKI needed - what you build in Lab 24.
5
Split vs full tunnel
Route everything through the VPN, or only the corporate subnets.
6
Why it matters
A VPN extends the trusted zone across an untrusted network - encryption in transit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
365

## Slide 366
OBJ 4.1 · ENCRYPTION IN TRANSIT
VPN Technologies Compared
IPSec
TLS VPN
WireGuard
Layer
Network (L3)
Session (TLS)
Network (L3)
Keys
IKE + certs / PSK
X.509 certificates
Static 32-byte key pairs
Codebase
Large, complex
Large (OpenVPN)
Tiny (~4k lines)
Speed
Good (HW offload)
Moderate
Excellent
Best for
Standards, site-to-site
Remote access via 443
Modern deployments
WHEN IT MATTERS WireGuard's allowed-ips doubles as a routing rule AND an inbound ACL - you will see this in Lab 24.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
366

## Slide 367
DOMAIN 4.0 · HANDS-ON
Site-to-Site VPN with WireGuard
LAB 24
Build a site-to-site WireGuard tunnel between two network namespaces and verify the handshake.
Create two namespaces as VPN endpoints, generate Curve25519 key pairs, configure wg0 interfaces with peer public keys and allowed-ips, bring the tunnel up, ping across it and inspect handshake state with wg show.
YOU'LL BUILD
An encrypted point-to-point tunnel (10.99.0.1 <-> 10.99.0.2) between two namespaces acting as two sites.
TOOLCHAIN
wireguard, wireguard-tools, iproute2
DONE WHEN
ping -c2 10.99.0.1 from site-b succeeds through the tunnel; wg show reports the peer public key, a recent handshake time and rising transfer counters.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
367

## Slide 368
LAB 24 · PROCESS MAP
How Lab 24 Runs
1
Install WireGuard
apt · step 1
2
Generate a key pair for each peer
wg · step 3
3
Assign the tunnel addresses
ip · step 5
4
Ping site-a across the encrypted
ip · step 8
5
Clean up namespaces and key files
ip · step 10
THE POINT
Build a site-to-site WireGuard tunnel between two network namespaces and verify the handshake.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
368

## Slide 369
LAB 24 · VERIFY
Site-to-Site VPN with WireGuard
✅ Expected result
ping -c2 10.99.0.1 from site-b succeeds through the tunnel; wg show reports the peer public key, a recent handshake time and rising transfer counters.
IF IT DOESN'T WORK
Ping fails across the tunnel
Check wg show for a handshake; verify each peer entry uses the other side's PUBLIC key
wg show shows no handshake
Confirm site-b's endpoint 127.0.0.1:51820 matches site-a's listen-port, and allowed-ips cover the peer /32
wg0 already exists
Stale run - delete with ip netns del site-a && ip netns del site-b and recreate
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
369

## Slide 370
OBJ 4.3 · ATTACK SURFACE
Every open port is a doorway.
Attack-surface reduction is the cheapest security win: enumerate what is listening, ask why it is there, and disable what nobody needs - before an attacker does the asking.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
370

## Slide 371
OBJ 4.2 · MALWARE
Malware Taxonomy
1
Virus / worm
A virus infects files; a worm self-propagates across the network unaided.
2
Trojan / RAT
Hides inside legitimate-looking software; a RAT hands the attacker remote control.
3
Ransomware
Encrypts your data and demands payment - today's top business threat.
4
Spyware / keylogger
Silently collects keystrokes, credentials and screen contents.
5
Rootkit
Buries itself under the OS to hide processes and survive detection.
6
Logic bomb
Dormant code that triggers on a date or event - often an insider plant.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
371

## Slide 372
OBJ 4.2 · SOCIAL ENGINEERING
Social Engineering
1
Phishing
Fraudulent mail and sites harvest credentials; spear phishing targets a person, whaling an exec.
2
Dumpster diving
Discarded printouts leak configs and passwords - shred everything.
3
Shoulder surfing
Watching screens and keypads - privacy filters and awareness defeat it.
4
Tailgating
Following a badge-holder through a secure door - vestibules stop it.
5
Impersonation
The fake IT-support call that just needs your password to help you.
6
Defence = education
Humans are part of the perimeter: train, phish-test, make reporting easy.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
372

## Slide 373
OBJ 4.2 · PASSWORD ATTACKS
Password Attacks
1
Brute force
Try every combination - length beats complexity; each extra character multiplies the work.
2
Dictionary
Try likely words and leaked passwords first - most humans are predictable.
3
Credential stuffing
Replay leaked username/password pairs on other sites - MFA breaks it.
4
Defences
Long passphrases, lockout policies, salted hashes, MFA everywhere.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
373

## Slide 374
OBJ 4.3 · ATTACK SURFACE
Vulnerability Management Loop
1
Scan the estate for exposed services
▶
2
Prioritise by CVSS score and exploitability
▶
3
Patch on a defined cadence with change control
▶
4
Re-scan to verify the exposure is closed
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
374

## Slide 375
DOMAIN 4.0 · HANDS-ON
Port Scanning and Service Hardening
LAB 25
Enumerate exposed services with nmap and reduce the attack surface by disabling what is unneeded.
SYN-scan all 65535 TCP ports on your own host, identify service versions and the OS, cross-check each open port against ss -tulnp, disable an unnecessary service and re-scan to confirm the port is closed.
YOU'LL BUILD
A port-by-port inventory of your host's attack surface, with an unneeded service disabled and verified closed.
TOOLCHAIN
nmap, ss, systemctl
DONE WHEN
The final nmap -sS -p 80 scan reports the port closed, and ss -tulnp no longer lists the disabled service - the attack surface measurably shrank.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
375

## Slide 376
LAB 25 · PROCESS MAP
How Lab 25 Runs
1
Install nmap
apt · step 1
2
Enumerate service versions
nmap · step 3
3
Fingerprint the operating system
nmap · step 4
4
Cross-check every open port against
ss · step 5
5
Re-scan to confirm the port is now
nmap · step 7
THE POINT
Enumerate exposed services with nmap and reduce the attack surface by disabling what is unneeded.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
376

## Slide 377
LAB 25 · VERIFY
Port Scanning and Service Hardening
✅ Expected result
The final nmap -sS -p 80 scan reports the port closed, and ss -tulnp no longer lists the disabled service - the attack surface measurably shrank.
IF IT DOESN'T WORK
Scan takes very long
-p- probes 65535 ports; in the lab scan a shortlist such as -p 1-1024 instead
nmap -O gives no result
OS fingerprinting needs root privileges and at least one open and one closed port
Port still open after disable
Another process owns it - find the PID with ss -tulnp and stop that unit too
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
377

## Slide 378
OBJ 4.2 · TYPES OF ATTACKS
Attack Catalogue: Vector, Layer, Defence
Attack
Layer
How it works
Primary defence
DoS / DDoS
3-7
Botnet floods links or servers
Scrubbing, rate limits
MAC flooding
2
Overflow CAM table; switch floods
Port security limits
ARP poisoning
2
Forged replies put attacker on-path
Dynamic ARP Inspection
VLAN hopping
2
Double tags / fake trunk cross VLANs
No native VLAN, no DTP
DNS poisoning
7
Fake records redirect victims
DNSSEC, patched resolvers
Evil twin
1-2
Cloned SSID captures clients
802.1X, WIPS monitoring
WHEN IT MATTERS For every attack, know the layer it lives at - the defence always sits at the same layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
378

## Slide 379
OBJ 4.2 · DoS/DDoS
DoS and DDoS in Depth
1
Botnet and C2
Compromised zombies take orders from a command-and-control server.
2
Volumetric
Saturate the pipe - UDP floods, amplification via open DNS/NTP servers.
3
Protocol attack
Exhaust state tables - SYN floods hold thousands of half-open connections.
4
Application attack
Cheap requests, expensive responses - HTTP floods and Slowloris.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
379

## Slide 380
OBJ 4.2 · ON-PATH ATTACKS
Anatomy of an ARP Poisoning Attack
1
Recon
attacker joins the LAN
2
Poison
forged ARP replies sent
3
On-path
victim traffic redirected
4
Harvest
credentials sniffed
5
Defend
DAI drops forged ARP
BREAK THE CHAIN
Dynamic ARP Inspection validates every ARP reply against the DHCP snooping binding table - forged replies are dropped at the switch port.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
380

## Slide 381
OBJ 4.2 · VLAN HOPPING
VLAN Hopping
1
Switch spoofing
The attacker negotiates a trunk via DTP and receives every VLAN - disable DTP, set access mode.
2
Double tagging
Outer tag stripped on the native VLAN, inner tag delivers into the victim VLAN - one-way but real.
3
Native VLAN hygiene
Use a dedicated, unused native VLAN; never carry user traffic on it.
4
Private VLANs
Port isolation stops peer-to-peer traffic even inside the same VLAN.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
381

## Slide 382
OBJ 4.2 · ROGUE DEVICES
Rogue Devices and On-Path Attacks
1
Rogue DHCP server
Hands out attacker-controlled gateway/DNS - a lease outside your network ID is the tell.
2
Rogue AP
An unauthorised access point bridging outsiders straight into the LAN.
3
Evil twin
A cloned corporate SSID; clients auto-join and their traffic is captured.
4
On-path (MITM)
The attacker relays between two parties, reading or altering everything.
5
Defence: snooping + 802.1X
DHCP snooping drops rogue offers; port authentication blocks rogue gear.
6
Defence: WIPS
Wireless IPS detects unknown SSIDs and contains rogue radios.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
382

## Slide 383
OBJ 4.2 · SPOOFING
Spoofing Attacks
1
MAC spoofing
Clone an allowed MAC address to slip past port filters.
2
IP spoofing
Forge the source address - the engine behind amplification DDoS.
3
DNS spoofing / poisoning
Corrupt resolver caches so good names resolve to bad hosts.
4
Defences
Ingress filtering (BCP 38), DNSSEC validation, Dynamic ARP Inspection.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
383

## Slide 384
OBJ 4.3 · NETWORK HARDENING
Switch and Network Hardening
1
DHCP snooping
Only trusted uplink ports may send DHCP offers - kills rogue DHCP.
2
Dynamic ARP Inspection
Validates ARP against the snooping bindings - kills ARP poisoning.
3
Port security
Limit MACs per port, err-disable on violation - kills MAC flooding.
4
RA guard
Blocks rogue IPv6 router advertisements at access ports.
5
Control plane policing
Rate-limits traffic to the device CPU so it survives a DoS.
6
Disable unused ports
A patch-panel jack nobody uses should terminate nowhere.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
384

## Slide 385
OBJ 4.3 · NAC
802.1X Network Access Control
1
Supplicant
device asks to join
2
Authenticator
switch relays EAP
3
RADIUS server
credentials checked
4
Posture check
patch level verified
5
VLAN assigned
access or quarantine
WHY IT MATTERS
Nothing gets a usable port until identity and device health are proven - NAC turns every access port and SSID into a checkpoint.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
385

## Slide 386
OBJ 4.1 · SEGMENTATION
Segmentation Enforcement Zones
Zone
What lives there
Why segregate it
IoT
Cameras, sensors, smart devices
Rarely patched; assume compromised
IIoT / OT
Industrial sensors, actuators
Uptime-critical; no direct IT access
SCADA / ICS
Plant supervisory control
Legacy protocols with no auth
Guest
Visitor phones and laptops
Internet only - zero internal reach
BYOD
Staff personal devices
Unmanaged; NAC posture, limited access
WHEN IT MATTERS Segment by trust and blast radius: a hacked camera must never see the finance VLAN.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
386

## Slide 387
OBJ 4.1 · DECEPTION
Deception Technologies
1
Honeypot
A deliberately vulnerable decoy host - any touch on it is by definition suspicious.
2
Honeynet
A whole decoy network of honeypots modelling your real estate.
3
Why deceive
Attackers burn time on fakes while defenders harvest indicators and early warning.
4
Placement
In the screened subnet or a dedicated VLAN - never among production data.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
387

## Slide 388
OBJ 4.3 · IDS/IPS
IDS or IPS - Where Does the Sensor Sit?
Should the sensor sit inline and block, or watch a copy and alert?
INLINE - IPS
Sits in the traffic path and drops malicious packets in real time. Risk: a false positive blocks legitimate traffic; adds latency.
PASSIVE - IDS
Watches a mirror/TAP copy and raises alerts for analysts. No traffic risk, but detection only - response is manual.
Suricata can run either mode - Lab 26 runs it passively as an IDS on eth0.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
388

## Slide 389
OBJ 4.3 · IDS/IPS
How IDS/IPS Detect
1
Signature-based
Match known patterns (ET rules) - precise, but blind to novel attacks.
2
Anomaly-based
Baseline normal, alert on deviation - catches zero-days, more false positives.
3
Rule feeds
Emerging Threats and Snort VRT keep signatures current - update daily.
4
Where alerts land
Suricata writes fast.log for humans and eve.json for SIEM pipelines.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
389

## Slide 390
OBJ 4.3 · IDS IN PRACTICE
Reading a Suricata Alert (eve.json)
The alert you trigger in Lab 26, as the JSON event your SIEM ingests.
$ cat eve.json | jq 'select(.event_type=="alert")'
{
"timestamp": "2026-08-19T10:42:07+0800",
"event_type": "alert",
"src_ip": "203.0.113.99",
"dest_ip": "10.0.0.5",
"alert": {
"signature": "GPL ATTACK_RESPONSE
id check returned root",
"category": "Potentially Bad Traffic",
"severity": 2
}
}
event_type
One JSON object per event - jq filters alerts out of the flow, DNS and TLS records.
signature
The ET rule that fired: the HTTP response contained uid=0(root) - a compromise tell.
src / dest
Who attacked whom - the fields a SIEM correlates across all your sensors.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
390

## Slide 391
DOMAIN 4.0 · HANDS-ON
Intrusion Detection with Suricata
LAB 26
Run Suricata as an IDS, trigger a known signature and read the alert in fast.log and eve.json.
Install Suricata, pull the Emerging Threats ruleset, start the engine on eth0, generate benign trigger traffic from testmynids.org, then trace the resulting alert through fast.log and the JSON eve.json event stream.
YOU'LL BUILD
A live IDS on eth0 with a current ET ruleset, plus a captured alert you can parse as JSON with jq.
TOOLCHAIN
suricata, suricata-update, jq, curl, TIS Cybersecurity Simulator
DONE WHEN
fast.log shows an alert like GPL ATTACK_RESPONSE id check returned root; filtering eve.json for event_type alert returns the same event with src/dest IPs and severity.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
391

## Slide 392
LAB 26 · PROCESS MAP
How Lab 26 Runs
1
Install Suricata and jq
apt · step 1
2
Start Suricata as a daemon
suricata · step 3
3
Trigger a well-known test signature
curl · step 5
4
Filter the same alert from the
cat · step 7
5
Stop Suricata
pkill · step 9
THE POINT
Run Suricata as an IDS, trigger a known signature and read the alert in fast.log and eve.json.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
392

## Slide 393
LAB 26 · VERIFY
Intrusion Detection with Suricata
✅ Expected result
fast.log shows an alert like GPL ATTACK_RESPONSE id check returned root; filtering eve.json for event_type alert returns the same event with src/dest IPs and severity.
IF IT DOESN'T WORK
No alerts appear
Confirm Suricata listens on the right interface (check ip a), then re-run the testmynids curl
suricata-update fails
Check Internet access - the rules download from the Emerging Threats feed
eve.json is empty
Give the engine a few seconds after the trigger; check suricata.log for startup errors
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
393

## Slide 394
OBJ 4.3 · ACL
Access Control Lists (ACLs)
1
Top-down evaluation
Rules are checked in order; the FIRST match wins and processing stops.
2
Implicit deny
Whatever no rule matches is dropped - place your permits above the deny.
3
Match criteria
Source and destination IP, protocol, port - the classic 5-tuple.
4
Where ACLs live
Router interfaces, switch VLANs, cloud security groups, iptables chains.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
394

## Slide 395
OBJ 4.3 · ACL IN PRACTICE
An iptables ACL, Line by Line
The Lab 27 rule set: permit MySQL from one subnet, drop the rest.
$ iptables -I INPUT -p tcp --dport 3306 \
-s 10.0.0.0/24 -j ACCEPT
$ iptables -A INPUT -p tcp --dport 3306 -j DROP
$ iptables -L INPUT -n -v --line-numbers
num target prot source dpt
1 ACCEPT tcp 10.0.0.0/24 3306
2 DROP tcp 0.0.0.0/0 3306
-I vs -A
-I inserts at the top, -A appends at the bottom - placement decides what matches first.
First match wins
10.0.0.0/24 hits rule 1 and is accepted; everyone else falls through to the DROP.
Scope
Only port 3306 is filtered here - pair with a default-deny policy for real hardening.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
395

## Slide 396
OBJ 4.3 · CONTENT FILTERING
URL and Content Filtering
1
URL filtering
Allow or block by domain and category - malware, phishing, gambling lists.
2
Content filtering
Inspect payloads - DLP stops card numbers leaving; AV strips attachments.
3
DNS filtering
The cheapest control: a resolver that refuses to resolve known-bad domains.
4
TLS inspection
Filtering encrypted traffic needs a re-signing proxy - governance required.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
396

## Slide 397
DOMAIN 4.0 · HANDS-ON
Building an ACL with iptables
LAB 27
Build an ordered iptables ACL that permits MySQL from one subnet and drops it from everywhere else.
Insert an ACCEPT rule for TCP 3306 from 10.0.0.0/24 above an appended DROP, verify ordering with --line-numbers, test both paths with nc from allowed and blocked sources, then persist the rules across reboots.
YOU'LL BUILD
A working two-rule ACL on the INPUT chain proving top-down, first-match evaluation, saved to survive reboot.
TOOLCHAIN
iptables, netcat, iptables-persistent
DONE WHEN
The probe from a blocked source hangs (dropped); the probe from 10.0.0.5 gets an instant refused/RST - accepted by the ACL, nothing listening. The filter demonstrably works.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
397

## Slide 398
LAB 27 · PROCESS MAP
How Lab 27 Runs
1
Inspect the current INPUT chain
iptables · step 1
2
Append
iptables · step 3
3
Test from a blocked source
nc · step 5
4
Add an allowed source address and
ip · step 6
5
Clean up
iptables · step 8
THE POINT
Build an ordered iptables ACL that permits MySQL from one subnet and drops it from everywhere else.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
398

## Slide 399
LAB 27 · VERIFY
Building an ACL with iptables
✅ Expected result
The probe from a blocked source hangs (dropped); the probe from 10.0.0.5 gets an instant refused/RST - accepted by the ACL, nothing listening. The filter demonstrably works.
IF IT DOESN'T WORK
ACL never blocks anything
The ACCEPT may sit below the DROP - first match wins; verify order with --line-numbers
Rules vanish after reboot
Install iptables-persistent and run netfilter-persistent save to write /etc/iptables/rules.v4
nc test looks inconclusive
With no MySQL listening, allowed sources see instant RST (refused); dropped sources see a timeout
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
399

## Slide 400
OBJ 4.1 · PHYSICAL SECURITY
Physical Security
1
Cameras (CCTV)
Detective control - record and deter; cover entrances, corridors and racks.
2
Locks
Preventive - server rooms, racks and cages; smart locks log every entry.
3
Badge readers
Authenticate entry per person and leave an audit trail.
4
Access control vestibule
A two-door airlock defeats tailgating - one person per badge.
5
Security guards
Flexible deterrent and response - verify visitors and deliveries.
6
Environmental sensors
Door-open, temperature and humidity alarms in the data centre.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
400

## Slide 401
OBJ 4.1 · PHYSICAL SECURITY
Physical Control Categories
Preventive
• Stop the event: locks, MFA, firewalls
• Access control vestibules
• Strongest when layered together
Detective
• Discover the event: CCTV, IDS, logs
• Audits and SIEM alerting
• Enables fast, informed response
Deterrent / compensating
• Warning signs, visible cameras
• Guards deter casual attempts
• Compensating controls cover gaps
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
401

## Slide 402
OBJ 4.1 · ASSET LIFECYCLE
System Life Cycle and Secure Disposal
1
Asset tags and inventory
You cannot secure what you do not track - tag and record every device.
2
Secure wipe
DoD 5220.22-M-style overwrite or crypto-erase before any disposal.
3
Factory reset
Acceptable only for devices that never held sensitive data.
4
Chain of custody
A documented audit trail from decommission to certified destruction.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
402

## Slide 403
DOMAIN 4 · EXAM CHECKPOINT
Exam Checkpoint - Numbers to Memorise
• RADIUS: UDP 1812/1813 (legacy 1645/1646) - TACACS+: TCP 49
• LDAP 389, LDAPS 636, Kerberos 88, HTTPS 443, SSH 22
• IDS detects on a mirror copy; IPS sits inline and blocks
• Screened subnet (DMZ) hosts public services between two firewalls
• MFA needs two DIFFERENT factors: know / have / are
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
403

## Slide 404
DOMAIN 4 · RECAP
Layers, least privilege, verify everything.
Domain 4 in one line: encrypt in transit and at rest, authenticate with multiple factors, segment aggressively, harden every device, and watch the logs.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
404

## Slide 405
DOMAIN 4.0 RECAP
Recap — Network Security
• You can now: Configure a default-deny host firewall with UFW: global allows, source-restricted rules, rule management.
• You can now: Generate a self-signed X.509 certificate, serve HTTPS from nginx and inspect the TLS handshake.
• You can now: Harden SSH: Ed25519 key authentication, password login disabled, config validated before reload.
• You can now: Build a site-to-site WireGuard tunnel between two network namespaces and verify the handshake.
• You can now: Enumerate exposed services with nmap and reduce the attack surface by disabling what is unneeded.
• You can now: Run Suricata as an IDS, trigger a known signature and read the alert in fast.log and eve.json.
• You can now: Build an ordered iptables ACL that permits MySQL from one subnet and drops it from everywhere else.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
405

## Slide 406
DOMAIN 5.0 · 24% OF THE EXAM
Network Troubleshooting
Methodology · cabling & physical interfaces · network services · performance · tools
5.0
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
406

## Slide 407
WHAT YOU'LL DO
Hands-On Labs — Network Troubleshooting
Labs 28–30
• Layer 1/2 Diagnostics with ip and ethtool
• Reachability with ping, traceroute and mtr
• DNS Troubleshooting with dig and resolvectl
Labs 31–33
• ARP and the IPv6 Neighbour Table
• Packet Capture with tcpdump and TIS PCAP Analyzer
• MTU and Path-MTU Discovery
Labs 34–36
• Diagnosing Routing Problems
• Simulating Slow and Lossy Links with tc
• Service Reachability Triage with curl, nc and openssl
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
407

## Slide 408
DOMAIN 5 · 24% OF THE EXAM
Network Troubleshooting.
Domain 5 is 24% of the N10-009 exam - the biggest single slice. Master one method, then apply it to cables, switches, routes, DNS and services.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
408

## Slide 409
OBJ 5.1 · METHODOLOGY
Why a Method Beats Guesswork
1
Symptoms are not causes
A 'slow website' can be DNS, routing, loss, MTU or the app itself - the method finds which before you change anything.
2
Gather before you touch
Information gathered first - symptoms, scope, timing - is evidence; information gathered after a change is contaminated.
3
The OSI model is your map
Every fault lives at a layer; walking the stack top-down, bottom-up or from the middle turns chaos into a search.
4
Change one thing at a time
Isolate variables - if you change three things and it works, you still do not know the cause and cannot prevent it.
5
Prevention is part of the fix
A ticket is not closed at 'it works' - it closes at 'it cannot happen again', or at least 'we will see it coming'.
6
Documentation compounds
Yesterday's documented outage is today's 10-minute fix - lessons learned are the cheapest training you will get.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
409

## Slide 410
OBJ 5.1 · METHODOLOGY
CompTIA's 7-Step Troubleshooting Method
1
1 · Identify the problem
gather, question, dupe
2
2 · Establish a theory
probable cause
3
3 · Test the theory
confirm or re-theorise
4
4+5 · Plan and implement
or escalate
5
6 · Verify
full functionality
6
7 · Document
lessons learned
WHY IT MATTERS
Exam scenario questions state which step you are in and ask for the next action - knowing the order is free marks.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
410

## Slide 411
OBJ 5.1 · METHODOLOGY
Step 1 - Identify the Problem
1
Gather information
Ticket text, monitoring alerts, logs, topology diagrams - collect the facts before forming any opinion.
2
Question users
Ask open questions first ('what were you doing?'), then closed ones ('does it fail on Wi-Fi too?').
3
Identify symptoms
Pin down exactly what fails, for whom, since when and how often - 'the internet is down' is never the real symptom.
4
Determine if anything changed
New firmware, a moved desk, a patch window, a new switch - most outages follow a change.
5
Duplicate the problem
If you can reproduce it on demand, you can test theories against it safely and prove the eventual fix.
6
Approach problems individually
Two simultaneous complaints may be two faults - splitting them avoids chasing a cause that explains only half.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
411

## Slide 412
OBJ 5.1 · METHODOLOGY
Questioning Users and Finding the Change
Ask the user
Ask the environment
• What exactly do you see - error text, spinner, timeout?
• When did it last work, and what changed since?
• Does it affect one app, one site or everything?
• Are colleagues nearby affected too?
• Does it follow you to another desk or network?
• Check the change log and maintenance windows
• Compare against monitoring baselines and alerts
• Did patching, firmware or config pushes run overnight?
• Look for moved equipment, new cables, new devices
• Scope it: one user, one switch, one VLAN or one site?
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
412

## Slide 413
OBJ 5.1 · METHODOLOGY
Step 2 - Establish a Theory of Probable Cause
1
Question the obvious
Cable seated? Power on? Right SSID? Caps Lock? The embarrassing causes are the most common - eliminate them first.
2
Top-to-bottom OSI
Start at L7 and walk down - natural when the app clearly fails but the network looks healthy.
3
Bottom-to-top OSI
Start at L1 and walk up - natural for a single dead desk: cable, link light, then IP, then services.
4
Divide and conquer
Start mid-stack: ping the gateway. Success rules out L1-L3 locally; failure rules out everything above.
5
Consider multiple approaches
Hold more than one candidate theory and rank them by likelihood and by how cheap they are to test.
6
Use scope as evidence
One user points down the stack at their gear; a whole site points up at shared infrastructure - WAN, DNS, DHCP, core.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
413

## Slide 414
OBJ 5.1 · METHODOLOGY
Divide and Conquer - Where to Start
A user cannot reach the app. Are other users affected too?
YES - start in the middle
Shared infrastructure is suspect. Ping the gateway and a known IP: works means look up (DNS, app); fails means look down (L1-L3).
NO - start at the bottom
A single victim is usually local. Check cable and link light, then IP/mask/gateway, then walk up the stack layer by layer.
Divide and conquer halves the search space with every test - the binary search of troubleshooting.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
414

## Slide 415
OBJ 5.1 · METHODOLOGY
Step 3 - Test the Theory
Theory confirmed
• Determine the next steps to resolve
• Move straight to a plan of action
• Record what proved the cause
Theory busted
• Re-establish a new theory
• Re-question the obvious
• Widen the scope of what you test
Beyond your access or skill
• Escalate - do not keep digging
• Hand over the evidence so far
• List the tests already performed
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
415

## Slide 416
OBJ 5.1 · METHODOLOGY
Steps 4 and 5 - Plan, Implement or Escalate
1
Plan before you touch
Write the steps, the order, and who does what - a fix applied ad hoc at 2 a.m. becomes tomorrow's mystery config.
2
Identify potential effects
Will the fix drop users, restart services, or trigger STP recalculation? Say so before it happens.
3
Schedule the change
Non-urgent fixes go in a change window with approval; outage fixes still get a one-line plan first.
4
Prepare the rollback
Know how to undo the change before you make it - save the running config, snapshot, or note the old value.
5
Implement or escalate
Execute your plan - or hand it to the vendor, ISP or senior engineer if it exceeds your authority or access.
6
Verify as you go
Test after each step of the plan, not only at the end, so a failed step is caught immediately.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
416

## Slide 417
OBJ 5.1 · METHODOLOGY
Steps 6 and 7 - Verify and Document
1
Verify FULL functionality
Test more than the reported symptom - the user's app, neighbours on the same switch, and anything your change touched.
2
Have the user confirm
The ticket closes when the reporter agrees it works, not when your ping succeeds.
3
Implement preventive measures
Monitoring alerts, config backups, UPS, spare cables, tightened change control - stop the repeat.
4
Document findings
What was broken and what the root cause was - written for the next engineer, not for yourself.
5
Document actions and outcomes
Exactly what was changed, where, and the result - this becomes tomorrow's change log.
6
Capture lessons learned
What slowed the diagnosis? What would have caught it sooner? Feed that into runbooks and training.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
417

## Slide 418
OBJ 5.1 · METHODOLOGY
The 7 Steps at a Glance
Step
Goal
Key actions
1 Identify
Know the real problem
Gather info, question users, what changed?
2 Theorise
Rank probable causes
Question the obvious; walk the OSI stack
3 Test
Confirm or discard
Prove the theory, re-theorise or escalate
4+5 Plan + implement
Fix safely
Plan steps and effects; act or escalate
6 Verify
Whole system works
Full functionality + preventive measures
7 Document
Keep the knowledge
Findings, actions, outcomes, lessons
WHEN IT MATTERS Exam questions quote a scenario mid-flow and ask for the NEXT step - learn the order cold.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
418

## Slide 419
OBJ 5.1 · METHODOLOGY
Symptom to Layer to First Tool
Layer
Typical symptom
First tool to reach for
L1 Physical
No link light, error counters climb
Cable tester, ethtool, link LEDs
L2 Data Link
Floods, loops, VLAN oddities
ip neigh / arp, switch counters
L3 Network
Some destinations unreachable
ping, traceroute/mtr, ip route
L4 Transport
Connects to some ports only
nc -zv, ss -tlnp, firewall rules
L7 Application
TCP fine but service errors
curl -v, dig, server logs
WHEN IT MATTERS Pick the layer the symptom names, test there, then move up or down on the result.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
419

## Slide 420
OBJ 5.1 · METHODOLOGY
The Method in 60 Seconds - a Dry Run
1
Identify: one user, wired, no web since desk move
▶
2
Theory: cable damaged in the move (L1 first)
▶
3
Test: swap patch lead - link light returns
▶
4
Plan+fix: replace lead, label the run
▶
5
Verify + document: user confirms, ticket notes
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
420

## Slide 421
OBJ 5.2 · CABLING & INTERFACES
Physical first: most 'network down' calls end at a cable.
Objective 5.2: cabling faults, interface errors and hardware issues - the layer where troubleshooting most often starts and ends.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
421

## Slide 422
OBJ 5.2 · CABLING
Incorrect Cable Type
1
Wrong Cat rating
Cat 5e on a 10G link negotiates down or throws errors - match the category to the speed and the run length.
2
UTP where STP is needed
Unshielded cable beside motors, lifts or fluorescent ballasts picks up EMI - shielded (STP) or a new path fixes it.
3
Single-mode vs multimode
SMF (yellow, laser, long haul) and MMF (aqua/orange, short haul) do not mix - and neither do their transceivers.
4
TX/RX transposed
Fibre pair crossed at one end: both link lights stay dark. Flip the pair at ONE end only.
5
Copper vs fibre reach
UTP tops out at 100 m per horizontal run (EIA/TIA allows 90 m + patch); beyond that use fibre or add a switch.
6
The jacket tells a story
Read the print on the cable jacket - Cat level, shielding and plenum rating are all written on it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
422

## Slide 423
OBJ 5.2 · CABLING
Signal Degradation
1
Attenuation
Signal weakens with distance - runs past spec show as errors and negotiated-down speeds, worst at higher frequencies.
2
Crosstalk
Signal bleeding between pairs, usually from sloppy termination - pairs untwisted too far at the plug.
3
NEXT and FEXT
Near-end crosstalk is measured at the transmitter end, far-end at the receiver - certifiers report both in dB.
4
EMI / interference
Motors, HVAC, power runs and fluorescent lighting induce noise into copper - reroute the cable or shield it.
5
dB loss on fibre
Dirty connectors, tight bends and bad splices eat the optical budget - measure with an optical power meter.
6
The symptom pattern
Degradation rarely kills a link outright - it shows as CRC errors, retransmissions and 'slow' complaints.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
423

## Slide 424
OBJ 5.2 · CABLING
Improper Termination
1
T568A/B mixed ends
One end A, the other B makes an accidental crossover - modern MDI-X often saves you, but certifiers flag it.
2
Split pairs
Wires landed so a circuit uses conductors from two different twisted pairs - passes continuity, fails at speed.
3
Untwisted too far
More than ~13 mm untwisted at the punch-down or plug invites crosstalk - re-twist and re-terminate.
4
Bad punch-down / loose IDC
Half-seated conductors at the patch panel work intermittently - the classic 'wiggle the cable' fault.
5
Damaged RJ45 latch
A broken retention clip lets the plug back out of the jack - the link drops when anyone touches the desk.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
424

## Slide 425
OBJ 5.2 · CABLING
Cable Faults vs Tester Results
Fault
Wiremap / tester shows
Typical cause
Open
Pin fails continuity
Break or unpunched conductor
Short
Two pins joined
Crushed jacket, stray strand
Split pair
Map OK, NEXT fails
Pairs mis-landed on pins
Reversed pair
Pair order flipped
A/B mix at one end
Crossed pairs
1-2 swapped with 3-6
Crossover lead in the run
Excess length
Run over 90-100 m
TDR shows distance vs spec
WHEN IT MATTERS Wiremap finds opens, shorts and miswires; a TDR adds the distance to the fault.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
425

## Slide 426
OBJ 5.5 · TOOLS
Cable Test Instruments
1
Cable tester / wiremap
Confirms each of the 8 pins lands on the right pin at the far end and continuity exists - first tool on any drop.
2
Continuity test
Shows whether the conductor is broken anywhere along the run - a pass means the copper path is complete.
3
TDR
Time domain reflectometer - fires a pulse and times the echo to report cable length and the distance to a break.
4
OTDR
The optical TDR for fibre - locates breaks, bad splices and dirty connectors along a fibre run.
5
Cable certifier
Measures NEXT/FEXT, attenuation and return loss against the Cat spec - proves a run earns its rating.
6
Optical power meter
Measures received light in dBm - the tool for weak-signal and dirty-connector fibre faults.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
426

## Slide 427
OBJ 5.5 · TOOLS
Locating and Verifying: Toner, Loopback, Multimeter
1
Tone generator
Injects a signal onto a pair at one end - the 'Fox' of the classic Fox & Hound pair.
2
Tone probe
Held near cables, it sings when it finds the toned pair - traces unlabeled runs through walls and bundles.
3
Loopback plug
Loops TX back to RX so a NIC or switch port tests its own send/receive path in isolation.
4
Loopback address
127.0.0.1 (::1 in IPv6) tests the local IP stack with no cable at all - can this host even talk to itself?
5
Multimeter
Voltage, current, resistance and continuity - the tool for PoE voltage checks and suspect power.
6
Voltage monitor / UPS
Logs sags and drops in supply power - unexplained rack reboots are a power problem until proven otherwise.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
427

## Slide 428
OBJ 5.2 · INTERFACES
Reading Port Status
Status
Meaning
Your move
up / up
Admin up, carrier present
Healthy - look elsewhere
up / down
Enabled but no carrier
Cable, far end, transceiver
LOWERLAYERDOWN
Linux: no carrier sensed
Check the physical path
admin down
Deliberately disabled
no shutdown / ip link set up
err-disabled
Switch shut it on error
Fix the cause, then re-enable
WHEN IT MATTERS err-disabled common causes: port-security violation, BPDU guard, link flapping.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
428

## Slide 429
OBJ 5.2 · INTERFACES
Interface Error Counters
1
CRC errors
Frames that fail the checksum - bad cable, noise or duplex mismatch; any steadily climbing count is a fault.
2
Runts
Frames under 64 bytes, usually collision fragments - the classic signature of a duplex mismatch.
3
Giants
Frames over the MTU - typically an MTU or jumbo-frame mismatch between devices.
4
Drops / discards
The device threw frames away - buffers full (congestion) or frames it could not process.
5
Duplex mismatch
One side full, one side half: link stays up but collisions, CRCs and runts soar under load - forced-speed misconfig is the usual cause.
6
Read the DELTA
Absolute counts mean little - clear or note the counters, wait, re-read; the growth rate convicts.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
429

## Slide 430
OBJ 5.2 · INTERFACES
Reading an ethtool Counter Dump
Lab 28's core skill: convict a bad link from its counters.
$ ethtool eth0 | grep -E 'Speed|Duplex|Link'
Speed: 1000Mb/s
Duplex: Half
Link detected: yes
$ ethtool -S eth0 | grep -iE 'crc|err|drop'
rx_crc_errors: 18201
rx_errors: 18244
rx_dropped: 12
tx_errors: 0
HALF DUPLEX
Gigabit should negotiate full duplex - Half means autoneg failed or one side was forced.
RX CRC CLIMBING
18k CRC errors received: corrupt frames arriving - bad cable, noise or that duplex mismatch.
TX CLEAN
Zero TX errors - our side sends fine; the fault is inbound: cable, far end or negotiation.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
430

## Slide 431
OBJ 5.2 · HARDWARE
Hardware Issues: PoE and Transceivers
1
PoE budget exhausted
Every switch has a total PoE wattage; add one camera too many and the newest device simply gets no power.
2
PoE standard mismatch
802.3af (15.4 W), at/PoE+ (30 W), bt/PoE++ (60-90 W) - a device asking for more than the port class delivers won't boot.
3
Transceiver mismatch
SFP wavelength, speed and SMF/MMF type must match at BOTH ends - and some switches reject non-vendor optics.
4
Transceiver signal strength
Read optical RX power via DDM/DOM or a power meter: too low means dirty or bent fibre, too high can saturate the receiver.
5
Check the power draw
show power inline (or vendor equivalent) lists per-port draw against budget - first stop for a dead PoE device.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
431

## Slide 432
OBJ 5.2 · SCENARIOS
Wired Connection Scenarios
Symptom
Likely cause and first action
• No link light on NIC or switch
• Link up but slow / errors under load
• VoIP or video is choppy (jitter)
• Works until someone touches the desk
• Switch port LED never blinks
• Cable, port or far end - swap one at a time
• Cable spec below network speed - check Cat rating
• Buffer/QoS or increase speed - measure first
• Re-terminate - loose plug or damaged latch
• Try another port; confirm it is not an uplink port
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
432

## Slide 433
OBJ 5.2 · SCENARIOS
Scenario: The Dead Desk Port
1
Identify
one desk, no link light
2
Theory: L1
patch lead or outlet
3
Test
swap lead; tone the run
4
Fix
re-terminate wall jack
5
Verify + document
label run, note fix
PATTERN
Bottom-to-top fits single-user wired faults: cheap L1 tests first, and the toner finds which patch-panel port serves the desk.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
433

## Slide 434
DOMAIN 5.0 · HANDS-ON
Layer 1/2 Diagnostics with ip and ethtool
LAB 28
Diagnose cable and interface faults from link state, speed/duplex and error counters.
Use ip and ethtool on a Killercoda Ubuntu VM to read interface state, verify speed and duplex, hunt CRC and frame error counters, and bounce a NIC to recover the link.
YOU'LL BUILD
A verified eth0: link state decoded, speed/duplex confirmed and every error counter read and interpreted.
TOOLCHAIN
ethtool, iproute2, Killercoda Ubuntu playground
DONE WHEN
ip -brief link shows eth0 UP; ethtool reports Link detected: yes with matching speed/duplex, and you can explain what any non-zero error counter would mean.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
434

## Slide 435
LAB 28 · PROCESS MAP
How Lab 28 Runs
1
Install ethtool
apt · step 1
2
Inspect link speed
ethtool · step 3
3
Read the driver error counters
ethtool · step 4
4
Read kernel-level RX/TX statistics
ip · step 5
5
Note how speed/duplex would be forced
# · step 7
THE POINT
Diagnose cable and interface faults from link state, speed/duplex and error counters.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
435

## Slide 436
LAB 28 · VERIFY
Layer 1/2 Diagnostics with ip and ethtool
✅ Expected result
ip -brief link shows eth0 UP; ethtool reports Link detected: yes with matching speed/duplex, and you can explain what any non-zero error counter would mean.
IF IT DOESN'T WORK
ethtool: command not found
Run apt update && apt install -y ethtool first.
State shows LOWERLAYERDOWN
No carrier - in the real world check the cable/SFP; in the lab bring it up with ip link set eth0 up.
Counters show no errors
Normal on a clean virtual NIC - the skill is knowing where CRC and frame errors would appear.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
436

## Slide 437
OBJ 5.5 · TOOLS
The First-Response Command-Line Kit
1
ping
Sends ICMP echoes to measure reachability, RTT and loss - the baseline for every path complaint.
2
traceroute / tracert
Linux traceroute = Windows tracert: reveals every L3 hop to the destination and the RTT to each.
3
pathping
Windows hybrid - traces the path, then pings each hop over time for per-hop loss statistics.
4
mtr
Live traceroute + ping combined; its Loss% column shows exactly where loss begins - best first tool for path issues.
5
nslookup / dig
Query DNS directly, choosing the server, the record type and even the full delegation trace.
6
Speed testers
Browser or CLI bandwidth tests verify the up/down throughput actually delivered to one machine.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
437

## Slide 438
OBJ 5.5 · TOOLS
Reading a traceroute
Three RTT samples per hop - and the hops that lie.
$ traceroute 8.8.8.8
1 10.0.0.1 0.4 ms 0.3 ms 0.3 ms
2 100.64.12.1 2.1 ms 2.4 ms 2.0 ms
3 * * *
4 72.14.204.9 8.9 ms 9.2 ms 8.8 ms
5 dns.google 9.0 ms 8.9 ms 9.1 ms
HOP = ROUTER
Each line is one L3 hop; the three columns are three RTT samples to that router.
* * * AT HOP 3
That router won't answer probes - filtered, not broken: hops 4 and 5 still respond.
WHERE LATENCY JUMPS
A jump persisting to the last hop marks the slow segment; on one hop only it is rate-limiting.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
438

## Slide 439
OBJ 5.5 · TOOLS
Traceroute Gotchas
1
* * * is usually fine
Routers deprioritise or drop probe replies - only worry when every hop after it also fails.
2
ICMP is deprioritised
Routers answer probes on the slow CPU path while real transit is forwarded in hardware - hop RTTs exaggerate.
3
TCP traceroute
traceroute -T -p 443 uses TCP SYN probes that pass firewalls blocking ICMP or UDP probes.
4
Windows vs Linux probes
tracert uses ICMP echoes; Linux traceroute defaults to UDP - a firewall may pass one and block the other.
5
Paths change mid-trace
ECMP load balancing can split probes across paths - mtr gives a steadier per-hop view.
6
The return path is invisible
You see the outbound path only - the reply may come back a different way (asymmetric routing).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
439

## Slide 440
OBJ 5.5 · TOOLS
Reading an mtr Report
mtr -rwc 20 sends 20 cycles and prints per-hop loss.
$ mtr -rwc 20 8.8.8.8
HOST Loss% Snt Avg Wrst
1. 10.0.0.1 0.0% 20 0.4 1.1
2. isp-core-rtr 60.0% 20 2.2 3.7
3. 72.14.212.1 0.0% 20 8.7 11.9
4. dns.google 0.0% 20 9.0 11.4
60% AT HOP 2
Looks alarming - but hops 3 and 4 show 0% loss, so transit THROUGH hop 2 is fine.
RATE-LIMITING
Hop 2 rate-limits its own ICMP replies. Real loss persists on every hop below it.
REAL LOSS
Loss beginning at hop N and continuing to the final hop - report that segment to its owner.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
440

## Slide 441
OBJ 5.5 · TOOLS
Is That Packet Loss Real?
mtr shows loss at one hop. Does the loss persist to the final hop?
YES - real loss
The path drops packets from that hop onward - localise the segment and engage its owner (ISP or WAN provider) with the mtr report.
NO - cosmetic
That single router is rate-limiting ICMP replies while forwarding fine - transit is unaffected; do not chase it.
Only loss that continues all the way down the report is service-affecting.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
441

## Slide 442
OBJ 5.1 · METHOD APPLIED
Scenario: The Whole Office Is Slow
1
Identify
all users, started 2pm
2
Theory
WAN congestion (L3)
3
Test
mtr: loss at ISP hop
4
Fix / escalate
ticket with mtr report
5
Verify
loss clears, RTT normal
PATTERN
Whole-site symptoms point at shared links - measure first, because carriers act on an mtr report, not on 'it feels slow'.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
442

## Slide 443
DOMAIN 5.0 · HANDS-ON
Reachability with ping, traceroute and mtr
LAB 29
Localise latency and packet loss along a network path with ping, traceroute and mtr.
Baseline RTT and loss with ping, expose every L3 hop with traceroute, combine both views in a 20-cycle mtr report, then bypass ICMP filters with a TCP traceroute on port 443.
YOU'LL BUILD
An mtr loss report for 8.8.8.8 and a TCP traceroute that passes firewalls which block ICMP.
TOOLCHAIN
iputils-ping, traceroute, mtr-tiny
DONE WHEN
ping reports 0% loss, traceroute lists each hop with three RTT samples, and the mtr report shows 0.0% loss on the final hop.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
443

## Slide 444
LAB 29 · PROCESS MAP
How Lab 29 Runs
1
Install the tools
apt · step 1
2
Baseline RTT and loss with ping
ping · step 2
3
Trace the hop-by-hop path
traceroute · step 3
4
Read the Loss% column - find where
Step 5 of 6
5
Use TCP traceroute where ICMP is
traceroute · step 6
THE POINT
Localise latency and packet loss along a network path with ping, traceroute and mtr.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
444

## Slide 445
LAB 29 · VERIFY
Reachability with ping, traceroute and mtr
✅ Expected result
ping reports 0% loss, traceroute lists each hop with three RTT samples, and the mtr report shows 0.0% loss on the final hop.
IF IT DOESN'T WORK
traceroute prints * * *
That hop drops ICMP/UDP probes - usually filtered, not broken; try traceroute -T -p 443 instead.
mtr: command not found
Install the report-mode build with apt install -y mtr-tiny.
Loss shown on one middle hop only
ICMP rate-limiting on that router - only loss persisting to the final hop is real.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
445

## Slide 446
OBJ 5.3 · NETWORK SERVICES
DNS Troubleshooting Basics
1
Test with an IP, not a name
If the site loads by IP address while the name fails, connectivity is fine - the fault is DNS.
2
Find the configured resolver
Linux: cat /etc/resolv.conf or resolvectl status; Windows: ipconfig /all - know WHO you are asking.
3
Flush the cache
ipconfig /flushdns (Windows) or resolvectl flush-caches (Linux) clears poisoned or stale answers.
4
Query a server directly
dig @1.1.1.1 name or nslookup name 8.8.8.8 bypasses the local resolver to isolate which side is broken.
5
Compare two resolvers
Same name, two servers: one NXDOMAIN and one answer convicts the failing resolver, not the domain.
6
Check the record, not just the name
Wrong or stale A/AAAA/CNAME records resolve 'successfully' to the wrong place - read the answer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
446

## Slide 447
OBJ 5.3 · NETWORK SERVICES
Decoding DNS Response Codes
Status
Meaning
Likely cause
NOERROR
Query answered
Healthy (still read the answer!)
NXDOMAIN
Name does not exist
Typo, expired or missing record
SERVFAIL
Server-side failure
DNSSEC failure, broken zone
REFUSED
Server will not answer
ACL - you are not its client
Timeout
No response at all
Wrong server IP, port 53 blocked
WHEN IT MATTERS dig prints the status in its header line: ->>HEADER<<- opcode: QUERY, status: NXDOMAIN
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
447

## Slide 448
OBJ 5.3 · NETWORK SERVICES
Walking the Hierarchy with dig +trace
+trace resolves from the root down, showing each delegation.
$ dig +trace example.com
. NS a.root-servers.net.
com. NS a.gtld-servers.net.
example.com. NS a.iana-servers.net.
example.com. A 96.7.128.175
ROOT HANDS OFF
The root servers do not know example.com - they delegate to the .com TLD servers.
TLD DELEGATES
The .com servers point at the domain's authoritative servers - the zone's real home.
WHERE IT BREAKS
The last successful delegation shows which level failed - registrar, zone or record.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
448

## Slide 449
OBJ 5.3 · NETWORK SERVICES
Client-Side vs Server-Side DNS Faults
Client side
Server side
• Wrong DNS server configured (DHCP or static)
• Stale cache - flush and retry
• Search suffix appending the wrong zone
• hosts file override hijacking the name
• VPN swapping the resolver silently
• Zone expired or misloaded (SERVFAIL)
• Missing or wrong A, AAAA or CNAME record
• DNSSEC validation failure upstream
• Forwarder or recursion broken
• ACL refusing your source (REFUSED)
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
449

## Slide 450
OBJ 5.3 · NETWORK SERVICES
Scenario: 'The Site Is Down' - But Is It?
1
Identify
name fails, IP works
2
Theory
DNS, not the network
3
Test
dig both resolvers
4
Fix
correct resolver IP
5
Verify
name resolves; document
PATTERN
The IP-vs-name test splits the universe in one move: if the IP works, stop blaming the network and interrogate DNS.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
450

## Slide 451
DOMAIN 5.0 · HANDS-ON
DNS Troubleshooting with dig and resolvectl
LAB 30
Isolate DNS faults by comparing resolvers, tracing delegation and reading response codes.
Identify which resolver the system really uses, compare answers from 1.1.1.1 and 8.8.8.8, walk the delegation chain with dig +trace, time a lookup and flush the systemd-resolved cache.
YOU'LL BUILD
A decoded dig +trace delegation chain plus a flushed resolver cache and the NXDOMAIN/SERVFAIL/REFUSED decode.
TOOLCHAIN
dnsutils (dig), systemd-resolved (resolvectl)
DONE WHEN
dig +short returns the same A record from both resolvers, +trace shows root -> .com -> authoritative delegation, and resolvectl statistics resets after the flush.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
451

## Slide 452
LAB 30 · PROCESS MAP
How Lab 30 Runs
1
Install dnsutils
apt · step 1
2
Confirm which resolver the system is
cat · step 2
3
Compare two upstream resolvers
dig · step 3
4
Time a lookup to spot a slow upstream
time · step 5
5
Flush the cache and confirm the
resolvectl · step 6
THE POINT
Isolate DNS faults by comparing resolvers, tracing delegation and reading response codes.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
452

## Slide 453
LAB 30 · VERIFY
DNS Troubleshooting with dig and resolvectl
✅ Expected result
dig +short returns the same A record from both resolvers, +trace shows root -> .com -> authoritative delegation, and resolvectl statistics resets after the flush.
IF IT DOESN'T WORK
resolv.conf points to 127.0.0.53
Expected - systemd-resolved proxies DNS; use resolvectl status to see the real upstream.
SERVFAIL from one resolver
Upstream or DNSSEC failure - compare against a second resolver to confirm it is server-side.
dig +trace hangs
Some networks block outbound DNS to the root servers; rerun on the Killercoda VM.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
453

## Slide 454
OBJ 5.3 · L2 SERVICES
ARP and Neighbour Discovery
1
What ARP does
Maps an IPv4 address to a MAC so frames can be delivered on the local segment - no ARP entry, no delivery.
2
IPv6 uses NDP
IPv6 replaced ARP with ICMPv6 Neighbour Solicitation/Advertisement - same job, viewed with ip -6 neigh.
3
REACHABLE / STALE / FAILED
REACHABLE: recently confirmed. STALE: known, unconfirmed. FAILED: no answer - the neighbour is gone or blocked.
4
arping
Sends real ARP requests to one host - proves L2 adjacency even when ICMP ping is firewalled.
5
Gratuitous ARP
Unsolicited 'this IP is mine' broadcasts - normal after failover, but also the tool of ARP spoofers.
6
Flush to reset
ip neigh flush all (or arp -d) clears stale entries - the IP-layer equivalent of bouncing the NIC.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
454

## Slide 455
OBJ 5.3 · L2 SERVICES
Duplicate IPs and ARP Poisoning
1
The duplicate-IP symptom
Connectivity that flip-flops - works, breaks, works - as two hosts fight over one address in peers' ARP caches.
2
Where duplicates come from
Static IPs inside a DHCP scope, a cloned VM, or a second DHCP server handing out the same range.
3
Detect with DAD
arping -D probes your own address - 'address already in use' convicts a duplicate on the segment.
4
Find the culprit by MAC
The ARP reply carries the offender's MAC - trace it to a switch port via the MAC address table.
5
ARP poisoning
An attacker answers ARP for the gateway to sit in the middle - defend with dynamic ARP inspection (DAI).
6
Pin critical neighbours
A static ARP entry (ip neigh add ... ) locks the gateway or server MAC where poisoning is a real risk.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
455

## Slide 456
OBJ 5.3 · SWITCHING
Switching Issues: Loops, VLANs, ACLs
1
STP loop symptoms
LED storm on every port, CPU spikes, MAC table churn, whole-segment meltdown - seconds after someone loops a cable.
2
Why loops melt networks
Ethernet frames have no TTL - a broadcast circles forever and multiplies at every switch: broadcast storm.
3
STP blocking surprises
A port stuck in blocking after a topology change - or a cheap unmanaged switch that silently runs no STP at all.
4
Incorrect VLAN assignment
Port in the wrong VLAN: link up, DHCP answers from the wrong subnet, gateway unreachable - check switchport config.
5
Trunk / native VLAN mismatch
Mismatched allowed-lists or native VLANs silently drop exactly one VLAN's traffic across a link.
6
ACLs eating traffic
'Everything works except X between two subnets' is an ACL or firewall rule until proven otherwise - check hit counters.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
456

## Slide 457
OBJ 5.3 · SWITCHING
Layer 2 Faults: Symptom to Check
Fault
Classic symptom
First check
Switching loop
Storm: all LEDs solid, LAN dead
STP status, recent cabling
Blocked port
Uplink idle, path suboptimal
spanning-tree state per port
Wrong VLAN
Link up, DHCP from wrong subnet
switchport access vlan
Trunk mismatch
One VLAN dead across a link
allowed / native VLAN lists
Duplicate IP
Flip-flop reachability
arping -D, ARP tables
ACL block
One app/port pair fails, rest OK
ACL hit counters
WHEN IT MATTERS Link light on + wrong behaviour = think L2: VLANs, STP, ARP - before re-crimping anything.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
457

## Slide 458
OBJ 5.3 · SWITCHING
Scenario: New Switch, Network Meltdown
1
Identify
LAN dies at 9:05am
2
What changed?
intern added a switch
3
Theory
loop - no STP on it
4
Test / fix
unplug; storm stops
5
Prevent
BPDU guard on edge
PATTERN
'What changed?' solved this in one question - and the preventive step (BPDU guard) is what makes step 6 more than a checkbox.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
458

## Slide 459
DOMAIN 5.0 · HANDS-ON
ARP and the IPv6 Neighbour Table
LAB 31
Diagnose L2 adjacency problems with ip neigh and arping, including duplicate IP detection.
View and decode neighbour states, probe the default gateway with arping, run duplicate-address detection on your own IP, pin and flush ARP entries, then inspect IPv6 neighbour discovery.
YOU'LL BUILD
A decoded neighbour table with a static entry added and flushed, plus a duplicate-IP probe of your own address.
TOOLCHAIN
iputils-arping, iproute2, ndisc6
DONE WHEN
ip neigh shows the gateway REACHABLE after arping, DAD reports no duplicate for your IP, and the static 10.0.0.99 entry appears until the flush removes it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
459

## Slide 460
LAB 31 · PROCESS MAP
How Lab 31 Runs
1
Install arping
apt · step 1
2
Probe the default gateway directly
arping · step 3
3
Run duplicate address detection on
arping · step 4
4
Add a static ARP entry and verify it
ip · step 5
5
Inspect IPv6 neighbour discovery
ip · step 7
THE POINT
Diagnose L2 adjacency problems with ip neigh and arping, including duplicate IP detection.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
460

## Slide 461
LAB 31 · VERIFY
ARP and the IPv6 Neighbour Table
✅ Expected result
ip neigh shows the gateway REACHABLE after arping, DAD reports no duplicate for your IP, and the static 10.0.0.99 entry appears until the flush removes it.
IF IT DOESN'T WORK
arping: Operation not permitted
ARP probes need raw sockets - run as root (Killercoda terminals already are).
All entries show STALE
Normal - STALE means known but unconfirmed; traffic or arping promotes it to REACHABLE.
DAD says address already in use
Another host claims your IP - a real duplicate-IP incident; hunt it down by its MAC address.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
461

## Slide 462
OBJ 5.5 · TOOLS
Protocol Analyzers
1
What they do
Capture frames off the wire and decode every layer - the ground truth when ping and traceroute run out of answers.
2
Wireshark
The GUI analyzer: live capture, colour rules, stream following and per-protocol statistics.
3
tcpdump
The CLI capture workhorse - runs on servers and routers where no GUI exists; writes .pcap files.
4
tshark
Wireshark's terminal twin - the same dissectors and display filters, with scriptable field output.
5
Capture once, analyse anywhere
Write to .pcap with tcpdump -w, then open the same file in Wireshark, tshark or a web analyzer.
6
Port mirroring / TAP
To see OTHER hosts' traffic you need a SPAN/mirror port or a hardware TAP - switches don't flood unicast to you.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
462

## Slide 463
OBJ 5.5 · TOOLS
Capture Filter vs Display Filter
Capture filter (BPF)
Display filter
• Applied WHILE capturing - packets never stored
• Syntax: 'udp port 53 and host 10.0.0.5'
• Keeps the .pcap small on busy links
• Cannot be undone - discarded is gone
• Same syntax in tcpdump and Wireshark
• Applied AFTER capture - hides, never deletes
• Syntax: dns.flags.response==1
• Change it freely while analysing
• Wireshark GUI and tshark -Y
• The web analyzer's search box works this way
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
463

## Slide 464
OBJ 5.5 · TOOLS
Reading a tcpdump Line
One DNS query and its reply, decoded field by field.
$ tcpdump -nn -r /tmp/dns.pcap | head -4
12:04:01.123 IP 10.0.0.5.53622 > 1.1.1.1.53:
51291+ A? example.com. (29)
12:04:01.131 IP 1.1.1.1.53 > 10.0.0.5.53622:
51291 1/0/0 A 96.7.128.175 (45)
SRC > DST.PORT
10.0.0.5 from ephemeral port 53622 to 1.1.1.1 port 53 - client to resolver.
51291+ A?
Transaction ID 51291, recursion desired (+), question: the A record for example.com.
1/0/0 REPLY
Same ID back: 1 answer, 0 authority, 0 additional - the A record, 8 ms later.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
464

## Slide 465
OBJ 5.5 · TOOLS
netstat and ss: Who Is Listening?
1
What they show
Every open port and connection on THIS host - the tool for 'is the service even listening?'.
2
ss replaces netstat
Modern Linux ships ss; the letters carry over: ss -tlnp = TCP listeners, numeric, with processes.
3
-n numeric
Skip DNS and service-name lookups - faster output and no misleading resolved names.
4
-a all / -l listening
-a shows every socket including established connections; -l restricts to listening sockets.
5
-p / -o / -b processes
Which executable and PID own each socket (netstat -b and -o on Windows, ss -p on Linux).
6
-r routing table
netstat -r prints the local routing table - the same data as ip route or route print.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
465

## Slide 466
OBJ 5.5 · TOOLS
Reading ss -tlnp
Three listeners - and one classic bind mistake.
$ ss -tlnp
State Local Address:Port Process
LISTEN 0.0.0.0:22 sshd
LISTEN 127.0.0.1:3306 mysqld
LISTEN [::]:443 nginx
0.0.0.0:22
sshd listens on every IPv4 address - reachable from the network, firewall permitting.
127.0.0.1:3306
MySQL bound to loopback ONLY - remote clients get 'connection refused'; that is the bug.
[::]:443
nginx on the IPv6 wildcard - on dual-stack hosts this usually accepts IPv4 too.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
466

## Slide 467
OBJ 5.5 · TOOLS
The Capture Workflow + TIS PCAP Analyzer
1
1 · Filter tight, capture small
Capture with a BPF filter and -c count so the .pcap holds only the conversation you care about.
2
2 · Write to .pcap
tcpdump -w capture.pcap keeps the binary packets - analysis can happen later, elsewhere, repeatedly.
3
3 · First pass with tshark
Pull just the fields you need: -T fields -e dns.qry.name turns packets into a readable table.
4
4 · Go graphical in the browser
The TIS PCAP Analyzer (alfredang.github.io/pcapanalyzer) opens .pcap files in-browser - no install needed.
5
5 · Drill into the layers
Expand any packet to walk Ethernet -> IP -> UDP -> DNS - the OSI model made visible.
6
6 · Search like a display filter
The analyzer's filter box narrows by name or protocol - the same idea as Wireshark's -Y.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
467

## Slide 468
DOMAIN 5.0 · HANDS-ON
Packet Capture with tcpdump and TIS PCAP Analyzer
LAB 32
Capture DNS traffic to a .pcap and analyse it with tshark and the TIS PCAP Analyzer.
Capture ten DNS packets with a BPF capture filter, dissect them with tshark display filters, then move the .pcap to your laptop and explore it graphically in the browser-based TIS PCAP Analyzer.
YOU'LL BUILD
A dns.pcap captured with tcpdump and read three ways: tcpdump summary, tshark fields and the TIS PCAP Analyzer UI.
TOOLCHAIN
tcpdump, tshark, TIS PCAP Analyzer (alfredang.github.io/pcapanalyzer)
DONE WHEN
The TIS PCAP Analyzer shows your three queries with matching responses: each query leaves a high ephemeral source port for destination port 53, and query/response transaction IDs match.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
468

## Slide 469
LAB 32 · PROCESS MAP
How Lab 32 Runs
1
Install the capture tools
apt · step 1
2
Generate DNS queries to fill the
for · step 3
3
Show only the response packets
tshark · step 5
4
Base64 the pcap
base64 · step 7
5
Answer the analysis questions
Step 9 of 9
THE POINT
Capture DNS traffic to a .pcap and analyse it with tshark and the TIS PCAP Analyzer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
469

## Slide 470
LAB 32 · VERIFY
Packet Capture with tcpdump and TIS PCAP Analyzer
✅ Expected result
The TIS PCAP Analyzer shows your three queries with matching responses: each query leaves a high ephemeral source port for destination port 53, and query/response transaction IDs match.
IF IT DOESN'T WORK
Capture never reaches 10 packets
Your queries may not match the BPF filter - re-run the dig loop or loosen the filter.
tshark asks about non-root capture
Answer No for the lab - you are reading files, not capturing as a normal user.
Analyzer shows no packets
Re-decode the base64 on your laptop (base64 -d dns.pcap.b64 > dns.pcap) and upload again.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
470

## Slide 471
OBJ 5.4 · MTU & PMTUD
MTU: When Big Packets Vanish
1
MTU = biggest frame payload
Standard Ethernet carries 1500 bytes of IP packet; tunnels (VPN, GRE, PPPoE) reduce the usable size.
2
The header maths
Payload = MTU - 20 (IP) - 8 (ICMP/UDP) or - 20 (TCP): hence the magic ping size 1472 at MTU 1500.
3
DF: Don't Fragment
With DF set, an oversize packet is dropped and the router returns ICMP Type 3 Code 4: Fragmentation Needed.
4
Path MTU Discovery
Senders probe with DF packets and shrink until they fit - PMTUD depends entirely on those ICMP replies arriving.
5
Jumbo frames
9000-byte MTUs help storage and backup LANs - but EVERY device on the path must agree, or you manufacture giants.
6
Mismatch symptoms
Small packets sail through; anything full-size stalls - a signature no other fault quite copies.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
471

## Slide 472
OBJ 5.4 · MTU & PMTUD
Proving the MTU with DF-Bit Pings
Lab 33's probe: -M do forbids fragmentation.
$ ping -M do -s 1472 -c2 8.8.8.8
1480 bytes from 8.8.8.8: icmp_seq=1 ttl=118
1480 bytes from 8.8.8.8: icmp_seq=2 ttl=118
$ ping -M do -s 1500 -c2 8.8.8.8
ping: local error: message too long, mtu=1500
1472 PASSES
1472 payload + 8 ICMP + 20 IP = exactly 1500 - the largest ping that fits standard Ethernet.
1500 REFUSED
With DF set the kernel won't fragment - 1500 + 28 exceeds the MTU, so the send fails locally.
ON A REAL PATH
A mid-path bottleneck would return ICMP Type 3 Code 4 - unless a firewall eats it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
472

## Slide 473
OBJ 5.4 · MTU & PMTUD
The PMTUD Black Hole
Small pings and SSH work. Do large transfers hang at a fixed point?
YES - suspect MTU
A firewall is eating the Fragmentation Needed ICMP, so senders never shrink. Test with DF pings; clamp TCP MSS on the router.
NO - not MTU
A size-independent fault is congestion, loss or the application - go measure with ping and mtr instead.
MSS clamping: iptables -t mangle ... --clamp-mss-to-pmtu rescues TCP through the hole.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
473

## Slide 474
OBJ 5.4 · MTU & PMTUD
Living With Broken PMTUD
1
The classic report
'Web page starts loading then hangs' or 'SSH works, SCP stalls' - the first full-size packet is the one that dies.
2
Why ICMP gets blocked
Overzealous firewall policies drop ALL ICMP - killing the Type 3 Code 4 messages PMTUD depends on.
3
MSS clamping
The router rewrites TCP's advertised MSS during the handshake so segments never exceed the path MTU.
4
Lower the tunnel MTU
Setting VPN and tunnel interfaces to a matching MTU (e.g. 1400) prevents oversize packets at the source.
5
Allow the right ICMP
Permit ICMP Type 3 Code 4 - and IPv6 Packet Too Big - through firewalls; PMTUD is mandatory in IPv6.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
474

## Slide 475
DOMAIN 5.0 · HANDS-ON
MTU and Path-MTU Discovery
LAB 33
Demonstrate MTU limits with DF-bit pings and explain PMTUD black holes and MSS clamping.
Compute the ICMP payload maths (MTU minus 28), send Don't-Fragment pings at and over the limit, lower the interface MTU to 1400 and retest both sides of the new limit, then restore it.
YOU'LL BUILD
A demonstrated 1472-byte pass / 1500-byte 'message too long' fail, repeated at MTU 1400, and a restored interface.
TOOLCHAIN
iputils-ping, iproute2
DONE WHEN
1472-byte DF pings succeed at MTU 1500 and 1372-byte pings at MTU 1400, while oversize pings fail with 'message too long' showing the current mtu value.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
475

## Slide 476
LAB 33 · PROCESS MAP
How Lab 33 Runs
1
Check the interface MTU
ip · step 1
2
Exceed the MTU with DF set and read
ping · step 3
3
Lower the interface MTU to 1400
ip · step 4
4
Retest at the new limit
ping · step 5
5
Discuss
Step 7 of 7
THE POINT
Demonstrate MTU limits with DF-bit pings and explain PMTUD black holes and MSS clamping.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
476

## Slide 477
LAB 33 · VERIFY
MTU and Path-MTU Discovery
✅ Expected result
1472-byte DF pings succeed at MTU 1500 and 1372-byte pings at MTU 1400, while oversize pings fail with 'message too long' showing the current mtu value.
IF IT DOESN'T WORK
Oversize ping shows no error
Without -M do the kernel silently fragments - the DF bit is what makes the test honest.
1472 fails too
A tunnel/VPN lowers the effective path MTU - step the size down (1452, 1420...) until it passes.
Forgot to restore the MTU
ip link set eth0 mtu 1500 - a lowered MTU otherwise slows every later lab.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
477

## Slide 478
OBJ 5.3 · ROUTING
Routing Table Issues
1
Missing route
No entry covers the destination and no default exists - traffic dies with 'network unreachable'.
2
Wrong or missing default route
The gateway of last resort is wrong or absent: local subnets fine, everything beyond them dead.
3
Wrong next hop
The route exists but points at the wrong router - packets leave, replies never come, or redirects fly.
4
Longest prefix wins
10.99.0.0/24 beats 10.0.0.0/8 regardless of metric - the most specific route always forwards the packet.
5
Metric breaks ties
Between equal prefixes the lower metric wins - how floating static and backup routes stay dormant.
6
ip route get
Ask the kernel directly which route, interface and source IP a destination would use - no guessing.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
478

## Slide 479
OBJ 5.3 · ROUTING
Interrogating the Routing Table
Lab 34's key move: make the kernel show its choice.
$ ip route
default via 172.30.1.1 dev eth0
10.99.0.0/24 via 172.30.1.1 dev eth0 metric 100
172.30.1.0/24 dev eth0 src 172.30.1.2
$ ip route get 10.99.0.5
10.99.0.5 via 172.30.1.1 dev eth0 src 172.30.1.2
THREE ROUTE TYPES
A default, a static /24, and a connected route the kernel added for eth0's own subnet.
ROUTE GET = PROOF
The kernel names the winning route, egress interface and source IP for that destination.
LONGEST PREFIX
10.99.0.5 matches both the /24 and the default - the /24 wins because it is more specific.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
479

## Slide 480
OBJ 5.3 · ROUTING
Asymmetric Routing
1
What it is
Traffic leaves by one path and returns by another - legal in IP, but stateful middleboxes hate it.
2
Why firewalls break
A stateful firewall that never saw the outbound SYN drops the returning SYN-ACK as unsolicited.
3
How it happens
Two exits (dual WAN, two routers, ECMP) with inconsistent metrics - or NAT on only one of the paths.
4
How to spot it
traceroute from BOTH ends and compare; mtr -z shows the AS path, where asymmetry jumps out.
5
The usual fixes
Pin flows to one path with policy routing, sync firewall state, or make the metrics consistent.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
480

## Slide 481
OBJ 5.3 · ADDRESSING
Addressing Faults: Symptom to Test
Fault
Classic symptom
Fastest test
Wrong default gateway
LAN fine, nothing beyond it
ping the gw; ip route / ipconfig
Wrong subnet mask
SOME hosts unreachable
compare mask with a peer
DHCP pool exhausted
New hosts get 169.254.x.x
scope stats; lease table
Duplicate IP
Flip-flop connectivity
arping -D your own address
Static/DHCP overlap
Random conflicts appear
audit static assignments
WHEN IT MATTERS APIPA 169.254.x.x means 'I asked DHCP and nobody answered' - the client self-assigned.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
481

## Slide 482
OBJ 5.3 · NETWORK SERVICES
DHCP Pool Exhaustion
1
The symptom
New and returning devices fail to join; victims show APIPA 169.254.x.x self-assigned addresses.
2
Why pools run dry
A scope sized for desks meets BYOD phones and IoT - every device holds a lease whether active or not.
3
Long leases make it worse
8-day leases on guest Wi-Fi hold addresses for one-time visitors a week after they left.
4
Check scope statistics
The DHCP server shows leases used vs available - exhaustion is visible at a glance.
5
The fixes
Shorten lease times, widen the scope, add VLANs with their own scopes, evict statics from the pool.
6
Rogue DHCP servers
A second, often accidental, DHCP server hands out wrong addresses - DHCP snooping on switches blocks it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
482

## Slide 483
OBJ 5.3 · ADDRESSING
Gateway and Mask Misconfigurations
1
Wrong gateway signature
Everything on the local subnet works; every remote destination fails - off-net traffic has nowhere to go.
2
Test the gateway itself
ping the configured gateway IP: if that fails, check ARP for it; if it works, suspect what lies beyond.
3
Wrong mask signature
The strangest fault: SOME remote hosts work, some local ones don't - the boundary is drawn in the wrong place.
4
Why the mask does that
A too-wide mask claims remote hosts as 'local' (ARPed, never routed); too narrow sends local peers via the gateway.
5
Compare with a healthy peer
ip addr against a working neighbour finds mask and gateway typos in seconds - baselines beat theory.
6
Scope tells you where to look
DHCP misconfig hits everyone on the scope; a static typo hits one machine.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
483

## Slide 484
OBJ 5.3 · ROUTING
Scenario: Ping This, But Not That
1
Identify
10.1.x OK, 10.2.x dead
2
Theory
missing route to 10.2
3
Test
ip route get 10.2.0.5
4
Fix
add route via 10.1.0.2
5
Verify
ping + document route
PATTERN
Partial reachability is routing until proven otherwise - and ip route get turns 'I think' into 'the kernel says'.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
484

## Slide 485
DOMAIN 5.0 · HANDS-ON
Diagnosing Routing Problems
LAB 34
Read and manipulate the routing table; prove which route a destination uses with ip route get.
Print the routing table, query the kernel's route choice for two destinations, add a static route with a metric, inspect precedence and longest-prefix match, then remove the test route.
YOU'LL BUILD
A routing table with a temporary 10.99.0.0/24 static route, proven with ip route get and cleanly removed.
TOOLCHAIN
iproute2, traceroute
DONE WHEN
ip route get 10.99.0.5 switches from the default route to the new static route while it exists, and reverts to the default after ip route del.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
485

## Slide 486
LAB 34 · PROCESS MAP
How Lab 34 Runs
1
Print the full routing table
ip · step 1
2
Add a static route via the default
ip · step 3
3
Show the new route and its metric
ip · step 4
4
Re-run ip route get and watch the
ip · step 5
5
Remove the test route
ip · step 7
THE POINT
Read and manipulate the routing table; prove which route a destination uses with ip route get.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
486

## Slide 487
LAB 34 · VERIFY
Diagnosing Routing Problems
✅ Expected result
ip route get 10.99.0.5 switches from the default route to the new static route while it exists, and reverts to the default after ip route del.
IF IT DOESN'T WORK
RTNETLINK: file exists
The route is already present - delete it first with ip route del 10.99.0.0/24.
Route added but not used
A longer prefix elsewhere wins - longest-prefix match beats metric every time.
No default route at all
Re-add it: ip route add default via <gateway IP> dev eth0.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
487

## Slide 488
OBJ 5.4 · PERFORMANCE
Latency vs Loss vs Jitter
Metric
What it is
Hurts most
Measure with
Latency
Round-trip delay
Interactive apps, gaming
ping RTT, mtr Avg
Packet loss
Frames never arrive
TCP throughput collapse
ping / mtr Loss%
Jitter
Variation in delay
VoIP and live video
mtr Wrst-Avg, iperf3 -u
Bandwidth
Path capacity
Bulk transfer, backup
iperf3, speed testers
WHEN IT MATTERS VoIP wants jitter under ~30 ms and loss under 1% - buffers trade jitter for latency.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
488

## Slide 489
OBJ 5.4 · PERFORMANCE
A Little Loss Destroys a Lot of Throughput
Chart: 
| 0% | 0.5% | 1% | 2% | 5%
Relative TCP throughput (%) | 100 | 62 | 45 | 28 | 11
WHAT THE DATA SHOWS
TCP treats every loss as congestion and backs off - 1% loss roughly halves throughput long before a link is 'full'. This is why Lab 35's netem loss test feels so dramatic.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
489

## Slide 490
OBJ 5.4 · PERFORMANCE
Congestion and Bottlenecks
1
Oversubscribed uplinks
48 access ports funnelling into one 1G uplink - fine on average, saturated at 9 a.m. sharp.
2
The queueing signature
Latency climbs FIRST as buffers fill; loss follows when they overflow - watch the RTT trend before loss.
3
Duplex mismatch again
Still the classic false 'congestion': collisions and CRC errors under load on one specific link.
4
Find the top talkers
Interface counters, NetFlow/sFlow or a capture answer WHO is eating the link before you upgrade it.
5
Broadcast storms
A loop or a chatty protocol can consume a LAN with traffic nobody asked for - see the L2 slides.
6
QoS as triage
Prioritise voice and video over bulk data - it does not add capacity, it decides who suffers.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
490

## Slide 491
OBJ 5.4 · WIRELESS
Wireless Interference and Channel Overlap
1
2.4 GHz: three clean channels
Only 1, 6 and 11 avoid overlap - neighbouring APs on 3 and 8 interfere with BOTH sides.
2
Co-channel vs adjacent
Same-channel APs politely take turns (slow); OVERLAPPING channels corrupt each other (worse).
3
Non-Wi-Fi offenders
Microwave ovens, wireless mice and keyboards, Bluetooth, baby monitors - all camp on 2.4 GHz.
4
Escape to 5 / 6 GHz
Far more non-overlapping channels and less junk - the standing fix for a crowded 2.4 GHz office.
5
Survey before blaming
A Wi-Fi analyzer shows every SSID, channel and RSSI around you - pick the channel the survey supports.
6
Interference symptoms
Connected with strong signal yet slow and jittery - retries eat airtime before anything is 'down'.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
491

## Slide 492
OBJ 5.4 · WIRELESS
Room to Breathe: Channels by Band
Chart: 
| 2.4 GHz | 5 GHz | 6 GHz
Non-overlapping 20 MHz channels | 3 | 24 | 59
WHAT THE DATA SHOWS
2.4 GHz offers exactly three clean channels, shared with microwaves and Bluetooth; 5 and 6 GHz offer dozens - moving bands beats fighting for channel 6.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
492

## Slide 493
OBJ 5.4 · WIRELESS
More Wireless Scenarios
1
Over capacity
Too many clients per AP: strong signal, terrible throughput - add APs or steer clients to 5/6 GHz.
2
Incorrect antenna type
Omni antennas in a long corridor, or patch antennas facing the wrong way, waste the cell where users are.
3
Antenna placement
Placement is an art: test and retest - central, high, away from metal and water; re-survey after moving.
4
Cable gain loss
Every metre of antenna coax costs dB - keep antenna cables short or the gain never reaches the air.
5
Old standards drag the cell
Legacy 802.11b/g clients force protection modes that slow everyone - upgrade or isolate them.
6
Roaming problems
Sticky clients cling to a distant AP - tune min-RSSI and roaming thresholds so handoff happens.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
493

## Slide 494
OBJ 5.5 · TOOLS
Measuring Performance
1
iperf3
Client/server throughput tester - proves what the path can actually carry, TCP or UDP with loss and jitter stats.
2
Speed testers
Quick browser or CLI checks of real up/down rates to the internet - verify the circuit, not the marketing.
3
Wi-Fi analyzers
Show channels, signal strength and neighbouring networks - the survey tool behind every interference fix.
4
mtr over time
A long-running mtr catches the intermittent loss and jitter that a single ping snapshot misses.
5
tc netem (lab)
Injects delay, jitter and loss on purpose - reproduce the customer's WAN on one VM and test the app against it.
6
Baseline everything
A measurement means little without the 'normal' to compare against - collect baselines before trouble starts.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
494

## Slide 495
DOMAIN 5.0 · HANDS-ON
Simulating Slow and Lossy Links with tc
LAB 35
Reproduce WAN latency, jitter and loss with tc netem and cap bandwidth with tbf.
Baseline RTT, then use tc netem to inject 200 ms delay, +/-50 ms jitter and 5% loss, verifying each with ping; cap throughput at 1 Mbit/s with tbf, prove it with iperf3, then remove all shaping.
YOU'LL BUILD
A NIC that demonstrably ran at +200 ms delay, 5% loss and a 1 Mbit/s cap - and a clean qdisc afterwards.
TOOLCHAIN
iproute2 (tc/netem/tbf), iperf3
DONE WHEN
ping RTT rises by about 200 ms under netem, roughly 1 in 20 pings times out at 5% loss, and iperf3 reports about 1 Mbit/s under the tbf cap.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
495

## Slide 496
LAB 35 · PROCESS MAP
How Lab 35 Runs
1
Baseline the RTT
ping · step 1
2
Add +/-50 ms of jitter
tc · step 3
3
Clear netem before shaping bandwidth
tc · step 5
4
Cap bandwidth at 1 Mbit/s with a token
tc · step 6
5
Remove all shaping and confirm
tc · step 8
THE POINT
Reproduce WAN latency, jitter and loss with tc netem and cap bandwidth with tbf.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
496

## Slide 497
LAB 35 · VERIFY
Simulating Slow and Lossy Links with tc
✅ Expected result
ping RTT rises by about 200 ms under netem, roughly 1 in 20 pings times out at 5% loss, and iperf3 reports about 1 Mbit/s under the tbf cap.
IF IT DOESN'T WORK
RTNETLINK answers: file exists
A qdisc is already installed - use tc qdisc change, or delete the root qdisc first.
RTT did not change
You shaped the wrong interface - confirm the active NIC with ip -brief link.
iperf3 connection refused
Start the server first (iperf3 -s -D), then run the client against 127.0.0.1.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
497

## Slide 498
OBJ 5.3 · WAN
WAN Troubleshooting Scenarios
1
Start at your own edge
Most WAN faults are customer-side - cables, the router, config - not the ISP; check yours before calling.
2
Walk to the demarc
LAN interface -> router/modem LAN side -> WAN side -> provider: find the last healthy point.
3
Modem/ONT lights first
Sync and LOS LEDs on the modem or ONT tell you in seconds whether the carrier signal is even present.
4
Test around DNS
ping 8.8.8.8 vs ping google.com separates 'the WAN is down' from 'DNS is down' immediately.
5
Interference and environment
On DSL, coax and wireless WANs, interference is usually consumer-side - unless weather or disaster says otherwise.
6
Evidence for the carrier
mtr reports, timestamps, loss figures - carriers move faster when the ticket contains measurements.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
498

## Slide 499
OBJ 5.5 · TOOLS
Layered Service Triage
1
nc -zv host 443 - does TCP connect?
▶
2
openssl s_client - does TLS validate?
▶
3
curl -v - what HTTP status returns?
▶
4
curl -w timings - which phase is slow?
▶
5
Escalate with the failing layer named
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
499

## Slide 500
OBJ 5.5 · TOOLS
Breaking One Request Into Phases
curl -w prints a stopwatch for every stage of the request.
$ curl -so /dev/null https://example.com -w \
'DNS:%{time_namelookup} TCP:%{time_connect} \
TLS:%{time_appconnect} TTFB:%{time_starttransfer}'
DNS:2.104 TCP:2.121 TLS:2.189 TTFB:2.239
DNS: 2.1 SECONDS
Nearly the whole wait happened before any packet reached the server - the resolver is to blame.
GAPS, NOT VALUES
Read the DIFFERENCES: TCP-DNS = handshake, TLS-TCP = crypto, TTFB-TLS = server think time.
WHO TO CALL
Slow DNS: resolver team (Lab 30). Slow TTFB: app team. Slow TCP: network path (Lab 29).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
500

## Slide 501
OBJ 5.5 · TOOLS
HTTP Status Codes for Troubleshooters
Code
Meaning
Prime suspect
200
OK
Nothing - move on
301 / 302
Redirect
Follow it - check the target
401 / 403
Auth required / forbidden
Credentials, ACLs, permissions
404
Not found
URL path, deployment
500
Application error
The app itself - read its logs
502/503/504
Bad gateway/overload/timeout
Upstream server or proxy
WHEN IT MATTERS Any HTTP answer at all proves DNS, routing, TCP and TLS all worked - you are at Layer 7.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
501

## Slide 502
OBJ 5.5 · TOOLS
The nc -zv Fork
The site is unreachable. Does nc -zv host 443 succeed?
YES - go up the stack
Routing, firewall and listener are all fine. Test TLS (openssl s_client), then HTTP (curl -v) - the fault is above L4.
NO - stay low
No TCP handshake. Check DNS resolution, then the path (mtr), then firewalls, then whether anything listens (ss -tlnp).
One command splits the whole stack in half - divide and conquer as a habit.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
502

## Slide 503
OBJ 5.1-5.5 · SYNTHESIS
Symptom Sprint: Name the Likely Cause
1
Small pings OK, downloads stall
MTU / PMTUD black hole - run the DF-bit ping test, then clamp MSS (Lab 33).
2
169.254.x.x on new laptops
DHCP exhausted or unreachable - check scope statistics and the lease table (Lab 34).
3
Works by IP, not by name
DNS - compare resolvers with dig, flush the cache (Lab 30).
4
Every LED flashing, LAN dead
Switching loop / broadcast storm - find the new cable, enable BPDU guard (Lab 31).
5
One user flip-flops on/off
Duplicate IP - arping -D, then hunt the MAC (Lab 31).
6
Local fine, remote all dead
Default gateway wrong or down - ping the gateway, check ip route (Lab 34).
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
503

## Slide 504
OBJ 5.1 · METHOD APPLIED
Capstone: 'The Website Is Down'
1
Identify
all users, one site
2
Theory ladder
DNS? path? TLS? app?
3
Test in layers
dig, mtr, nc, curl
4
Fix or escalate
evidence attached
5
Verify + document
timings in ticket
WHY IT MATTERS
Lab 36 runs exactly this triage - each tool eliminates a layer, so the escalation names the failing layer instead of guessing.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
504

## Slide 505
DOMAIN 5.0 · HANDS-ON
Service Reachability Triage with curl, nc and openssl
LAB 36
Isolate a 'site is down' report to TCP, TLS, HTTP or the app using nc, openssl and curl.
Walk the layered triage: prove the TCP handshake with nc -zv, validate the certificate chain with openssl s_client, read HTTP status codes with curl -v, then break one request into DNS/TCP/TLS/TTFB timings.
YOU'LL BUILD
A complete layer-by-layer triage of example.com:443 with a timing breakdown that names the slow phase.
TOOLCHAIN
curl, netcat-openbsd, openssl
DONE WHEN
nc reports succeeded, openssl shows Verify return code: 0 (ok), curl returns HTTP 200, and the -w timings identify the slowest phase of the request.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
505

## Slide 506
LAB 36 · PROCESS MAP
How Lab 36 Runs
1
Install the triage tools
apt · step 1
2
Test L6
echo · step 3
3
Check subject
Step 4 of 7
4
Test L7
curl · step 5
5
Apply the decision tree
Step 7 of 7
THE POINT
Isolate a 'site is down' report to TCP, TLS, HTTP or the app using nc, openssl and curl.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
506

## Slide 507
LAB 36 · VERIFY
Service Reachability Triage with curl, nc and openssl
✅ Expected result
nc reports succeeded, openssl shows Verify return code: 0 (ok), curl returns HTTP 200, and the -w timings identify the slowest phase of the request.
IF IT DOESN'T WORK
nc hangs then times out
No TCP path - fall back to Lab 29 tools: check DNS, then mtr the host, then firewalls.
Verify return code is non-zero
Expired or untrusted certificate, or SNI mismatch - re-run with the right -servername.
HTTP 502/503/504
TCP and TLS are fine - the fault is the app or its upstream; escalate with your evidence.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
507

## Slide 508
OBJ 5.5 · TOOLS
The Troubleshooter's CLI, One Page
Tool
Layer
The question it answers
ping / mtr
L3
Is it reachable? Where is the loss?
traceroute
L3
Which hops does the path take?
ip / arp / ip neigh
L2-L3
Addressing, routes, MAC neighbours
dig / nslookup
L7
What does DNS actually answer?
ss / netstat / nmap
L4
What is listening or open?
tcpdump / Wireshark
L1-L7
What is REALLY on the wire?
WHEN IT MATTERS nmap scans REMOTE ports; ss lists LOCAL sockets - know which side each tool sees.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
508

## Slide 509
OBJ 5.5 · TOOLS
The Hardware Kit, One Page
1
Cable tester
First tool on any drop: wiremap and continuity catch opens, shorts and miswires before anything else runs.
2
Toner and probe
The Fox & Hound pair traces which patch-panel port or wall run a cable serves - no more label archaeology.
3
TDR / OTDR
Reports the distance to a break or bad splice on copper (TDR) or fibre (OTDR) - open the right ceiling tile.
4
Loopback plug
Loops TX to RX so a NIC or switch port proves itself with no far end involved.
5
Optical power meter
Reads received light in dBm against the link budget - the number that convicts dirty or bent fibre.
6
Wi-Fi analyzer
Surveys SSIDs, channels and signal strength so channel and AP-placement decisions rest on data.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
509

## Slide 510
DOMAIN 5 · 24% OF THE EXAM
Domain 5 Exam Technique
1
Know the 7 steps by NUMBER
Questions quote a scenario and ask 'what is the NEXT step?' - the order itself is tested.
2
Read the symptom's layer
Every scenario hides a layer clue: link light (L1), VLAN (L2), gateway (L3), port (L4), URL (L7).
3
'What changed?' wins often
When a scenario mentions any recent change, the answer almost always flows from it.
4
Eliminate by scope
One user vs many, one app vs all - scope eliminates half the answer options immediately.
5
Match tool to question
Tool-selection questions abound: know what each CLI and hardware tool uniquely proves.
6
Document is a real answer
After 'verify functionality', 'document findings' IS the correct next action - don't skip it for sounding dull.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
510

## Slide 511
DOMAIN 5 · WRAP-UP
Measure. Don't guess.
Troubleshooting is the discipline of shrinking the possibility space with every test - the seven steps make it repeatable, the tools make it fast, the documentation makes it stick.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
511

## Slide 512
DOMAIN 5.0 RECAP
Recap — Network Troubleshooting
• You can now: Diagnose cable and interface faults from link state, speed/duplex and error counters.
• You can now: Localise latency and packet loss along a network path with ping, traceroute and mtr.
• You can now: Isolate DNS faults by comparing resolvers, tracing delegation and reading response codes.
• You can now: Diagnose L2 adjacency problems with ip neigh and arping, including duplicate IP detection.
• You can now: Capture DNS traffic to a .pcap and analyse it with tshark and the TIS PCAP Analyzer.
• You can now: Demonstrate MTU limits with DF-bit pings and explain PMTUD black holes and MSS clamping.
• You can now: Read and manipulate the routing table; prove which route a destination uses with ip route get.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
512

## Slide 513
WRAP-UP
Course Summary & Next Steps
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
513

## Slide 514
LEARNING OUTCOMES
What You Achieved
1
LO1 · Explained networking concepts
OSI layers, appliances, cloud models, ports & protocols, media, topologies and IPv4/IPv6 subnetting.
2
LO2 · Implemented networks
Static & dynamic routing, NAT/PAT, 802.1Q VLANs, STP, bonding, wireless design and installations.
3
LO3 · Operated networks
SNMP, NetFlow, syslog, NTP, DHCP/DNS services, configuration backup and disaster recovery.
4
LO4 · Secured networks
Firewalls, ACLs, IDS, TLS/PKI, SSH hardening, VPNs, segmentation and attack recognition.
5
LO5 · Troubleshot networks
The seven-step CompTIA methodology with the right diagnostic tool at every layer.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
514

## Slide 515
NEXT STEPS
Preparing for the N10-009 Exam
1
Redo the labs
Repeat every lab from memory until the commands and workflow are automatic.
2
Master subnetting
Drill CIDR/VLSM until a /26 split takes under a minute — use the TIS IP Calculator to self-check.
3
Memorise the ports
FTP 20/21, SSH 22, Telnet 23, SMTP 25, DNS 53, DHCP 67/68, HTTP 80, HTTPS 443, SNMP 161/162, LDAP 389, RDP 3389, SIP 5060/5061.
4
Know the blueprint
Revise by the five domains and their weightings — troubleshooting scenarios are the largest share.
5
Practice exams
Attempt timed practice exams and review every wrong answer against the objectives.
6
Book the exam
Schedule N10-009 at a Pearson VUE centre or online when practice scores pass 80%.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
515

## Slide 516
TEST YOURSELF BEFORE THE REAL EXAM
Practice Exam — exams.tertiaryinfotech.com
1
1 · Open the portal
Go to https://exams.tertiaryinfotech.com/practice-exams/comptia/comptia-network-plus
2
2 · Choose Network+
Select the CompTIA Network+ practice exam that matches this course.
3
3 · Sit it timed
Attempt the full paper under exam timing — 90 minutes, no notes.
4
4 · Review and repeat
Review every explanation, revisit the weak domain's labs, then re-take it.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
516

## Slide 517
CONTINUE WITH TERTIARY INFOTECH
Recommended Courses
1
WSQ CompTIA Certified Security+ Training
2
WSQ CompTIA Certified PenTest+ Training
3
WSQ CompTIA Certified CySA+ Cybersecurity Analyst Training
4
WSQ CompTIA Certified Linux+ Training
5
WSQ CompTIA Certified Cloud+ Training
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
517

## Slide 518
WE'RE HERE TO HELP
Support
• If you have any enquiries during or after the class, you can contact us below.
• Email: enquiry@tertiaryinfotech.com
• Tel: +65 6100 0613
• Website: www.tertiarycourses.com.sg
• LMS / TMS: https://lms-tms.tertiaryinfotech.com
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
518

## Slide 519
WRAP-UP
Assessment
1
Written Assessment (SAQ)
1 hour · open book · short-answer knowledge questions.
2
Practical Performance (PP)
90 minutes · open book · hands-on networking tasks on the lab environment.
3
Digital attendance
Remember to take the Assessment digital attendance (TRAQOM) before you start.
4
Submit on the LMS
Upload your completed answers at https://lms-tms.tertiaryinfotech.com/
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
519

## Slide 520
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR on the LMS
2
Digital attendance
Scan the SSG QR
3
Sit WA then PP
Open book · 60 + 90 min
4
Submit on the LMS
Upload your answers
5
Sign the record
Assessment Summary
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
520

## Slide 521
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
521

## Slide 522
HAPPY NETWORKING
Thank You!
You can now design, implement, operate, secure and troubleshoot modern networks — and you are ready for the CompTIA Network+ (N10-009) exam.
CompTIA Network+ (N10-009) · TGS-2025054472
© 2026 Tertiary Infotech Academy Pte Ltd
522